## Slide 1
UCSD CSE 30
Keith Muller
Numbers Data and Memory
Lecture 4 – Oct 4, 2022
Computer Organization and Systems Programming
Version 1.03
Cray XMP-1982

## Slide 2: Review: Decimal Numbering
Decimal is base 10
  from “decem” (Latin) ⇒ Ten Characteristics
Ten symbols (Why?)
  0 1 2 3 4 5 6 7 8 9
How do we represent larger numbers?
  Large numbers are a sequence of digits
  Each digit is one of the available symbols
  n-digit numbers as coefficients in a polynomial
... = • + • + ... + • 10 +
Examples
  7061 in decimal (base 10)
  706110 = (7 103) + (0 102) + (6 101) + (1 100)
Digit position
symbol value
x

## Slide 3: Review: Binary Numbering
Binary is base 2
  adjective: being in a state of one of two mutually exclusive conditions such as on or off, true or false, molten or frozen, presence or absence of a signal
  From Late Latin bīnārius (“consisting of two”)
Two symbols:
  0 1
Numbers in C starting with 0b are binary
Example: What is 0b110 in base 10?
  0b110 = 1102 = (1 22) + (1 21) + (0 20) = 610
A bit is a single binary digit
A byte is an 8-bit value
powers of two
=
x

## Slide 4: Review: Octal Numbering
Eight symbols
  0, 1, 2, 3, 4, 5, 6, 7
  Notice that we no longer use 8 or 9
Base comparison:
  Base 10: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12…
  Base 8: 0, 1, 2, 3, 4, 5, 6, 7, 10, 11, 12, 13, 14…
Numbers in C starting with a 0: 07061, are octal
Example: What is 070618 in base 10?
  070618 = (7 83) + (0 82) + (6 81) + (1 80) = 363310
powers of eight
subscript indicates base
in C leading 0 indicates octal
=
x

## Slide 5: Review: Hexadecimal Numbering
hexadecimal is base 16
  From “hexa” (Ancient Greek ἑξα-) ⇒ six
  and from “decem” (Latin) ⇒ ten
Sixteen symbols
  0 1 2 3 4 5 6 7 8 9 a b c d e f
Numbers in C starting with 0x are hexadecimal
  1610 = 0x1016
Example: What is 0xa5 in base 10?
  0xa5 = a516 = (10 161) + (5 160) = 16510
Hexadecimal numbers are very commonly used in programming to express binary values
  Imagine the difficulty in correctly expressing a 64-bit binary value in your code
=
x

## Slide 6: Number Base Overview (as written in C)
Decimal is base 10, Hexadecimal is base 16, and octal is base 8
Octal digits have 8 values 0 – 7 (written in C as 00 – 07, careful 073 is octal = 59 in decimal)
Hex digits have 16 values 0 - 9 a - f (written in C as 0x0 – 0xf)
No standard prefix in C for binary (most use hex) – gcc (compiler) allows 0b prefix others might not
Hex digit Octal digit | 0x0 00 | 0x1 01 | 0x2 02 | 0x3 03 | 0x4 04 | 0x5 05 | 0x6 06 | 0x7 07
Decimal value | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Binary value | 0b0000 | 0b0001 | 0b0010 | 0b0011 | 0b0100 | 0b0101 | 0b0110 | 0b0111
Hex digit Octal digit | 0x8 010 | 0x9 011 | 0xa 012 | 0xb 013 | 0xc 014 | 0xd 015 | 0xe 016 | 0xf 017
Decimal value | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Binary value | 0b1000 | 0b1001 | 0b1010 | 0b1011 | 0b1100 | 0b1101 | 0b1110 | 0b1111
x

## Slide 7: Binary <---> Hexadecimal Equivalences
Hex Binary: = 1 digit hex = 4 digits binary
  Replace hex digits with binary digits
  drop leading zeros
  Example: 0x2d to binary
    0x2 is 0b0010, 0xd is 0b1101
    Drop two leading zeros, answer is 0b101101
Binary Hex:
  Pad with enough leading zeros until number of digits is a multiple of 4
  replace each group of 4 with the HEX equivalent
  Example: 0b101101
    Pad on the left to: 0b 0010 1101
    Replace to get: 0x2d
Base 10 | Base 2 | Base 16
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | a
11 | 1011 | b
12 | 1100 | c
13 | 1101 | d
14 | 1110 | e
15 | 1111 | f
x

## Slide 8: Hex to Binary (group 4 bits per digit from the right)
1111 1010 0101 0011
0x f
a
5
3
0b1111101001010011
binary start with a 0b in C
x
Each Hex digit is 4 bits in base 2 =

## Slide 9: Binary to Hex (group 4 bits per digit from the right)
4 binary bits is one Hex digit
0b 0110 1010 0011 1111
6
a
3
f
0x6a3f
hex start with 0x in C
x

## Slide 10: Binary to Octal (group 3 bits per digit from the right)
3 binary bits is one Octal digit
0b 0 110 101 000 111 111
6
5
7
7
0
0
065077
octal start with a 0 in C
x

## Slide 11: Octal to Binary (group 3 bits per digit from the right)
1 111 101 001 010 011
7
5
2
3
1
01
0b1111101001010011
binary start with a 0b in C
x
One Octal digit is three binary digits

## Slide 12: Looking at the Powers of Two
Multiple – left shift
Divide – right shift
Base 10 |  |  |  |  |  | 
5 | 0 | 0 | 0 | 1 | 0 | 1
10 | 0 | 0 | 1 | 0 | 1 | 0
20 | 0 | 1 | 0 | 1 | 0 | 0
40 | 1 | 0 | 1 | 0 | 0 | 0
Base 10 |  |  |  |  |  | 
5 | 0 | 0 | 0 | 1 | 0 | 1
10 | 0 | 0 | 1 | 0 | 1 | 0
20 | 0 | 1 | 0 | 1 | 0 | 0
40 | 1 | 0 | 1 | 0 | 0 | 0
=
x
Divide by 10 (whole numbers) – shift left by a digit
  123/10 = 12
Multiply by 10 (whole numbers) – shift right by a digit
  123 x 10 = 1230

## Slide 13: Multiply By Base: Shift Left 1 digits = Multiply by 2
0
3
0
0
7
0
0
2
0
3
0
0
7
0
0
2
0
shift in 1 digits set to zero
0
Shift In
Throw away 1 digits
“bit bucket”
Truncate to Final 8-digit Value
Initial 8-digit Value
Most significant
Digit
Least significant
Digit
x
Binary
Base 10

## Slide 14: Divide by Base: Shift Right 1 Digit = Divide by 2
0
7
0
0
9
0
0
4
0
7
0
0
9
0
0
4
0
shift in 1 zero
0
Carry Bit
“bit bucket”
Final 8-digit Value
Initial 8-digit Value
Most significant
Digit
Least significant
digit
Shift In
x
Binary
Base 10

## Slide 15: Use a Right Bit Shift: Unsigned Decimal To Unsigned Binary
Here is an Algorithmic approach to convert unsigned numbers to binary
Perform a sequence of divisions (right shift) to isolate the remainder
= ) +) +
x
0
1
0
0
0
0
0
0
0
0
1
1
0
0
0
0
0
0
1
1
0
0
0
0
0
0

## Slide 16: Unsigned Decimal to Unsigned Binary Conversion
x
dividend 249 | Quotient | Remainder | Bit Position
249/2 | 124 | 1 | b0
124/2 | 62 | 0 | b1
62/2 | 31 | 0 | b2
31/2 | 15 | 1 | b3
15/2 | 7 | 1 | b4
7/2 | 3 | 1 | b5
3/2 | 1 | 1 | b6
1/2 | 0 | 1 | b7
249(base 10) =
11111001 = (1x128) + (1x64) + (1x32) + (1x16) + (1x8) + 1 = 249

## Slide 17: Left Bit Shift & add: Unsigned Binary to Unsigned Decimal
Base conversion via a sequence of n multiplications (left shift) and n additions
  111 base 2 -> ((1x2 + 1) x 2) + 1
Alternatively, you can memorize and use the positional weights to convert
x
1
1
1
1
0
1
1
1
0
0
1
+
(
)
1
1
0
0
3
+
(
)
0
1
0
0
7
+
(
)
0
0
1
0
0
14
+
(
)
0
0
0
0
0
29
+
0
0
11101 base 2 = (1 x 16) + (1 x 8) + (1 x 4) + (0 x 2) + (1 x 1) = 29

## Slide 18: Unsigned Binary to Unsigned Decimal Conversion
What is 0 1 1 0 0 1 0 1(base 2) in decimal (N)?
101(base 10) = (1x64) + (1x32) + (1x4) + 1 (checking the conversion)
x
Product Shift Left | Addend | Bit Position | Product
0 | + 0 | b7 | 0
0 | + 1 | b6 | 1
2 x 1 = 2 | + 1 | b5 | 3
2 x 3 = 6 | + 0 | b4 | 6
2 x 6 = 12 | + 0 | b3 | 12
2 x 12 = 24 | + 1 | b2 | 25
2 x 25 = 50 | + 0 | b1 | 50
2 x 50 = 100 | + 1 | b0 | 101

## Slide 19
UCSD CSE 30
Keith Muller
Numbers Data and Memory
Lecture 4 – Oct 4, 2022
Computer Organization and Systems Programming
Version 1.03
Cray XMP-1982

## Slide 20: Different Type of Numbers each have a Fixed # of Bits Spanning one or more contiguous bytes of memory
x
C Data Type | AArch-32 contiguous Bytes
char (arm unsigned) | 1
short int | 2
unsigned short int | 2
int | 4
unsigned int | 4
long int | 4
long long int | 8
float | 4
double | 8
long double | 8
pointer * | 4
0
31
00000000
00000001
00000010
00000011
Word 32-bit integer uses 4 bytes
0
7
15
00000000
000000001
Half Word 16-bit integer uses 2 bytes
0
7
00000000
Byte 8-bit integer uses 1 byte
most significant bit (largest power of 2)
most significant bit (smallest power of 2)
most significant byte
least significant byte

## Slide 21: Unsigned Integers (positive numbers) Impact of Fixed # of Bits
4 bits is = ONLY 16 distinct values
Modular (C operator: %) or clock math
  Numbers start at 0 and “wrap around” after 15 and go back to 0
Keep adding 1
wraps (clockwise)
  0000 -> 0001 … -> 1111 -> 0000
Keep subtracting 1
wraps (counter-clockwise)
  1111 -> 1110 … -> 0000 -> 1111
Addition and subtraction use normal "carry" and "borrow" rules, just operate in binary
x

## Slide 22: Addition
Add two numbers in decimal
2 7 1 2
+ 2 0 + 7 8
4 7 9 0
+1 carry = 2
Adding Single digits in binary
  0 + 0 = 0
  0 + 1 = 1
  1 + 0 = 1
  1 + 1 = 0 (with 1 carry) or 10 base 2
x

## Slide 23: Unsigned Binary Number: Addition in 8 bits
1 0 1 0 0 0 0 1
0 0 1 1 0 0 1 1
0
0
0
0
1
1
1
1
1
1
0
1
0
0
0
0
+
carries
sum
161
51
212
Carry Bit
x
Be Aware in Binary
1 + 1 = 10 base 10: (1 + 1 = 2)
1 + 1 + 1 = 11 base10: (1 + 1 + 1 = 3)

## Slide 24: Subtraction
Add two numbers in decimal
2 7 6 2
- 1 0 + 2 3
1 7 3 9
+10 borrow = 12
Subtracting Single digits in binary
  0 - 0 = 0
  0 - 1 = 1 (with a +2 (a 1) from the column to the left)
  1 - 0 = 1
  1 - 1 = 0
x
-1 borrow = 5

## Slide 25: Unsigned Binary Number: Subtraction in 8 bits
1 0 1 0 0 0 0 1
0 0 1 1 0 0 1 1
-
borrows
difference
161
51
-
x
Be Aware in Binary
1 - 1 = 0
10 - 1 = 1 base 10: (2 – 1 = 1)

## Slide 26: Unsigned Binary Number: Subtraction in 8 bits Build of previous slide – note warning
1 0 1 0 0 0 0 1
0 0 1 1 0 0 1 1
0
1
1
1
1
0
1
0
10
0
-
borrows
difference
161
51
110
1
10
1
10
1
10
0
10
1
10
NOTICE
This slide is performing the Subtraction shown in the previous slide using PowerPoint builds
when this slide is viewed in a pdf it will look incorrect
-
x
Be Aware in Binary
1 - 1 = 0
10 - 1 = 1 base 10: (2 – 1 = 1)

## Slide 27: Overflow: Going Past the Boundary Between max and min
min
max
Overflow: Occurs when an arithmetic result (from addition or subtraction for example) is is more than min or max limits
Example shown is for a 4-bit number
x
C (and Java) ignore overflow exceptions
You end up with a bad value in your program and absolutely no warning or indication… happy debugging!….

## Slide 28: Unsigned Integer Number Overflow: Addition in 8 bits
1 0 1 0 0 0 0 1
0 1 0 1 1 1 1 1
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
+
carries
sum
161
95
256
Carry
Bit
Rule: When Carry Bit != 0, overflow has occurred for unsigned integers!
only 8 bits for numbers in this example carry bit is always dropped from result
x

## Slide 29: Overflow: Unsigned Values 4-bit limit
Addition Overflow:
Subtraction Overflow:
15
+ 2
17
1111
+ 0010
10001
oops 1
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Unsigned
1
- 2
-1
0001
- 0010(counter clockwise)
1111
oops 15
UMAX
UMIN
Overflow: Occurs when an arithmetic result is exceeds the min or max limits
only 4 bits for numbers in this example
carry bit is dropped from the result
x

## Slide 30: Unsigned Binary Multiplication example
x b = 0 0 0 0 0 1 0 1 (5)
0 1 0 1 0 0 1 1
a = 0 1 0 1 0 0 1 1 (83)
0 0 0 0 0 0 0 0
0 1 0 1 0 0 1 1
0 1 1 0 0 1 1 1 1 1 (415!!)
Exceeds what we can represent in 8 bits (255)
x b = 0 0 0 0 0 0 1 0 (2)
0 1 0 1 0 0 1 1
a = 0 1 0 1 0 0 1 1 (83)
0 0 0 0 0 0 0 0
0 1 0 1 0 0 1 1 0 (166)
Since we are multiplying by a power of two
we can shift left by 2 (zero insert at LSB)
a = 0 1 0 1 0 0 1 1 (83)
0 1 0 1 0 0 1 1 0 (166)
x

## Slide 31: Unsigned Binary Number Divide
1 1 0 0
11
0
-0
1
Consider 12/3 = 4
1
-1 1
0
0
1
0
0
0
0
-0 0
-0 0
0
0
-0
1
1 1 0 0
10
Consider 12/2 = 6
1
-1 0
1
0
1
1
0
0
0
-1 0
-0
0
1 1 0 0
Since we are dividing by a power of two
we can shift right by 1 (zero insert at MSB)
0 1 1 0
drop (bit bucket)
x

## Slide 32: Problem: How to Encode Both Positive and Negative Integers
How do we represent the negative numbers within a fixed number of bits?
  Allocate some bit patterns to negative and others to positive numbers (and zero)
distinct bit patterns to encode positive and negative values
Unsigned values: 0 ... –1
Signed values: … –1 (dividing the range in ~ half including 0)
On a number line (below): 8-bit integers – signed and unsigned (e.g., char in C)
-
+
-1
Same “width” (same number of encodings), just shifted in value
-1
Unsigned
Signed
x
-1 comes from counting 0 as a "positive" number

## Slide 33: Negative Integer Numbers: Sign + Magnitude Method
Use the Most Significant Bit as a sign bit
  0 as the MSB represents positive numbers
  1 as the MSB represents negative numbers
Two (oops) representations for zero: 0000, 1000
Tricky Math (must handle sign bit independently)
  Positive and Negatives “increment” (+1) in the opposite directions!
Sign bit
Remaining bits
31
30
0
MSB
these numbers show bit position boundaries
LSB
x

## Slide 34: Signed Magnitude Examples (Sign bit is always MSB)
0 110
positive
6
1 011
negative
3
0 0000000
positive
0
1 0001100
negative
12
1 000 = -0
1 001 = -1
1 010 = -2
1 011 = -3
1 100 = -4
1 101 = -5
1 110 = -6
1 111 = -7
0 000 = 0
0 001 = 1
0 010 = 2
0 011 = 3
0 100 = 4
0 101 = 5
0 110 = 6
0 111 = 7
Examples (4 bits):
x

## Slide 35: 2's Complement Signed Integer Method
Positive numbers encoded same as unsigned numbers
All negative values have a one in the leftmost bit
All positive values have a zero in the leftmost bit
  This implies that 0 is a positive value
Only one zero
For n bits, Number range is) to - 1)
  Negative values “go 1 further” than the positive values
Example: the range for 8 bits: -128, -127, .. 0, .. 126, +127
Example the range for 32 bits: -2147483648 .. 0, .. +2147483647
Arithmetic is the same as with unsigned binary!
x

## Slide 36: Two’s Complement: The MSB Has a Negative Weight
4-bit (w = 4) weight = = -23 = -8
  10102 unsigned: 1x23 + 0x22 + 1x21 + 0x20 = 10
  10102 two’s complement: -1x23 + 0x22 + 1x21 + 0x20 = -8 + 2 = –6
  -8 in two’s complement: 10002 = -23 + 0 = -8
  -1 in two’s complement: 11112 = -23 + (23 – 1) = -8 + 7 = -1
weight is ), all other bits: have positive weights )
. . .
b0
bn-1
bn-2
x

## Slide 37: Negation Of a Two’s Complement Number (Method 1)
7 = 0111
invert = 1000
add 1 + 1
-7 1001
7 = 0111
-7 = + 1001
(discard carry) 0000
-7 = 1001
invert = 0110
add 1 + 1
7 0111
1 = 0001
invert = 1110
add 1 + 1
-1 1111
-1 = 1111
invert = 0000
add 1 + 1
1 0001
-x == ~x + 1;
-8 = 1000
invert = 0111
add 1 + 1
-8 1000 oops!
x

## Slide 38: Negation of a Two’s Complement Number (Method 2)
copy unchanged right most bit containing a 1 and all the 0's to its right
Invert all the bits to the left of the right-most 1
0 1 1
1
7 =
-7 =
1 0 0
1
invert
Copy
0
1 0 0
4 =
-4 =
1
1 0 0
invert
Copy
0 0 1 1
1 0 0 0
56 =
-56 =
1 1 0 0
1 0 0 0
invert
Copy
0 0 0 0
0 =
0 =
0 0 0 0
Copy
1 0 0 0
-8 =
-8 =
1 0 0 0
Copy
OOPS!
x

## Slide 39: Signed Decimal to Two's Complement Conversion
x
dividend -102 | Quotient | Remainder | Bit Position
102/2 | 51 | 0 | b0
51/2 | 25 | 1 | b1
25/2 | 12 | 1 | b2
12/2 | 6 | 0 | b3
6/2 | 3 | 0 | b4
3/2 | 1 | 1 | b5
1/2 | 0 | 1 | b6
0/2 | 0 | 0 | b7
102(base 10) =
Get the two complement of 01100110 is 10011010

## Slide 40: Two's Complement to Signed Decimal Conversion - Positive
What is 0 1 1 0 0 1 0 1(base 2) in decimal (N)?
Signed Bit Bias | Bit | Bit Position | Bias
-2W-1 = -28-1 = -128 | x 0 | b7 | 0
Product Shift Left | Addend | Bit Position | Product
0 | + 1 | b6 | 1
2 x 1 = 2 | + 1 | b5 | 3
2 x 3 = 6 | + 0 | b4 | 6
2 x 6 = 12 | + 0 | b3 | 12
2 x 12 = 24 | + 1 | b2 | 25
2 x 25 = 50 | + 0 | b1 | 50
2 x 50 = 100 | + 1 | b0 | SUM = 101
 |  | Bias + SUM: | 0 + 101 = 101
x

## Slide 41: Two's Complement to Signed Decimal Conversion - Negative
What is 1 1 1 0 0 1 0 1(base 2) in decimal (N)?
Signed Bit Bias | Bit | Bit Position | Bias
-2W-1 = -28-1 = -128 | x 1 | b7 | -128
Product Shift Left | Addend | Bit Position | Product
0 | + 1 | b6 | 1
2 x 1 = 2 | + 1 | b5 | 3
2 x 3 = 6 | + 0 | b4 | 6
2 x 6 = 12 | + 0 | b3 | 12
2 x 12 = 24 | + 1 | b2 | 25
2 x 25 = 50 | + 0 | b1 | 50
2 x 50 = 100 | + 1 | b0 | SUM = 101
 |  | Bias + SUM: | -128 + 101 = -27
x

## Slide 42: Two’s Complement Addition and Subtraction
`
Addition: just add the two number directly
Subtraction: you can convert to addition: difference = minuend – subtrahend
    difference = minuend + 2’s complement (subtrahend)
x = 0 1 0 1 0 0 1 1
y = 0 0 0 0 1 0 1 1
x + y = 0 1 0 1 1 1 1 0
x-y = 0 1 0 0 1 0 0 0
x = 0 1 0 1 0 0 1 1
y = 0 0 0 0 1 0 1 1
x = 0 1 0 1 0 0 1 1
x – y = x +(-y) = 0 1 0 0 1 0 0 0
2’s complement first and then add
+ (-y) = 1 1 1 1 0 1 0 1
Cout
0 0 0 0 0 0 1 1
x

## Slide 43: Two’s Complement Positive Overflow
4-bit Two’s complement numbers (positive overflow)
0 1 0 1 5
+ 0 1 1 0 6
1 0 1 1 -5 != 11
Cout
0
0
1
0
SMIN
SMAX
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
0
+ 1
+ 2
+ 3
+ 4
+ 5
+ 6
+ 7
– 8
– 7
– 6
– 5
– 4
– 3
– 2
– 1
Two’s Complement
Overflow: Occurs when an arithmetic result is beyond the min or max limits
x
signed numbers: overflow occurs if
operands have same sign and result’s sign is different

## Slide 44: Two’s Complement Negative Overflow
4-bit Two’s complement numbers (negative overflow)
1 0 0 1 -7
+ 1 0 1 1 -5
0 1 0 0 +4 != -12
Cout
1
1
0
1
signed numbers: overflow occurs if
operands have same sign and result’s sign is different
SMIN
SMAX
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
0
+ 1
+ 2
+ 3
+ 4
+ 5
+ 6
+ 7
– 8
– 7
– 6
– 5
– 4
– 3
– 2
– 1
Two’s Complement
Overflow: Occurs when an arithmetic result is beyond the min or max limits
carry bit is dropped from result
x

## Slide 45: Summary: When Does Overflow Occur
Operand 1
+ Operand 2
Result
Operand 1 Sign | Operand 2 Sign | Is overflow Possible?
+ | + | YES
- | - | YES
+ | - | NO
- | + | NO
x

## Slide 46: Sign Extension in C: Type casts
Convert from smaller to larger integral data types
C and Java automatically performs sign extension
Example (on pi-cluster with 32-bit int and 16-bit short)
x
#include <stdlib.h>
#include <stdio.h>
int main(void)
{
signed char c = -1;
signed int i = c;
unsigned char d = 1;
unsigned int j = d;
printf("c decimal = %hd\n", c);
printf("c = 0x%hhx\n", c);
printf("i decimal = %d\n", i);
printf("i = 0x%x\n", i);
printf("\nd decimal = %hd\n", d);
printf("d = 0x%hhx\n", d);
printf("j decimal = %d\n", j);
printf("j = 0x%x\n", j);
return EXIT_SUCCESS;
}
%./a.out
c decimal = -1
c = 0xff
i decimal = -1
i = 0xffffffff
d decimal = 1
d = 0x1
j decimal = 1
j = 0x1

## Slide 47: Sign Extension (how type promotion works)
Sometimes you need to work with integers encoded with different number of bits
8 bits (char) -> (16 bits) short -> (32 bits) int
Sign extension increases the number of bits: -bit wide signed integer , EXPANDS to a wider n + -bit signed integer where both have the same value
Unsigned
Just add leading zeroes to the left side
Two’s Complement Signed:
If positive, add leading zeroes on the left
  Observe: Positive stay positive
If negative, add leading ones on the left
  Observe: Negative stays negative
• • •
• • •
• • •
• • •
n
original
copies of MSB
x

## Slide 48: Example: Two’s Complement Sign or bit Extension - 1
Adding 0's in front of a positive numbers does not change its value
7 = 0111
extend to
8 bits
00000111
Number is still 7
x
1 = 0001
extend to
8 bits
00000001
Number is still 1

## Slide 49: Example: Two’s Complement Sign or bit Extension -2
Adding 1's if front of a negative number does not change its value
7 = 0111
invert = 1000
add 1 + 1
-7 1001
7 = 00000111
invert = 11111000
add 1 + 1
-7 11111001
-7 = 1001
extend to
8 bits
11111001
x
1001 = -8 + 1 = -7
11111001 =
(-128 + 64 + 32 + 16 + 8) + 1 = -8 + 1 = -7

## Slide 50: Sign Extension Under Different representations
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
zeroed | original bits
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
s | zeroed | magnitude
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
sign extension | original bits
1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
How to sign extend this bit pattern?
0xd6
0x00d6
unsigned
0xffd6
two’s
complement
0x8056
signed
magnitude
move the sign bit
(replace original with a 0)
extend the sign bit
x

## Slide 51: Summary: Min, Max Values: Unsigned and Two’s Complement
Two’s Complement Unsigned for n bits
Unsigned Value Range
  UMin = 0b00…00 =
  UMax = 0b11…11 =
Two’s Complement Range
  SMin = 0b10…00 =
  SMax = 0b01…11 =
For n=4
x

## Slide 52: Variables: Size
Integer types
  char, int
Floating Point
  float, double
Modifiers for each base type
  short [int]
  long [int, double]
  signed [char, int]
  unsigned [char, int]
  const: variable read only
char type
  One byte in a byte addressable memory
  Signed vs Unsigned Char implementations
  Be careful char is unsigned on arm and signed on other HW like intel
C Data Type | AArch-32 contiguous Bytes | AArch-64 contiguous Bytes | printf specification
char (arm unsigned) | 1 | 1 | %c
short int | 2 | 2 | %hd
unsigned short int | 2 | 2 | %hu
int | 4 | 4 | %d / %i
unsigned int | 4 | 4 | %u
long int | 4 | 8 | %ld
long long int | 8 | 8 | %lld
float | 4 | 4 | %f
double | 8 | 8 | %lf
long double | 8 | 16 | %Lf
pointer * | 4 | 8 | %p
x
size of a pointer is the word size

## Slide 53: Fixed size types in C
Sometimes programs need to be written for a particular range of integers or for a particular size of storage, regardless of what machine the program runs on
We will need to do this in PA6 and PA7
In the file <stdint.h> the following fixed size types are defined for use in these situations:
x
Signed Data types | Unsigned Data types | Exact Size
int8_t | uint8_t | 8 bits (1 byte)
int16_t | uint16_t | 16 bits (2 bytes)
int32_t | uint32_t | 32 bits (4 bytes)
int64_t | uint64_t | 64 bits (8 bytes)

## Slide 54: Example: Limits of Some Types on 32-bit ARM
WARNING: If you want to force a char to be signed or unsigned use either
signed char or unsigned char
type | Smallest | largest
unsigned char | 0 | 255
char (ARM - unsigned) | 0 | 255
char (INTEL - signed) | -128 | 127
unsigned short | 0 | 65,535
short | -32,768 | 32,767
uint32_t | 0 | 2^32 -1
int32_t | -2^31 | 2^31 -1
x

## Slide 55: Fractional Binary Numbers (Software not Hardware)
“Binary Point,” like decimal point, signifies boundary between integer and fractional parts
Bits to right of “binary point” represent fractional powers of 2
Example: 10.10102 = 1×21 + 1×2-1 + 1×2-3 = 2.62510
Binary | Decimal
2-1 | 0.5
2-2 | 0.25
2-3 | 0.125
2-4 | 0.0625
x
0
0
1
1
0
0
1
1
1
1
1
1
0
0
1
integer part
fractional part
1
radix point
xx.yyyy
21
20
2-1
2-2
2-3
2-4
1
1
0
1
0
0

## Slide 56: Fixed Point Binary Number Divide
1 0 1 0 .0
100
-1 0 0
0 1
Consider 10/4 = 2.5
1
0
.1
0
0
x
-0 0 0
0
0
1 0
-1 0 0
0
1 0 1 0 .0 0
1000
-1 0 0 0
0 1 0
Consider 10/8 = 1.25
0
1
.0 1
0
-0 0 0 0
0
0
1 0 0
-1 0 0 0
0
0

## Slide 57: Fixed Point Binary Number Limitations
Limitation #1
  Can only exactly represent numbers of the form x/2k
    Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Limitation #2
  Just one setting of binary point within the w bits
  Limited range of numbers (very small values? very large?)
x

## Slide 58: Scientific Notation Binary
Computer hardware that supports this is called floating point hardware due to the “floating” of the binary point
Declare such variable in C as float (or double)
+1.012 × 2-1
radix (base)
binary point
exponent
mantissa
sign
x

## Slide 59: Floating Point Representation
Analogous to scientific notation
In Decimal:
  Not 12000000, but 1.2 x 107 In C: 1.2e7
  Not 0.0000012, but 1.2 x 10-6 In C: 1.2e-6
In Binary:
  Not 11000.000, but 1.1 x 24
  Not 0.000101, but 1.01 x 2-4
x

## Slide 60: Normalized Scientific Notation
Convert from scientific notation to fixed binary point
Perform the multiplication by shifting the decimal until the exponent disappears
    Example: 1.0112 24 = 101102 = 2210
    Example: 1.0112 2-2 = 0.010112 = 0.3437510
Convert from binary point to normalized scientific notation
  Distribute out exponents until binary point is to the right of a single digit
  Example: 1101.0012 = 1.1010012 x 23
Binary | Decimal
2-1 | 0.5
2-2 | 0.25
2-3 | 0.125
2-4 | 0.0625
x

## Slide 61: Encoding Fractions Observations
In Base 2:
10.1 x 25 = 1.01 x 26
1011.1 x 25 = 1.0111 x 28
0.110 x 25 = 1.10 x 24
Normalizing with base 2 :
adjust so there always a 1 to the left of the decimal point!
this 1 is called the hidden bit as we do not have use a bit to store it since it is there in every normalized mantissa
Adjust x to always be in the format 1.XXXXXXXXX… (fraction is normalized)
Fraction portion ONLY encodes what is to the right of the decimal point
“Hidden bit” allows number to have One additional digit for increased precision
Fraction encoding is 1.[FRACTION BINARY DIGITS]
x

## Slide 62: Floating Point Numbers: Implementation Approach
Supports a wide range of numbers
Flexible “floating” decimal point
Represent scientific notation numbers like 1.202 x
(–1)s M 2E
Sign bit (a single bit): 0 positive, 1 negative
Exponent: encoding of E above (it is NOT E directly represented in binary)
Fraction: encoding of M above (it is NOT M directly represented in binary)
sign bit
exponent
fraction
S
E
M
x

## Slide 63: Floating Point Number in a Byte (Not A Real Format)
Mantissa encoding: = 1.[xxxx] encoded as an unsigned value
  4 bits = 16 values + leading digit is always a 1
Exponent encoding: 3 bits encoded to represent both – and + exponents
sign bit
exponent
fraction
S = 1 bit
E = 3 bits
M = 4 bits
0
3
4
6
7
1 byte = 8 bits total
x

## Slide 64: IEE 754 Floating Point
Evolving Standard
Single – 32 bit "C Float"
Double – 64 bit "C Double"
Half – 16 bit
Quad – 128 bit
Binary Floating Point
Standard also defined decimal FP (not supported by most hardware)
Special Encodings
  NAN – not a number (quiet, signaling)
  + and - (biggest positive #, and smallest negative number)
Subnormal Numbers
sign | Exp = E +127 | mantissa
1 | 8 | 23
sign | Exp = E + 1023 | mantissa
1 | 11 | 52
x

## Slide 65: Floating Point and Linearity
Chart: Positive FP8 Number Line
Exp=000
Exp=001
Exp=010
Exp=011
Exp=100
  Why the non-linearity?
  Note, Exp=000 is treated specially
x

## Slide 66: IEEE Floating Point and "C" FP Types
IEEE Type | size | sign | exponent | mantissa | “C” name
bfloat (not IEEE yet) | 16 | 1 | 8 | 7 | (subset of float)
half | 16 | 1 | 5 | 10 | 
single | 32 | 1 | 8 | 23 | 
double | 64 | 1 | 11 | 52 | 
quad | 128 | 1 | 15 | 112 | 
x

## Slide 67: Memory Review: Organized in Units of Bytes
One bit (digit) of storage (in memory) has two possible states: 0 or 1
Memory is organized into a fixed unit of 8 bits, called a byte
Conceptually, memory is a single, large array of bytes, where each byte has a unique address (byte addressable memory)
An address is an unsigned (positive #) fixed-length n-bit binary value
  Range (domain) of possible addresses = address space
Each byte in memory can be individually accessed and operated on given its unique address
..00000000
..00000001
n-bit Memory
Address
..00000010
..00000011
..00000100
..00000101
..00000110
..00000111
Low address
High address
01010101
10101010
01010101
10101010
01010101
10101010
01010101
10101010
1 byte
(8-bits wide)
Memory
contents
Bit position in Byte |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Content of each bit |  |  |  |  |  |  | 
MSB
Most Significant Bit
LSB
(Least Significant Bit)
x

## Slide 68: Memory Size
Since memory addresses are implemented in hardware using binary
  The Size (number of byte sized cells) of Memory is specified in powers of 2
Memory size/capacity in bytes is specified by the “Number of bits" in an address
  32 bits of address = 232 = 4,294,967,296
  Address Range is 0 to 232 – 1 (unsigned)
Shorthand notation for address size (Memory Capacity)
  KB = 210 (K=1024) kilobyte
  MB = 220 megabyte
  GB = 230 gigabyte
  TB = 240 terabyte
  PB = 250 petabyte
x
Data Bits
Data Bits
Address Bits
Memory dimm

## Slide 69: Variables in Memory: Size and Address
The number of contiguous bytes a variable uses is based on the type of the variable
  Different variable types require different numbers of contiguous bytes
Variable names map to a starting address in memory
Example Below: Variables all starting at address 0x80
x
01010101
memory
char
80
Start
00000000
11111111
10101010
01010101
memory
int
4 bytes
80
82
81
83
Start
Size in bytes
memory
short int
2 bytes
80
10101010
81
01010101
Start
Size in bytes

## Slide 70: Address and Pointers
An address refers to a location in memory, the lowest or first byte in a contiguous sequence of bytes
A pointer is a variable whose contents (or value) can be properly used as an address
  The value in a pointer should be a valid address allocated to the process by the operating system
The variable x is at memory address 0x00001008
The variable pt is at memory location 0x00001000
The contents of pt is the address of x 0x00001008
00
00
00
77
(1 Byte)
00
00
01
08
0x00001000
0x00001001
0x00001002
0x00001003
0x00001004
0x00001005
0x00001006
0x00001007
0x00001008
0x00001009
0x0000100A
0x0000100B
0x0000100C
0x0000100D
0x0000100E
0x0000100F
32-bit address
(hex)
int x =
0x77; ------>
pt is a pointer to x------>
x

## Slide 71: Byte Ordering of Numbers In Memory: Endianness
Two different ways to place multi-byte integers in a byte addressable memory
Big-endian: Most Significant Byte (“big end”) starts at the lowest (starting) address
Little-endian: Least Significant Byte (“little end”) starts at the lowest (starting) address
Example: 32-bit integer with 4-byte data
a1
b2
c3
d4
0x100
0x101
0x102
0x103
01
23
a1
b2
c3
d4
01
23
d4
c3
b2
a1
Big-Endian
Little-Endian
MSB
Most significant byte
LSB
Least significant byte
x
0x100
0x101
0x102
0x103

## Slide 72: Byte Ordering Example
Decimal: 12345
Binary: 0011 0000 0011 1001
Hex: 3 0 3 9
int x = 12345;
// or x = 0x3039;
39
30
00
00
IA32, ARM32 (little-endian)
30
39
00
00
(big-endian)
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
x

## Slide 73: Extra Slides

## Slide 74: 1's Complement Signed Integer Method
Use the MSB is the sign bit to represent a negative value is encoded as the 1's complement
All negative values have a one in the leftmost bit
All positive values have a zero in the leftmost bit
The problem is there are two values for zero
  1111 and 0000 in 4-bits
  arithmetic is tricky when you cross over the zeros
Number | + | -
0 | 0000 | 1111
1 | 0001 | 1110
2 | 0010 | 1101
3 | 0011 | 1100
4 | 0100 | 1011
5 | 0101 | 1010
6 | 0110 | 1001
7 | 0111 | 1000
x
-0
0
-1
-2
-7
7
1
2

## Slide 75: Negative Integer Numbers: Sign + Magnitude Method
Use the Most Significant Bit as a sign bit
  0 as the MSB represents positive numbers
  1 as the MSB represents negative numbers
Two (oops) representations for zero: 0000, 1000
Tricky Math (must handle sign bit independently)
With Simple math, Positive and Negatives “increment” (+1) in the opposite directions!
Sign bit
Remaining bits
31
30
0
0100 - 0011 0001
4 - 3 1
✓
0100 + 1011 1111
4 + -3 -7
✗
MSB
these numbers show bit position boundaries
LSB
x

## Slide 76: Signed Magnitude Examples (Sign bit is always MSB)
Examples Using Hex notation (8 bits):
  0x00 = 0b00000000 is positive, because the sign bit is 0
  0x7F = 0b01111111 is positive (+12710)
  0x85 = 0b10000101 is negative (-510)
  0x80 = 0b10000000 is negative… also zero
0 110
positive
6
1 011
negative
3
0 0000000
positive
0
1 0001100
negative
12
1 000 = -0?
1 001 = -1
1 010 = -2
1 011 = -3
1 100 = -4
1 101 = -5
1 110 = -6
1 111 = -7
0 000 = 0?
0 001 = 1
0 010 = 2
0 011 = 3
0 100 = 4
0 101 = 5
0 110 = 6
0 111 = 7
Examples (4 bits):
x

## Slide 77: Sign Extension Signed Magnitude number
Just move the sig bit and expand the magnitude with zeros to the left
x
1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
s | magnitude
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
s | zeroed | magnitude
move the sign bit
(replace original with a 0)

## Slide 78: Interpreting and extending with Different representations
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
zeroed | original bits
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
s | zeroed | magnitude
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
sign extension | original bits
1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
How to extend this bit pattern?
0xd6
0x00d6
unsigned
0xffd6
two’s
complement
0x8056
signed
magnitude
move the sign bit
(replace original with a 0)
extend the sign bit
x

## Slide 79: Watch out for Hardware differences: Example: Is a Char signed or unsigned?
variable c is being cast promoted to an int
So, what is printed?
Depends on the hardware
Aarch32 and Aarch64 (arm) it is unsigned
255
Intel 64-bit it is signed
-1
#include <stdio.h>
#include <stdlib.h>
int
main(void)
{
char c = 255;
printf("%d\n", (int)c);
return EXIT_SUCCESS;
}
x

## Slide 80: sizeof(): Variable Size (number of bytes) Operator
sizeof() operator returns:
the number of bytes used to store a variable or variable type
  size_t size = sizeof(variable_type);
  or
  size_t size = sizeof(variable_name); // preferred!
The argument to sizeof() is often an expression:
size = sizeof(int * 10);
  reads as:
    number of bytes required to store 10 integers (an array of [10])
#include <stddef.h>
/* size_t type may vary by system but is always unsigned */
x

## Slide 81: sizeof() Examples (On the pi-cluster)
#include <stdio.h>
#include <stdlib.h>
int
main (void){
printf("char is %zu\n", sizeof(char));
printf("short is %zu\n",sizeof(short));
printf("int is %zu\n", sizeof(int));
printf("long is %zu\n", sizeof(long));
return EXIT_SUCCESS;
}
% ./a.out (on the picluster)
char is 1
short is 2
int is 4
long is 4

## Slide 82: Floating Point Number in a Byte (Not A Real Format)
Mantissa encoding: = 1.[xxxx] encoded as an unsigned value
Exponent encoding: 3 bits encoded as an unsigned value using bias encoding
  Bias encoding = (2E-1 – 1)
  3 bits for the bias we have 23-1 - 1 = 22 - 1 = a bias of 3
  With a Bias of 3: positive and negative numbers range: small to large is: 2-3 to 24
sign bit
exponent
fraction
S = 1 bit
E = 3 bits
M = 4 bits
0
3
4
6
7
1 byte = 8 bits total
Actual | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4
Biased | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Bias | + 3 | + 3 | + 3 | + 3 | + 3 | + 3 | + 3 | +3
x

## Slide 83: Encoding Fractions Observations
Examples In Base 10:
42.4 x 105 = 4.24 x 106
324.5 x 105 = 3.245 x 107
0.624 x 105 = 6.24 x 104
Observation on base 10:
We usually adjust the exponent until we get down to one digit to the left of the decimal point
x

## Slide 84: Characteristics of Signed Numbers
Digital Hardware (and C) supports two flavors of integers
  unsigned – only non-negative (positive) numbers
  signed – both negative and non-negatives (positive) numbers
A Signed integer must be able to represent:
  Negative integer
  Zero (0)
  Positive Integer
  number + (- representation of number) = 0
So, with a fixed number of bits, some of the bit patterns in the wheel at the left must be reallocated to represent negative numbers
x
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15

## Slide 85: Example: Two’s Complement Sign or bit Extension - 3
Adding 1's if front of a negative number does not change its value
1 = 0001
invert = 1110
add 1 + 1
-1 1111
-1 = 1111
extend to
8 bits
11111111
x
-1 = 11111111
extend to
16 bits
1111111111111111

## Slide 86: Sign Extension in C: Type casts
Convert from smaller to larger integral data types
C and Java automatically performs sign extension
Example (remember we are working with 32-bit int and 16-bit short)
short int sx = 12345;
int ix = (int) sx;
Var | Decimal | Hex | Binary
sx | 12345 | 30 39 | 00110000 00111001
ix | 12345 | 00 00 30 39 | 00000000 00000000 00110000 00111001
Var | Decimal | Hex | Binary
sy | -12345 | CF C7 | 11001111 11000111
iy | -12345 | FF FF CF C7 | 11111111 11111111 11001111 11000111
0b0011
0b1100
x
short int sy = -12345;
int iy = (int) sy;

## Slide 87: Shift Operations in C
n is number of bits to shift a variable x of width w bits
Shifts by n < 0 or n ≥ w are undefined
Left shift (x << N)
  Shift N bits left, Fill with 0s on right
In C: behavior of >> is determined by compiler
  gcc: it depends on data type of x (signed/unsigned)
Right shift (x >> N)
  Logical shift (for unsigned variables)
    Shift N bits right, Fill with 0s on left
  Arithmetic shift (for signed variables) – Sign Extension
    Shift N bits right while Replicating the most significant bit on left
    Maintains sign of x
In Java: logical shift is >>> and arithmetic shift is >>
Left Shift
Right logical Shift
Right Arithmetic Shift
x

## Slide 88: Arithmetic Shift Right 1 Digit = Divide by 2 for 2's Complement Values
1
1
0
0
1
0
0
1
1
0
0
1
0
0
1
1
Replicate MSB
Carry Bit
“bit bucket”
Final 8-digit Value
Initial 8-digit Value
Most significant
Digit
Least significant
digit
x
Binary
Positive Number
1

## Slide 89: Number ranges: limits.h
The include file <limits.h> defines various symbolic names where the names represent the various limits on resources that the implementation imposes on applications;
The standard C integer types were intended to allow code to be portable among machines with different inherent data sizes (word sizes), so each type may have different range of numbers on different machines
C Data Type | signed min | signed max | unsigned max
char | SCHAR_MIN | SCHAR_MAX | UCHAR_MAX
short int | SHRT_MIN | SHRT_MAX | USHRT_MAX
int | INT_MIN | INT_MAX | UINT_MAX
long int | LONG_MIN | LONG_MAX | ULONG_MAX
#include <limits.h>
int i = INT_MAX;
…
printf("Max int is: %d\n", i);
…
x

## Slide 90: Excess N Bias Encoding Method
Excess, Bias (or offset) encoding maps negative numbers to an unsigned (positive) integer range by adding an offset number (called the bias) to encode positive and negative numbers
  Most negative number maps to zero, most positive number maps to all 1's
For example: Say we have a number that is limited to 3 bits (0 to 7 unsigned)
Actual | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4
Biased Encoded | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Bias | + 3 | + 3 | + 3 | + 3 | + 3 | + 3 | + 3 | +3
x

## Slide 91: Excess Bias Encoding (As used in floating point numbers)
Given a number in E bits, to divide the range in about 1/2 the following is used:
excess N bias = (2E-1 – 1) (this is just one of many bias formulas)
With this excess N Bias approach: actual numbers range from most negative to most positive is: -(bias) to bias+1
So, for a number that is limited to 4 bits (0 to 15 unsigned)
  Then excess N bias = 24-1 - 1 = 23 - 1 = a bias of +7
x
actual | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
bias | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7
bias encoded | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15

## Slide 92: Another Way to Look at 2's Complement Encoding
A 2's compliment value can be thought of as using a slightly different bias encoding for negative numbers only (more negative values): -2W-1
The leftmost bit is then interpreted as a decision to apply the bias (if 1) or not (if 0)
  1 apply the bias
  0 do not apply the bias
For example, for a 4-bit number (w = 4) , the negative number bias weight would be = = -23 = -8
Observe: adding +1 makes the number more positive for both negative and positive numbers
3 bit | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111 | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
Actual | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
+Bias | -8 | -8 | -8 | -8 | -8 | -8 | -8 | -8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
decimal | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
2's | 1000 | 1001 | 1010 | 1011 | 1100 | 1101 | 1110 | 1111 | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111
x

## Slide 93: Scientific Notation Decimal
Scientific Normalized form:
exactly one digit (non-zero) to left of decimal point
Alternatives to representing 1/1,000,000,000
  Normalized: 1.0×10-9
  Not normalized: 0.1×10-8, 10.0×10-10
+6.0210 × 1023
radix (base)
decimal point
exponent
mantissa
sign
x

## Slide 94: Floating Point Number in a Byte (Not A Real Format)
Mantissa encoding: = 1.[xxxx] encoded as an unsigned value
Exponent encoding: 3 bits encoded as an unsigned value using bias encoding
  Bias encoding = (2E-1 – 1)
  3 bits for the bias we have 23-1 - 1 = 22 - 1 = a bias of 3
  With a Bias of 3: positive and negative numbers range: small to large is: 2-3 to 24
sign bit
exponent
fraction
S = 1 bit
E = 3 bits
M = 4 bits
0
3
4
6
7
1 byte = 8 bits total
Actual | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4
Biased | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Bias | + 3 | + 3 | + 3 | + 3 | + 3 | + 3 | + 3 | +3
x

## Slide 95: Floating Point Number (8-bits) Number Range: 2-3 to 24
sign bit
exponent
fraction
S = 1 bit
E = 3 bits
M = 4 bits
0
000
0000
S = 1 bit
E = 3 bits
M = 4 bits
0.0 Special case in this simple model
we do not put back the “hidden bit”
0
000
0001
S = 1 bit
E = 3 bits
M = 4 bits
Smallest Non-zero Positive
0.0010001 = 1/8 + 1/128 = 0.1328125 base 10
0/1
111
1111
S = 1 bit
E = 3 bits
M = 4 bits
Largest Positive/Negative
1.1111 x 24 = 11111 = 31 base 10
1
000
0000
S = 1 bit
E = 3 bits
M = 4 bits
Smallest (closest to zero) Number
1.0000 x 2-3 = 0.001000 = 1/8 = -0.125 base 10
Note: Orange is hidden bit added back
x

## Slide 96: Decimal to Float
Step 1: convert from base 10 to binary (absolute value)
-0.375(decimal) = 0000.01102
Step 2: Find out how many places to shift to get the number into the normalized 1.xxxx mantissa format
0000.01102 = 1.1000 x (2-2)base 10
exponent: -210 + bias of 310 = 110 = 0b001 for the exponent (after adding the bias)
Step 3: Use as many digits that fit to the right of the decimal point in the fractional .xxxx part 1.1000
Step 4: Sign bit
positive sign bit is 0
negative sign bit is 1
7 | 6 |  |  |  | 4 | 3 |  |  |  |  | 0
s | exponent (3 bits) |  |  |  |  | fraction (4 bits) |  |  |  |  | 
Bias of 3
s | exponent | fraction
1 | 0b001 | 0b1000
0x9 |  | 0x8
= 0x98
x

## Slide 97: Float to Decimal
Step 1: Break into binary fields
0x45 =
Step 2: Extract the unbiased exponent
0b100 = 4base 10 - bias of 310 = 110 for the exponent (bias removed)
Step 3: Express the mantissa (restore the hidden bit)
1.0101
Step 4: Apply the unbiased exponent
1.0101base 2 x (21)base 10 = 10.101
Step 5: Convert to decimal
10.101 = 2.625base 10
Step 6: Apply the Sign
+ 2.625base 10
7 | 6 |  |  |  | 4 | 3 |  |  |  |  | 0
s | exponent (3 bits) |  |  |  |  | fraction (4 bits) |  |  |  |  | 
Bias of 3
0x4 |  | 0x5
s | exponent | fraction
0 | 0b100 | 0b0101
x

## Slide 98: IEEE “754” Floating Point Double and Single Precision
31 | 30 |  | 23 | 22 |  |  |  |  | 0
sign | Exponent (8 bits) Uses a Bias of 127 |  |  | fraction (23 bits) |  |  |  |  | 
63 | 62 |  | 52 | 51 |  |  |  |  | 0
sign | Exponent (11 bits) Uses a Bias of 1023 |  |  | fraction (52 bits) |  |  |  |  | 
Single Precision (C float)
x 1.fraction
Double Precision (C Double)
x 1.fraction
x

## Slide 99: Decimal to IEEE Single Precision Float
Step 1: convert from base 10 to binary (absolute value)
-13.375(decimal) = 1101.0110
Step 2: Find out how many places to shift to get the number into the normalized 1.xxxx mantissa format
1101.0110 = 1.1010110 x (23)base 10
3 + bias of 127 = 130 for the exponent = 0b1000 0010
Step 3: Use as many digits that fit to the right of the decimal point in the fractional .xxxx part (0 pad )
1.1010110 0000 0000 0000 0000
Step 4: If the sign is positive sign bit is 0, otherwise it is 1
s | exponent | fraction
1 | 100 0001 0 | 101 0110 0000 0000 0000 0000
31 | 30 |  | 23 | 22 |  |  |  |  | 0
sign | Exponent (8 bits) Bias is 127 |  |  | fraction (23 bits) |  |  |  |  | 
= 0xc1560000
0xc
0x1
0x5
0x6
0x0
0x0
0x0
0x0
x

## Slide 100: IEEE Single Precision Float to Decimal
Step 1: Break into binary fields and expand as needed
0xc0b00000 =
Step 2: Find the exponent
0b10000001 = 129base 10 - bias of 12710 = 210 exponent with bias added
Step 3: Express the mantissa (restore the hidden bit)
1.0110
Step 4: Apply the exponent
1.0110 x (22)base 10 = 101.10
Step 5: Convert to decimal
101.10 = 5.5
Step 6: Apply the Sign
-5.5
1 | 100 0000 1 | 011 0000 0000 0000 0000 0000
31 | 30 |  | 23 | 22 |  |  |  |  | 0
sign | Exponent (8 bits) Bias is 12710 |  |  | fraction (23 bits) |  |  |  |  | 
0xc
0x0
0xb
0x0
0x0
0x0
0x0
0x0
x

## Slide 101: Reference: 8-Bit Overflow Examples
1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 
 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0
+ | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
carries
=23410
=5410
=3210
Unsigned Integer
Because carry-out bit is 1 (and dropped), overflow is detected
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 
 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0
+ | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
carries
=10610
=5410
=-9610
Two’s Complement
Both operands are positive, but resulting sign is negative
see that cout != cin at the MSB
overflow is detected
1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 
 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0
+ | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
carries
=-2210
=5410
=3210
Two’s Complement
Unlike unsigned arithmetic, no overflow even though the carry-out bit is 1.
As the operand's signs differ, overflow is not possible (cout == cin)
cout
cout
cout
cin
cin
x

## Slide 102: Decimal to Float
Step 1: convert from base 10 to binary (absolute value)
6.625(decimal) = 0110.1010
Step 2: Find out how many places to shift to get the number into the normalized 1.xxxx mantissa format
0110.1010 normalizes to -> 1.101010 x (22)base 10
exponent: 210 + a bias of 310 = 510 = 0b101 for the exponent (after adding the bias)
Step 3: Use as many digits to the right of the decimal point that will fit in the fractional .xxxx part
1.101010 (we will truncate drop the trailing 10, Real FP use complex rounding approaches)
Step 4: Sign bit
positive sign bit is 0
negative sign bit is 1
7 | 6 |  |  |  | 4 | 3 |  |  |  |  | 0
s | exponent (3 bits) |  |  |  |  | fraction (4 bits) |  |  |  |  | 
Bias of 3
s | exponent | fraction
0 | 0b101 | 0b1010
0x5 |  | 0xa
= 0x5a
x