## Slide 1
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 1.09
Lecture 13 – November 1, 2022
Aarch32 Assembly – Part 1

## Slide 2: Arm Core Organization & Floorplan Examples
Single core arm die (not an A72) Floorplan
x

## Slide 3: Memory Triangle: Hardware Cost/Performance/Capacity Tiers
Clock cycle =~ time to access; larger is slower
Source: Dive Into Systems Text
x
DIMM memory Module
PCI-E
ALU & Logic
Address
Data
Registers
Caches
Address
Data
CPU
~300 K Cycles
Goal: keep most Data Accesses high in the Triangle
Smallest Capacity
Highest Performance
Highest cost/capacity
Largest Capacity
Slowest performance
Lowest Cost $/capacity
Assume 1 clock cycle per machine instruction
Design Tradeoff: Based on workload considering cost and performance targets

## Slide 4: 32-Bit Arm - Registers
Registers are memory located within the CPU
Registers are the fastest read and write storage
Register is word size in length stores 32-bit values
  Memory is accessed using pointers in registers
In assembly language the registers have predefined names starting with an r to differentiate them from memory addresses which are labels (address)
16 registers: from r0 to r15 (encoded: 0x0 – 0xf)
x
Registers
4-bytes
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
4-bit address
Capacity: 16 Words
1- Byte
32-bit address
External memory
0x00000000
0xFFFFFFFF
Capacity:4 GBytes
CPU
CPU Memory Bus = Address + Data
arithmetic Logic Unit

## Slide 5: Assembly and Machine Code
Machine Language (or code): Set of instructions the CPU executes are encoded in memory using patterns of ones and zeros (like binary numbers)
Assembly language is a symbolic version of the machine language
Each assembly statement (called an Instruction)
  Executes exactly one from a list of simple commands
  Instructions describe operations (e.g., =, +, -, *)
  Execution goes low to high memory one instruction at a time unless there is a branch
One line of arm32 machine code contains one instruction in one word (32 bits)
Assembler (gnu as)
  (1) translates assembly to machine code
  (2) Generates the contents of: text, read only data, and static data memory sections
x
0xFF…FF
0x00…00
32-bit address space
OS kernel [protected]
Stack
Heap
Static Data (+BSS)
Shared Libraries
Read Only Data
Read Only Text Segment
1040c: e28db004 add fp, sp, 4
10410: e59f0010 ldr r0, [pc, 16]
10414: ebffffb3 bl 102e8 <printf>
10418: e3a00000 mov r0, 0
1041c: e24bd004 sub sp, fp, 4
Memory word (4-bytes)
Address contents Assembly Language
Machine Code
high <- low bytes

## Slide 6: Anatomy of an Assembly instruction
Assembly language instructions specify an operation and the operands to the instruction (arguments of the operation)
Three basic types of operands
  Destination: where the result will be stored
  Source: where data is read from
  Immediate: an actual value like the 1 in y = x + 1
add r0, r1, r2
add r0, r1, 1
Operands (variables)
Source Operands
Destination Operand
Immediate Operand
x
operation

## Slide 7: Meaning of an Instruction
Operations are abbreviated int opcodes (1– 5 letters)
Assembly Instructions are specified with a very regular syntax
  Opcodes are followed by arguments
  Usually the destination argument is next, then one or more source arguments (this is not strictly the case, but it is generally true)
Why this order?
Analogy to C or Java
int r0, r1, r2;
r0 = r1 + r2; // c
x
r0 = r1 + r2
add r0, r1, r2 // assembly

## Slide 8: 32-Bit Arm - Registers
Almost all arithmetic, logic operations and data movement operations involve at least one register
As a result, Register addresses are directly encoded into 4-bit fields in machine instructions (see below)
x
4-bytes
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
4-bit address
Capacity: 16 Words
registers
Arithmetic & Logic Unit (ALU)
All computations (add, subtract, etc.) are performed in the ALU

## Slide 9: Program Execution: A Series of Instructions
Instructions are retrieved sequentially from memory
Each instruction executes to completion before the next instruction is completed
Conceptually the pc (program counter) points at executing instruction
exceptions: loops, function calls, traps,..
add r0, r1, r1
add r0, r0, r0
add r0, r0, r0
sub r1, r0, r1
r0 = 4 r1 = 2
r0 = 1 r1 = 2
r0 = 8 r1 = 2
r0 = 16 r1 = 2
r0 = 16 r1 = 14
x
Memory Content in Text segment
initial values
Low memory
High memory
OS kernel [protected]
Stack
Heap
Static Data (+BSS)
Shared Libraries
Read Only Data
Read Only Text Segment
Register contents inside the CPU
Main Memory

## Slide 10: Program Execution: Looping in the Execution Flow
Repeat the series of instructions in a loop means altering the flow of execution
This is used with if statements and loops
Below is an infinite loop (br instruction: unconditional branch: "goto"
.Lloop: add r0, r1, r1
add r0, r0, r0
add r0, r0, r0
sub r1, r0, r1
r0 = 4 r1 = 2
r0 = 1 r1 = 2
r0 = 8 r1 = 2
r0 = 16 r1 = 2
r0 = 16 r1 = 14
x
br .Lloop
branch to the instruction at memory location with the label: .Lloop
the address of this instruction has the name .Lloop
Infinite loop C
do {
r0 = r1 + r1;
r0 = r0 + r0;
r0 = r0 + r0;
r1 = r0 – r1;
} while(1);

## Slide 11: How to Access Memory?
31 | 0
Address of a location in memory | 
Consider a = b + c are operands are in memory
  Operation code: add Destination: a
  Operand 1: b Operand 2: c
Aarch32 Instructions are always word size: 32 bits wide
  Some bits must be used to specify the operation code
  Some bits must be used to specify the destination
  Some bits must be used to specify the operands
Address space is 32 bits wide so put a POINTER in a register
31 |  |  | 0 | 
Opcode
Destination
NOT ENOUGH BITS for FULL Addresses to be stored in the instruction
32 bits wide
x
Operand 1
Operand 2
0xFF…FF
0x00…00
32-bit Address space
OS kernel [protected]
Stack
Heap
Static Data (+BSS)
Shared Libraries
Read Only Data
Read Only Text Segment

## Slide 12: 32-Bit Arm is a Load/Store Architecture
x
4-bytes
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
4-bit address
Capacity: 16 Words
registers
1- Byte
32-bit address
memory
0x00000000
0xFFFFFFFF
Capacity:4 GBytes
Arithmetic & Logic Unit (ALU)
All computations (add, subtract, etc.) are performed in the ALU
Instruction operands and results are only in registers
Load:
(also called a Fill)
Copy the contents of a variable from memory into a register.
Store:
(also called a Spill)
Copy the contents of a register back into a variable in memory.

## Slide 13: Using Registers as Pointers to Memory - Load
x
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
0x1004
0x4321
0x1
0x2
0x3
0x4
External memory
0x00001000
0x00001004
0x00001008
0x0000100c
0x00001010
We want to do a x[1] = x[0]
We have to do this in two steps
int r3;
int x[2];
int *r1 = &x; // r1 contains address
…
r3 = *(r1); // memory to register
*(r1 + 1) = r3; // register to memory
Load register from memory (read)
ldr r3, [r1, 0]
address = r1 + 0 = 0x1004
x[0]
x[1]
we will cover this instruction in more detail later
The [ ] around the operands is like the * dereference op
points at
reads memory

## Slide 14: Using Registers as Pointers to Memory - Store
x
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
0x1004
0x4321
0x1
0x2
0x3
0x4
External memory
0x00001000
0x00001004
0x00001008
0x0000100c
0x00001010
We want to do a x[1] = x[0]
We have to do this in two steps
int r3;
int x[2];
int *r1 = &x; // r1 contains address
…
r3 = *(r1); // memory to register
*(r1 + 1) = r3; // register to memory
Store register to memory (write)
str r3, [r1, 4]
address = r1 + 4 = 0x1008
x[0]
x[1]
We will cover this instruction in more detail later
The [ ] around the operands is like the * dereference op
r1 + 4
points at
writes memory
0x1
0x2
0x3
0x4

## Slide 15: Arm Register Summary
16 Named registers r0 – r15
The operands of almost all instructions are registers
To operate on a variable in memory do the following:
  Load the value(s) from memory into a register
  Execute the instruction
  Store the result back into memory (only if needed!)
Going to/from memory is expensive
  4X to 20X+ slower than accessing a register
Strategy: Keep variables in registers as much as possible
x

## Slide 16: Using Aarch32 Registers
There are two basic groups of registers, general purpose and special use
General purpose registers can be used to contain up to 32-bits of data, but you must follow the rules for their use
  Rules specify how registers are to be used so software can communicate and share the use of registers (later slides)
Special purpose registers: dedicated hardware use (like r15 the pc) or special use when used with certain instructions (like r13 & r14)
r15/pc is the program counter that contains the address of an instruction being executed (not exactly … later)
r8
r9
r10
r4
r5
r6
r7
Preserved registers
Called functions can't change
r0
r1
r2
r3
Scratch Registers
First 4 Function Parameters
Function return value
Called functions can change
x
r15/pc
r13/sp
r14/lr
r11/fp
r12/ip
Special Use Registers
function call implementation & long branching
Special Use Registers
program counter

## Slide 17
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 1.09
Lecture 14 – November 3, 2022
Aarch32 Assembly – Part 1

## Slide 18: CPU Operational Overview: Executing Machine Code
0001042c <inloop>:
1042c: e3530061 cmp r3, 0x61
10430: ba000002 blt 10440 <store>
10434: e353007a cmp r3, 0x7a
10438: ca000000 bgt 10440 <store>
1043c: e2433020 sub r3, r3, #32
00010440 <store>:
10440: e7c13002 strb r3, [r1, r2]
10444: e2822001 add r2, r2, 0x1
10448: e7d03002 ldrb r3, [r0, r2]
1044c: e3530000 cmp r3, 0x0
10450: 1afffff5 bne 1042c <inloop>
Everything has a memory address: instructions & data
  Machine code uses addresses for loops, branches, function calls, variables, etc.
1 Fetch
  read the instruction into memory (fetch)
  program counter is automatically incremented (+4) to contain the address of the next instruction in memory Instructions are 32 bits
2 Decode
  Decodes the instruction and sets up execution
3 Execute
  CPU completes the execution of the instruction
  Execution may alter the pc to take branches, etc.
  Go to fetch
address contents
assembly version
text segment in memory
x
r15/pc
r15/pc
r15/pc
r15/pc
r15/pc
r15/pc
Edited output For output Created by the command
%objdump –d a.out
%objdump –d –S a.out adds source code

## Slide 19: AArch32 Instruction Categories
Data movement to/from memory
  Data Transfer Instructions between memory and registers
    Load, Store
Arithmetic and logic
  Data processing Instructions (registers only)
    Add, Subtract, Multiply, Shift, Rotate, …
Control Flow
  Compare, Test, If-then, Branch, function calls
Miscellaneous
  Traps (OS system calls), Breakpoints, wait for events, interrupt enable/disable, data memory barrier, data synchronization barrier
  Many others that we will not cover in the class
Arithmetic and logic
Data Movement
Control Flow
Miscellaneous
x

## Slide 20: First Look: Copying Values To Registers - MOV
mov r0, r1
// Copies all 32 bits
// of the value held
// in register r1 into
// the register r0
register r0
register r1
mov r0, 100
// Expands an imm8 value 100
// stored in the instruction
// into the register r0
register r0
100
x
Immediate "addressing"
register direct "addressing"

## Slide 21: mov – Copies Register Content between registers
mov r1, r5 // r1 = r5
mov r1, 1 // r1 = 1
mov r1, -4 // r1 = -4
constant (immediate value)
destination register
mov
Rd
source register
mov
Rd
Rm
destination register
rot4
imm8
mov Rd, constant // Rd = constant
mov Rd, Rm // Rd = Rm
machine code bit fields
x
Immediate "addressing"
register direct "addressing"

## Slide 22: First Look: Add/Sub Registers
add r0, r1, r2
// Adds r1 to r2 and
// stores the result // in r0
register r0
register r1
register r2
+
x
sub r0, r1, 100
// Perform r1 – 100 and
// stores the result in
// r0
register r0
register r1
100
-

## Slide 23: add/sub/rsb – Add or Subtract two integers
add r1, r2, r3 // r1 = r2 + r3
sub r1, r1, 1 // r1 = r1 – 1; or r1--
add r1, r2, 234 // r1 = r2 + 234
add Rd, Rn, constant // Rd = Rn + constant
sub Rd, Rn, constant // Rd = Rn - constant
rsb Rd, Rn, constant // Rd = constant - Rn
add Rd, Rn, Rm // Rd = Rn + Rm
sub Rd, Rn, Rm // Rd = Rn - Rm
rsb Rd, Rn, Rm // Rd = Rm - Rn
mov r5, 5 // r5 = 5
mov r7, 7 // r7 = 7
add r7, r7, r5 // r7 = 12 r5 = 5
Operand 2 constant
destination
add/sub/rsb
Rd
rot4
imm8
Rn
operand 1
Operand 2
destination
add/sub/rsb
Rd
Rn
operand 1
Rm
x

## Slide 24: Writing a Sequence of Add & Subtract Instructions
You need to perform the following sequence of integer adds/subtracts
a = b + c + d - e;
Since ARM uses a three-operand instruction set, you can only operate on two operands at a time
So, you need to use one register as an accumulator and create a sequence of add instructions to build up the solution
a = b + c + d - e;
r0 = r1 + r2 + r3 – r4;
r0 = ((r1 + r2) + r3) – r4;
r0 = r1 + r2;
r0 = r0 + r3
r0 = r0 – r4
r0  a
r1  b
r2  c
r3  d
r4  e
a = (b + c) – 5;
r0 = (r1 + r2) – 5;
x
add r0, r1, r2
add r0, r0, r3
sub r0, r0, r4
add r0, r1, r2
sub r0, r0, 5

## Slide 25: R (register) Type Data Processing: Machine Code
Instructions that process data using three-register arguments
The general instruction format is (not all fields will be in every instruction)
opcode Rd (destination), Rn (operand 1), Rm (operand 2)
add r0, r1, r3
1110 0000 1000 0001 0000 0000 0000 0011
0xe0810003
is encoded as
in hex is
x

## Slide 26: I (immediate) Type Data Processing: Machine Code
add r0, r1, 49
1110 0000 1000 0001 0000 0000 0011 0001
0xe0810031
is encoded as
in hex is
Instructions that process data using two registers and a constant (in the instruction)
The general instruction format is (not all fields will be in every instruction)
opcode Rd (destination), Rn (operand 1), constant
x
I
immediate value
12 bits only!!!!

## Slide 27: Overview: Line Layout in an Arm Assembly Source File - 1
Assembly language source text files are line oriented (each ending in a '\n')
Each line represents a starting address in memory and does one of:
  Specifies the contents of memory for a variable (segments containing data)
  Specifies the contents of memory for an instruction (text segment)
  Assembler directives tell the assembler to do something (for example, change label scope, define a macro, etc.) that does not allocate memory
Each line is organized into up to four columns
  Not every column is used on each line
  Not every line will result in memory being allocated
label: operation operand(s) // comments
tab
white space
white space
x
column 1 column 2 column 3 column 4

## Slide 28: Overview: Line Layout in an Arm Assembly Source File - 2
Labels (optional); starts in column 1
  Only put a label on a line when you need to associate a name (a global variable, a function name, a loop/ branch target, etc.) to that lines location in memory
  You then refer to the address by name in an instruction
Operation type 1: assembler directives (all start with a period e.g. .word )
Operation Type 2: assembly language instructions
Zero or more operands as required by the instruction or assembler directive
Comments: C and C++ style; also @ in the place of a C++ comment //
x
label: operation operand(s) // comment
// assembler directive below
cnt: .word 5 /* define a global int cnt = 5; */
/* instruction example below */
add r1 r2, r3 // add the values

## Slide 29: Labels in Arm Assembly
Remember, a Label associates a name with memory location
Regular Label:
  Used with a Function name (label) or all static variables in any of the data segments
Local Label: Name starts with .L (local label prefix) only usable in the same file
  Targets for
    branches: if switch, goto, break, continue,
    loops: for, while, do-while
  Anonymous variables (the address of string not the address of foo in the following)
    char *foo = "anonymous variable"
x
.Lmesg: .string "Hello CSE30! We Are CountinG UpPpER cASe letters!"
...
main:
push {fp, lr}
...
.Lwhile:
add r2, r2, 1 // increment char pointer
local label
Regular label
local label
label main is the starting address of the push instruction
label .Lmesg is the starting address for the ascii string
label .Lwhile is the starting address of the add instruction

## Slide 30: Assembler Directives: Label Scope Control (Normal Labels only)
.extern <label>
  Imports label (function name, symbol or a static variable name);
  An address associated with the label from another file can be used by code in this file
.global <label>
  Exports label (or symbol) to be visible outside the source file boundary (other assembly or c source)
  label is either a function name or a global variable name
  Without .global, by default labels are local to the file from the point where they are defined
.extern printf
.extern fgets
.extern strcpy
.global fbuf
x

## Slide 31: Assembler Directives: .equ and .equiv
.equ <symbol>, <expression>
  Defines and sets the value of a symbol to the evaluation of the expression
  Used for specifying constants, like a #define in C
  You can (re)set a symbol many times in the file, last one seen applies
  .equ BLKSZ, 10240 // buffer size in bytes
  // other lines
  .equ BLKSZ, 1024 // buffer size in bytes
.equiv <symbol>, <expression>
  .equiv directive is like .equ except that the assembler will signal an error if symbol is already defined
.equ BLKSZ, 10240 // buffer size in bytes
.equ BUFCNT, 100*4 // buffer for 100 ints
.equiv STRSZ, 128 // buffer for 128 bytes
.equiv STRSZ, 1280 // ERROR! already defined!
.equ BLKSZ, STRSZ * 4 // redefine BLKSZ from here
x

## Slide 32: Example: Assembler Directive and Instructions
10 .equ NULL, 0
11 main:
12 3000 0310A0E1 mov r1, r3
13 .Lloop:
14 3004 043083E2 add r3, r3, 4
15 3008 001093E5 ldr r1, [r3]
16 300c 000051E3 cmp r1, NULL
17 3010 FBFFFF1A bne .Lloop
Instruction Memory Addresses (lowest 2-bits are always are 00)
Notice alignment and how addresses increase by 4 (32-bit instructions)
Regular label main
is associated with memory location 0x3000
Local label .Lloop
is associated with memory location 0x3004
assembler directive .equ does not allocate any memory (NULL = 0)
Memory Contents
Warning contents shown in "reverse" byte order: Lsb – Msb
output generated with
gcc -c -Wa,-ahlns space.S
partial output is shown
space.S
x

## Slide 33: Unconditional Branching – Forces Execution to Continue at a Specified Label (goto)
b .Ldone
:
.Ldone: add r0, EXIT_SUCCESS // set return value
Unconditional Branch instruction (branch to only local labels in CSE30)
b .Llabel
Causes an unconditional branch (aka goto) to the instruction with the address .Llabel
.Llabel is called a branch target label (the "target" of a branch instruction)
Be careful! do not to branch to a function label!
.Llabel: pc is the base register with the offset being imm24 shifted left two bits (+/- 32 MB)
  imm24 is the number of instructions from pc+8
b
imm24
x

## Slide 34: Examples of of Unconditional Branching
Branches are used to change execution flow using labels as the branch target
In these example, .Lforward and .Lbackward are the branch target labels
Branch target labels are placed at the beginning of the line (or above it)
Caution: Backward branches should only used with loops!
b .Lforward
add r1, r2, 4
add r0, r6, 2
add r3, r7, 4
.Lforward:
sub r1, r2, 4
.Lbackward:
add r1, r2, 4
sub r1, r2, 4
add r4, r6, r7
b .Lbackward
// not reachable unless there is a label after the .b above
Backward Branch
(Infinite loop)
Unconditional Branch Forward
x

## Slide 35: Anatomy of a Sample Branch: Changing the Next Instruction to Execute
if (r3 != r4) {
r1 = r2 + 1;
}
r3 = r1;
x
Branch guard: determines whether to execute the "true" block
Step 1: evaluate the branch guard(s) (involves one or more compares/tests)
Step 2: If branch guard evaluates to false
  then branch around the true block
  else execute the true block
Branch condition depend on the result of a Test (comparison)
(This test is called a branch guard)
condition true block

## Slide 36: cmp/cmm – Making Conditional Tests
cmp r1, 0 // r1 – 0 and sets flags on the result
cmp r1, r2 // r1 – r2 and sets flags on the result
cmp Rn, constant // Rn – constant; then sets condition flags
cmm Rn, constant // Rn + constant; then sets condition flags
cmp Rn, Rm // Rn – Rm; then sets condition flags
cmm Rn, Rm // Rn + Rm; then sets condition flags
Operand 2 constant
cmp/cmm
rot4
imm8
Rn
operand 1
Operand 2
cmp/cmm
Rn
operand 1
Rm
Bytes: 0 <= imm8 <= 255 + values from "rotating" rot 4 bits
The values stored in the registers Rn and Rm are not changed
The assembler will automatically substitute cmn for negative immediate values
x

## Slide 37: Quick Overview of the Condition Bits/Flags
The CSPR is a special register (like the other registers) in the CPU
The four bits at the left are called the Condition Code flags
  Summarize the result of a previous instruction
  Not all instruction will change the CC bits
Specifically, Condition Code flags are set by cmm/cmp (and others)
Example: cmp r4, r3
N (Negative) flag: Set to 1 when the result of r4 – r3 is negative, set to 0 otherwise
Z (Zero) flag: Set to 1 when the results of r4 – r3 is 0, set to 0 otherwise
C (Carry bit) flag: Set to 1 when r4 – r3 does not have a borrow, set to 0 otherwise
V flag (oVerflow): Set to 1 when r4 – r3 causes an overflow, set to 0 otherwise
N
Z
C
V
CPSR
31
30
29
28
5 0
Execution Mode
x

## Slide 38: Program Flow: Keeping the same "Block Order" as C
In ARM32, you either fall through (execute the next instruction in sequence) or branch around to a specific instruction and then resume sequential instruction execution
In order to keep the same block order as the C version that says: fall through to the condition true block when the branch guard evaluates to be true
  Assembly: invert the condition test to branch around the condition true block
Summary: In ARM32 use a condition test that specifies the opposite of the condition used in C , then branch around the condition true block
int r0;
if (r0 == 5) {
/* when true "fall through" to here */
/* condition true block */
/ * fall through */
}
/* in assembly branch to here if not true */
x
Branch guard
condition true block

## Slide 39: Conditional Branch: Changing the Next Instruction to Execute
cmp r3, r4
beq .Ldone
// otherwise fall through do the add
add r1, r2, 1
// now fall through to mov
.Ldone:
mov r3, r1
x
Condition | Meaning | Flag Checked
BEQ | Equal | Z = 1
B | Always (unconditional) | 
Use a cmp/cmm instruction to set the condition bits
Follow the cmp/cmm with one or more variants of the conditional branch instruction Conditional branch instructions if evaluate to true (bases on the CC bits set) will go to the instruction with the branch label. Otherwise, it executes the instruction that follows
You can have one or more conditional branches after a single cmp/cmm
cmp r3, r4 // r3 – r4
// if r3 != r4 sets Z = 0
if (r3 != r4)
r1 = r2 + 1;
r3 = r1;

## Slide 40: Examples: Guards (Conditional Tests) and their Inverse
Changing the conditional test (guard) to its inverse, allows you to swap the order of the blocks in an if else statement
Compare in C | "Inverse" Compare in C
== | !=
!= | ==
> | <=
>= | <
< | >=
<= | >
x

## Slide 41: Conditional Branch: Changing the Next Instruction to Execute
Branch instruction
bsuffix .Llabel
Bits in the condition field specify the conditions when the branch happens
If the condition evaluates to be true, the next instruction executed is located at .Llabel:
If the condition evaluates to be false, the next instruction executed is located immediately after the branch
Unconditional branch is when the condition is "always"
b
imm24
cond
Condition | Meaning | Flag Checked
BEQ | Equal | Z = 1
BNE | Not equal | Z = 0
BGE | Signed ≥ ("Greater than or Equal") | N = V
BLT | Signed < ("Less Than") | N ≠ V
BGT | Signed > ("Greater Than") | Z = 0 && N = V
BLE | Signed ≤ ("Less than or Equal") | Z = 1 ¦¦ N ≠ V
BHS | Unsigned ≥ ("Higher or Same") or Carry Set | C = 1
BLO | Unsigned < ("Lower") or Carry Clear | C = 0
BHI | Unsigned > ("Higher") | C = 1 && Z = 0
BLS | Unsigned ≤ ("Lower or Same") | C = 0 ¦¦ Z = 1
BMI | Minus/negative | N = 1
BPL | Plus - positive or zero (non-negative) | N = 0
BVS | Overflow | V = 1
BVC | No overflow | V = 0
B (BAL) | Always (unconditional) | 
x

## Slide 42: Program Flow: Simple If statement, No Else
Approach: adjust the conditional test then branch around the true block
Use a conditional test that specifies the inverse of the condition used in C
cmp r0, 5
bne .Lendif
/* condition true block */
/* then fall through */
.Lendif:
/* branch around to this code */
C source Code | Incorrect Assembly | Correct Assembly
int r0; if (r0 > 10) | cmp r0, 10 bgt .Lendif .Lendif: | cmp r0, 10 ble .Lendif .Lendif:
x
If r0 == 5 false
then branch around the true block
int r0;
if (r0 == 5) {
/* condition true block */
/* then fall through */
}
/* branch around to this code */
If r0 == 5 true
then fall through to the true block

## Slide 43: Branch Guard "Adjustment" Table Preserving Block Order In Code
if (r0 compare 5)
/* condition true block */
/* then fall through */
}
Compare in C | "Inverse" Compare in C | "Inverse" Signed Assembly | "Inverse" Unsigned Assembly
== | != | bne | bne
!= | == | beq | beq
> | <= | ble | bls
>= | < | blt | blo
< | >= | bge | bhs
<= | > | bgt | bhi
cmp r0, 5
inverse .Lelse
// condition true block
// then fall through
.Lendif:
x

## Slide 44: When do you use a Signed or Unsigned Conditional Branch?
Condition | Suffix For Unsigned Operands: | Suffix For Signed Operands:
> | BHI (Higher Than) | BGT (Greater Than)
>= | BHS (Higher Than or Same) (BCS) | BGE (Greater Than or Equal)
< | BLO (Lower Than) (BCC ) | BLT (Less Than)
<= | BLS (Lower Than or Same) | BLE (Less Than or Equal)
== | BEQ (Equal) | 
!= | BNE (Not Equal) | 
example with 4 bits (arm is 32)
01112 > 11002 ?
Compare
7 > 12 ?
unsigned
(FALSE)
Compare
+7 > -4 ?
signed
2's complement
(TRUE)
x

## Slide 45: Anatomy of a Conditional Branch: If statement
if (r0 != 5) {
/* condition block #2 */
} else {
/* condition block #1 */
/* fall through */
}
In C, when the branch guard (condition test) evaluates non-zero you fall through to the condition true block, otherwise you branch to the condition false block
Block order: (the order the blocks appear in C code) can be changed by inverting the conditional test, swapping the order of the true and false blocks
if (r0 == 5) {
/* condition block #1 */
} else {
/* condition block #2 */
/ * fall through */
}
x
Branch condition
Test (branch guard)
condition true block
condition false block
condition true block
condition false block
Branch condition
Test (branch guard)