## Slide 1
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 1.03
Lecture 15 – November 8, 2022
Aarch32 Assembly – Part 2

## Slide 2: Conditional Branch: Changing the Next Instruction to Execute
cmp r3, r4
beq .Ldone
// otherwise fall through do the add
add r1, r2, 1
// now fall through to mov
.Ldone:
mov r3, r1
x
Condition | Meaning | Flag Checked
BEQ | Equal | Z = 1
B | Always (unconditional) | 
How to implement a branch/loop guard in CSE30
Use a cmp/cmm instruction to set the condition bits
Follow the cmp/cmm with one or more variants of the conditional branch instruction
  Conditional branch instructions if evaluate to true (based on the flags set by the cmp) the next instruction will the one at the branch label
  Otherwise, execution falls through to the instruction that immediately follows the branch
You may have one or more conditional branches after a single cmp/cmm
cmp r3, r4 // r3 – r4
// if r3 != r4 sets Z = 0
if (r3 != r4)
r1 = r2 + 1;
r3 = r1;
Branch guard

## Slide 3: Examples: Guards (Conditional Tests) and their Inverse
Compare in C | "Inverse" Compare in C
== | !=
!= | ==
> | <=
>= | <
< | >=
<= | >
x

## Slide 4: Conditional Branch: Changing the Next Instruction to Execute
Branch instruction
bsuffix .Llabel
Bits in the condition field specify the conditions when the branch happens
If the condition evaluates to be true, the next instruction executed is located at .Llabel:
If the condition evaluates to be false, the next instruction executed is located immediately after the branch
Unconditional branch is when the condition is "always"
b
imm24
cond
Condition | Meaning | Flag Checked
BEQ | Equal | Z = 1
BNE | Not equal | Z = 0
BGE | Signed ≥ ("Greater than or Equal") | N = V
BLT | Signed < ("Less Than") | N ≠ V
BGT | Signed > ("Greater Than") | Z = 0 && N = V
BLE | Signed ≤ ("Less than or Equal") | Z = 1 ¦¦ N ≠ V
BHS | Unsigned ≥ ("Higher or Same") or Carry Set | C = 1
BLO | Unsigned < ("Lower") or Carry Clear | C = 0
BHI | Unsigned > ("Higher") | C = 1 && Z = 0
BLS | Unsigned ≤ ("Lower or Same") | C = 0 ¦¦ Z = 1
BMI | Minus/negative | N = 1
BPL | Plus - positive or zero (non-negative) | N = 0
BVS | Overflow | V = 1
BVC | No overflow | V = 0
B (BAL) | Always (unconditional) | 
x

## Slide 5: Eliminate unnecessary branches and labels: use Fall Throughs
x
mov r2, 0
b .Lnext // not needed, slows code
.Lnext:
add r1, r2, r3
Use fall-through!
do not branch to a Label on the next statement!
mov r2, 0
add r1, r2, r3

## Slide 6: Branching, What not to do: Spaghetti Code
x
mov r1, 1
mov r2, 2
b .Lthree
mov r5, 5
b .Lsix
.Lthree:
mov r3, 3
mov r4, 4
b .Lseven
.Lsix:
mov r6, 6
.Lseven:
mov r7, 7
mov r1, 1
mov r2, 2
mov r3, 3
mov r4, 4
mov r7, 7
Much faster and easier to read!
Observation
Using many branch commands (conditional or unconditional) is an indication you should look to reorganize your code
To the left are many unreachable sections of code

## Slide 7: Program Flow: Simple If statement, No Else
Approach: adjust the conditional test then branch around the true block
Use a conditional test that specifies the inverse of the condition used in C
cmp r0, 5
bne .Lendif
/* code */
/* then fall through */
.Lendif:
/* branch around to this code */
C source Code | Incorrect Assembly | Correct Assembly
int r0; if (r0 == 5) { //code } | cmp r0, 5 beq .Lendif //code .Lendif: | cmp r0, 5 bne .Lendif // code .Lendif:
x
If r0 != 5 true
then branch around the true block
int r0;
if (r0 == 5) {
/* code */
/* then fall through */
}
/* branch around to this code */
If r0 == 5 true
then fall through to the true block

## Slide 8: Branch Guard "Adjustment" Table Preserving Block Order In Code
if (r0 compare 5) {
/* condition true block */
/* then fall through */
}
Compare in C | "Inverse" Compare in C | "Inverse" Signed Assembly | "Inverse" Unsigned Assembly
== | != | bne | bne
!= | == | beq | beq
> | <= | ble | bls
>= | < | blt | blo
< | >= | bge | bhs
<= | > | bgt | bhi
cmp r0, 5
inverse .Lelse
// condition true block
// then fall through
.Lendif:
x

## Slide 9: When do you use a Signed or Unsigned Conditional Branch?
Condition | Suffix For Unsigned Operands: | Suffix For Signed Operands:
> | BHI (Higher Than) | BGT (Greater Than)
>= | BHS (Higher Than or Same) (BCS) | BGE (Greater Than or Equal)
< | BLO (Lower Than) (BCC ) | BLT (Less Than)
<= | BLS (Lower Than or Same) | BLE (Less Than or Equal)
== | BEQ (Equal) | 
!= | BNE (Not Equal) | 
example with 4 bits (arm is 32)
01112 > 11002 ?
Compare
7 > 12 ?
unsigned
(FALSE)
Compare
+7 > -4 ?
signed
2's complement
(TRUE)
x

## Slide 10: If statement examples – Branch Around the True block!
int r0;
if (r0 == 5) {
r1 = r2++ + r3;
}
r3 = r2;
int r0;
if (r0 <= 5) {
r1 = r2++;
}
r3 = r2;
unsigned int r0, r1;
if (r0 > r1) {
r1 = r0;
}
r3 = r2;
cmp r0, 5
bne .Lendif
add r1, r2, r3
add r2, r2, 1
.Lendif:
mov r3, r2
cmp r0, 5
bgt .Lendif
mov r1, r2
add r2, r2, 1
.Lendif:
mov r3, r2
cmp r0, r1
bls .Lendif
mov r1, r0
.Lendif:
mov r3, r2
x
If r0 == 5 false
then branch around the true block
Fall through
Fall through
Fall through

## Slide 11: Branching: Using Fall through!
Some call this "goto like" structure
Do not use unnecessary branches when a “fall through” works
You can see this by structures that have a conditional branch around an unconditional branch that immediately follows it
Do not do the following:
cmp r0, 0
beq .Lthen
b .Lendif
.Lthen:
add r1, r1, 1
.Lendif:
add r1, r1, 2
x
Do the following:
cmp r0, 0
bne .Lendif
// fall through
add r1, r1, 1
.Lendif:
add r1, r1, 2
Caution!
Two adjacent branches

## Slide 12: Anatomy of a Conditional Branch: If - Else statement
if (r0 != 5) {
/* condition block #2 */
} else {
/* condition block #1 */
/* fall through */
}
In C, when the branch guard (condition test) evaluates non-zero you fall through to the condition true block, otherwise you branch to the condition false block
Block order: (the order the blocks appear in C code) can be changed by inverting the conditional test, swapping the order of the true and false blocks
if (r0 == 5) {
/* condition block #1 */
} else {
/* condition block #2 */
/ * fall through */
}
x
Branch condition
Test (branch guard)
condition true block
condition false block
condition true block
condition false block
Branch condition
Test (branch guard)

## Slide 13: Program Flow: If with an Else
if (r0 == 5) {
/* cond. true block */
/* branch around false */
} else {
/* condition false block */
/* fall through */
}
r1 = 4;
If r0 == 5 false
then branch to false block
Make the adjustment to the conditional test to branch to the false block
When you finish the true block, you do an unconditional branch around the false block
The false block falls through to the following instructions
x
cmp r0, 5
bne .Lelse
/* cond. true block */
/*
* Now branch around the
* condition false block
*/
b .Lendif
.Lelse
// condition false block
// fall through
.Lendif:
mov r1, 4
If r0 == 5 false
then branch to false block

## Slide 14: If with an Else Examples
…
if (r0 < r1) {
r2 = 1;
// branch around else
} else {
r2 = 0;
/* fall through */
}
r4 = r2 + r4;
  cmp r0, r1
  bge .Lelse
  mov r2, 1
  b .Lendif
.Lelse:
mov r2, 0
/* fall through */
.Lendif:
add r4, r2, r4
x
If r0 < r1 false
then branch to false block
Branch condition
Test (branch guard)
condition true block
condition false block

## Slide 15: If with an Else Block order: All These Are Equivalent
if (r0 < r1) {
r2 = 1;
// now branch around else
} else {
r2 = 0;
/* fall through */
}
r4 = r2 + r4;
x
if (r0 >= r1) {
r2 = 0;
// now branch around else
} else {
r2 = 1;
/* fall through */
}
r4 = r2 + r4;
  cmp r0, r1
  blt .Lelse
mov r2, 0
  b .Lendif // around else
.Lelse:
  mov r2, 1
/* fall through */
.Lendif:
add r4, r2, r4
  cmp r0, r1
  bge .Lelse
  mov r2, 1
  b .Lendif
.Lelse:
mov r2, 0
/* fall through */
.Lendif:
add r4, r2, r4
  cmp r0, r1
  bge .Lelse
  mov r2, 1
  b .Lendif // around else
.Lelse:
mov r2, 0
/* fall through */
.Lendif:
add r4, r2, r4
Same test
swapped blocks

## Slide 16: Switch Statement
switch (r0) {
case 1:
// block 1
break;
case 2:
// block 2
break;
default:
// default 3
break;
}
cmp r0, 1
bne .Lblk2
// block 1
b .Lendsw // break
.Lblk2:
cmp r0, 2
bne .Ldefault
// block 2
b .Lendsw // break
.Ldefault:
// default 3
// fall through
// NO b .Lendsw
.Lendsw:
x
cmp r0, 1
beq .Lblk1
cmp r0, 2
beq .Lblk2
// fall through
// default 3
b .Lendsw // break
.Lblk1:
// block 1
b .Lendsw // break
.Lblk2:
// block 2
// fall through
// NO b .Lendsw
.Lendsw:
Approach 1 – Branch Block
Approach 2 – if else equiv.
Branch block

## Slide 17: Bad Style: Branching Upwards (When Not a loop)
Do not Branch "Upwards" unless it is part of a loop (later slides)
If you cannot easily write the equivalent C code for your assembly code, you may have code that is harder to read than it should be
Action: adjust your assembly code to have a similar structure as an equivalent version written in C
  cmp r3, r4
  blt .Lendif
  beq .Lelse1
  bgt .Lelse2
.Lelse1:
mov r2, 0
b .Lendif
.Lelse2:
add r4, r3, r2
b .Lelse1
.Lendif:
add r4, r2, r4
x
Upwards
branch
  cmp r3, r4
  blt .Lendif
  beq .Lelse1
add r4, r3, r2
.Lelse1:
mov r2, 0
.Lendif:
add r4, r2, r4
eliminate this branch
replace with fall through
eliminate this branch

## Slide 18: Program Flow – Short Circuit or Minimal Evaluation
In evaluation of conditional guard expressions, C uses what is called short circuit or minimal evaluation
Each expression argument is evaluated in sequence from left to right including any side effects (modified using parenthesis), before (optionally) evaluating the next expression argument
If after evaluating an argument, the value of the entire expression can be determined, then the remaining arguments are NOT evaluated (for performance)
x
if ((x == 5) || (y > 3)) // if x == 5 then y > 3 is not evaluated
if ((a != 0) && func(b)) // if a is 0, func(b) is not called
// do_something();

## Slide 19: Program Flow – If statements && compound tests - 1
if ((r0 == 5) && (r1 > 3)) {
r2 = r5; // true block
/* fall through */
}
r4 = r3;
cmp r0, 5
bne .Lendif
cmp r1, 3
ble .Lendif
mov r2, r5 // true block
// fall through
.Lendif:
mov r4, r3
If r0 == 5 false
then short circuit branch around the true block
x

## Slide 20: Program Flow – If statements && compound tests - 2
cmp r0, 5 // test 1
bne .Lelse
cmp r1, 3 // test 2
ble .Lelse
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse:
mov r5, r2 //false block
// fall through
.Lendif:
mov r4, r3
if r0 == 5 false
then short circuit branch to the false block
if ((r0 == 5) && (r1 > 3)) {
r2 = r5; // true block
// branch around else
} else {
r5 = r2; False block */
/* fall through */
}
r4 = r3;
x
if r1 > 3 false
then branch to the false block

## Slide 21: Program Flow – If statements || compound tests - 1
if ((r0 == 5) || (r1 > 3)) {
r2 = r5; // true block
/* fall through */
}
r4 = r3;
cmp r0, 5
beq .Lthen
cmp r1, 3
ble .Lendif
// fall through
.Lthen:
mov r2, r5 // true block
/* fall through */
.Lendif:
mov r4, r3
If r0 == 5 true, then branch to true block
if r1 > 3 false then branch around true block
x

## Slide 22: Program Flow – If statements || compound tests - 2
cmp r0, 5
beq .Lthen
cmp r1, 3
ble .Lelse
// fall through
.Lthen:
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse
mov r5, r2 // false block
// fall through
.Lendif:
if ((r0 == 5) || (r1 > 3)) {
r2 = r5; // true block
/* branch around else */
} else {
r5 = r2; // false block
/* fall through */
}
x
If r0 == 5 true, then branch to the true block
if r1 > 3 false then branch to false block

## Slide 23: Program Flow – Pre-test and Post-test Loop Guards
loop guard: code that must evaluate to true before the next iteration of the loop
If the loop guard test(s) evaluate to true, the body of the loop is executed again
pre-test loop guard is at the top of the loop
  If the test evaluates to true, execution falls through to the loop body
  if the test evaluates to false, execution branches around the loop body
post-test loop guard is at the bottom of the loop
  If the test evaluates to true, execution branches to the top of the loop
  If the test evaluates to false, execution falls through the instruction following the loop
x
while (i < 10) {
/* block */
i++;
}
pre-test
loop guard
loop control variable
zero or more iterations
do {
/* block */
i++;
} while (i < 10);
post-test
loop guard
one or more iterations

## Slide 24: Pre-Test Guards - While Loop
.Lwhile:
cmp r1, 10
bge .Lendw
// block
add r1, r1, 1
b .Lwhile
.Lendw:
mov r2, r1
while (r1 < 10) {
/* block */
r1++;
}
r2 = r1;
x
pre-test
loop guard
loop iteration
.Lwhile:
cmp r1, 10
bge .Lendw
cmp r2, r1
beq .Lnext
// block
.Lnext:
add r1, r1, 1
b .Lwhile
.Lendw:
mov r2, r1
while (r1 < 10) {
if (r2 != r1) {
/* block */
}
r1++;
}
r2 = r1;
pre-test
loop guard
loop iteration
inverted test
if stmt guard

## Slide 25: Post-Test Guards – Do While Loop
.Ldo:
// block
add r1, r1, 1
cmp r1, 10
blt .Ldo
mov r2, r1
.Ldo:
cmp r2, r1
beq .Lnext
// block
.Lnext
add r1, r1, 1
cmp r1, 10
blt .Ldo
move r2, r1
do {
/* block */
r1++;
} while (r1 < 10);
r2 = r1;
x
loop iteration
post-test
loop guard
do {
if (r2 != r1) {
/* block */
}
r1++;
} while (r1 < 10);
r2 = r1;
loop iteration
post-test
loop guard
test is not inverted

## Slide 26: Program Flow – Counting (For) Loop
mov r1, 0
.Lfor:
cmp r1, 10
bge .Lendfr
// block code
add r1, r1, 1
b .Lfor
.Lendfr:
A counting loop has three parts:
Pre-loop setup
Pre-test loop guard conditions
Post-loop update
Alternative:
move Pre-test loop guard before the loop
Add post-test loop guard
  converts to do while
  removes an unconditional branch
for (r1 = 0; r1 < 10; r1++) {
/* block */
}
mov r1, 0
cmp r1, 10
bge .Lendfr
.Ldo:
// block code
add r1, r1, 1
cmp r1, 10
blt .Ldo
.Lendfr:
Alternative
Pre loop setup
Pre-test
Loop guard
Post loop update
x
Post loop update
Pre loop setup
Pre-loop setup
Post loop update
Pre-test loop guard
Pre-test loop guard
Post-test loop guard

## Slide 27: Nested loops
Nest loop blocks as you would in C or Java
Do not branch into the middle of a loop, this is hard to read and is prone to errors
for (r3 = 0; r3 < 10; r3++) {
r0 = 0;
do {
r0 = r0 + r1++;
} while (r1 < 10);
// fall through
r2 = r2 + r1;
}
r5 = r0;
x
mov r3, 0
.Lfor:
cmp r3, 10 // loop guard
bge .Lendfor
mov r0, 0
.Ldo:
add r0, r0, r1
add r1, r1, 1
cmp r1, 10 // loop guard
blt .Ldo
// fall through
add r2, r2, r1
add r3, r3, 1 // loop iteration
b .Lfor
.Lendfor:
mov r5, r0

## Slide 28: Keep loops Properly Nested: Do not branch into the middle of a loop
It is hard to understand and debug loops when you branch into the middle of a loop
Keep loops proper nested
Do not do the following:
.Lloop1:
add r1, r1, 1
.Lloop2:
add r2, r2, 1
add r2, r1, r3
cmp r1, 10
blt .Lloop1
beq .Lend1
add r3, r3, 1
cmp r2, 20
ble .Lloop2
.Lend1:
x
Bad practice: branch into loop body

## Slide 29
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 1.03
Lecture 16 – November 10, 2022
Aarch32 Assembly – Part 2

## Slide 30: What is a Bitwise Operation?
Bitwise operators are applied independently to each of the corresponding bit positions in each variable
Each bit position of the result depends only on bits in the same bit position within the operands
a = | a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
 | <op> | <op> | <op> | <op> | <op> | <op> | <op> | <op>
b = | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
result = | c7 | c6 | c5 | c4 | c3 | c2 | c1 | c0
x

## Slide 31: Bitwise (Bit to Bit) Operators in C
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
output = a | b;
| with 1 to set a bit to 1
| with 0 to let a bit through
a | ~a
0 | 1
1 | 0
output = ~a;
a | b | a ^ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
output = a ^ b; //EOR
^ with 1 will flip the bit
^ with 0 to let a bit through
a | b | a & b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
output = a & b;
& with 1 to let a bit through
& with 0 to set a bit to 0
0110
& 1100
----
0100
Bitwise
AND
0110
| 1100
----
1110
Bitwise
OR
0110
^ 1100
----
1010
Bitwise
EOR
~ 1100
----
0011
Bitwise
NOT
x

## Slide 32: Bitwise Not (vs Boolean Not)
a | ~a
0 | 1
1 | 0
in C
int output = ~a;
x
Boolean operators act on the entire value not the individual bits
Meaning | Operator | Operator | Meaning
Boolean NOT | !b | ~b | Bitwise NOT
 | Bitwise Not
number | 0101 1010 0101 1010 1111 0000 1001 0110
~number | 1010 0101 1010 0101 0000 1111 0110 1001
Type | Operation | result
bitwise | ~0x01 | 1111 1111 1111 1111 1111 1111 1111 1110
Boolean | !0x01 | 0000 0000 0000 0000 0000 0000 0000 0000
~ 1100
----
0011
Bitwise NOT

## Slide 33: First Look: Copying Values To Registers – MVN (not)
A bitwise NOT operation
mvn r0, r1
// Copies all 32 bits
// of the value held
// in register r1 into
// the register r0
// then does a bitwise NOT
register r0
register r1
mvn r0, 12
// Expands an imm8 value 0x0c
// stored in the instruction
// into a register then does
// a bitwise NOT
0xffff fff3
0x0c
x
~ 1100
----
0011
Bitwise NOT
register r0
0xfffffff3
0x 0c
imm8 expansion
0x0000000c
bitwise not

## Slide 34: mvn – Copies NOT (~) (1's Compliment Copy)
constant (immediate value)
destination register
mvn
Rd
source register
mvn
Rd
Rm
destination register
bitwise NOT operation. Immediate (constant) version copies to 32-bit register, then does a bitwise NOT
mvn r1, 4 // x = ~4
mvn r1, r5 // x = ~y in C
mvn r1, 0 // x = -1
imm8 | extended imm8 | inverted imm8 | signed base 10
0x00 | 0x00 00 00 00 | 0xff ff ff ff | -1
0xff | 0x00 00 00 ff | 0xff ff ff 00 | -256
0xfffffffb
r1
0x4
invert the bits
0x00000004
copy into 32 bits zero extend
0xaaaaaaaa
0x55555555
r5
r1
rot4
imm8
~ 1100
----
0011
Bitwise NOT
x
mvn Rd, constant // Rd = constant
mvn Rd, Rm // Rd = Rm
0x0
0x11111111
r1

## Slide 35: Bitwise versus C Boolean Operators
Boolean operators act on the entire value not the individual bits
& versus &&
0x10 & 0x01 = 0x00 (bitwise)
0x10 && 0x01 = 0x01 (Boolean)
! versus ~
~0x01 = 0xfffffffe (bitwise)
!0x01 = 0x0 (Booelan)
Meaning | Operator | Operator | Meaning
Boolean AND | a && b | a & b | Bitwise AND
Boolean OR | a ¦¦ b | a ¦ b | Bitwise OR
Boolean NOT | !b | ~b | Biwise NOT
x

## Slide 36: Bitwise Instructions
<op> Rd, Rn, constant // Rd = Rn <op> constant
<op> Rd, constant // Rd = Rd <op> constant
<op> Rd, Rn, Rm // Rd = Rn <op> Rm
Operand 2 constant
destination
<op>
Rd
rot4
imm8
Rn
operand 1
Operand 2
destination
<op>
Rd
Rn
operand 1
Rm
Bytes: 0 <= imm8 <= 255 + values from "rotating" rot 4 bits
Bitwise <op> description | C Syntax | Arm <op> Syntax | Operation
Bitwise AND | ~x | and Rd, Rn, Op2 | Rd  Rn & Op2
Bit Clear each bit in Op2 that is a 1, the same bit in Rd, is cleared | <none> | bic Rd, Rn, Op2 | Rd  Rn & ~Op2
Bitwise OR | a & b | orr Rd, Rn, Op2 | Rd  Rn ¦ Op2
Exclusive OR | a ^ b | eor Rd, Rn, Op2 | Rd  Rn ^ Op2
x

## Slide 37: The act (operation) of Masking
Bit masks access/modify specific bits in memory
Masking act of applying a mask to a value with a specific op:
orr: 0 passes bit unchanged, 1 sets bit to 1
eor: 0 passes bit unchanged, 1 inverts the bit
bic: 0 passes bit unchanged, 1 clears it
and: 0 clears the bit, 1 passes bit unchanged
x
a = | a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
 | <op> | <op> | <op> | <op> | <op> | <op> | <op> | <op>
b = | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
result = | c7 | c6 | c5 | c4 | c3 | c2 | c1 | c0

## Slide 38: Mask on and Mask off
force lower 16 bits to 1 "mask on" operation
  1 to set a bit to 1
  0 to let a bit through unchanged
orr r1, r2, r3
x
force lower 8 bits to 0 "mask off" operation
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, r3
DATA: r2 0xab ab ab 77
orr
MASK: r3 0x00 00 ff ff
RSLT: r1 0xab ab ff ff
forces to a 1
unchanged
DATA: r2 0xab ab ab 77
and
MASK: r3 0xff ff ff 00
RSLT: r1 0xab ab ab 00
forces to a 0
unchanged

## Slide 39: Mask off versus Bit Clear
x
force lower 8 bits to 0 "mask off" operation
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, r3
DATA: r2 0xab ab ab 77
and
MASK: r3 0xff ff ff df
RSLT: r1 0xab ab ab 57
forces to a 0
unchanged
df: 1101 1111
77: 0111 0111
57: 0101 0111
clear bit 5 to a 0 without changing the other bits
r1 = r2 & ~r3
bic r1, r2, r3
forces to a 0
unchanged
DATA: r2 0xab ab ab 77
bic
MASK: r3 0x00 00 00 20
RSLT: r1 0xab ab ab 57
r3: 0010 0000
~r3: 1101 1111
clears bit 5
unchanged

## Slide 40: Extracting (Isolate) a Field of Bits with a mask
x
extract top 8 bits of r2 into r1
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, r3
DATA: r2 0xab ab ab 77
and
MASK: r3 0xff 00 00 00
RSLT: r1 0xab 00 00 00
forces to a 0
unchanged

## Slide 41: Finding if a bit is set
x
query the status of a bit "bit status" operation
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, r3
cmp r1, 0
bne .Lis_set
// code
.Lis_set
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 02 is bit 1 set?
RSLT: r1 0x00 00 00 02 != 0 if set
forces to a 0
unchanged
77: 0111 0111
01: 0000 0010
and
r1: 0000 0010
75: 0111 0101
01: 0000 0010
and
r1: 0000 0000

## Slide 42: Even/Odd : MOD %<power of 2>
remainder (mod): num % d where num ≥ 0 and d = 2k
mask = 2k -1 so for mod 16, mask = 16 -1 = 15
and r1, r2, r3
Even or odd, check LSB (same as mod %2)
check LSB (bit 0) if set then odd, else even
and r1, r2, r3
cmp r1, 1
beq .Lodd
// code
.Lodd:
x
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 01 (mod 2 even or odd)
RSLT: r1 0x00 00 00 01 (odd)
forces to a 0
unchanged
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 0f (mod 16)
RSLT: r1 0xab 00 00 07
forces to a 0
unchanged

## Slide 43: Flipping bits: bit toggle Used in PA8
x
invert (flip) the lower 8-bits "bit toggle" operation
  1 will flip the bit
  0 to let a bit through
eor r1, r2, r3
Observation: When applied twice, it returns the original value (symmetric encoding)
With a mask of all 1's is a 1's compliment
DATA: r2 0xab ab ab 77
eor
MASK: r3 0x00 00 00 ff
RSLT: r1 0xab ab ab 88
inverts (flips)
unchanged
77: 0111 0111
88: 1000 1000
DATA: r1 0xab ab ab 88
eor
MASK: r3 0x00 00 00 ff apply a 2nd time
RSLT: r1 0xab ab ab 77 original value!
inverts (flips)

## Slide 44: Shift and Rotate Instructions
Instruction | Syntax | Operation | Notes | Diagram
Logical Shift Left int x; x << 1; | LSL Rd, Rm, const5 LSL Rd, Rm, Rs | Rd  Rm << const5 Rd  Rm << Rs | Zero fills shift: 0 - 31 | 
Logical Shift Right unsigned int x; x >> 1; | LSR Rd, Rm, const5 LSR Rd, Rm, Rs | Rd  Rm >> const5 Rd  Rm >> Rs | Zero fills shift: 1 - 32 | 
Arithmetic Shift Right int x; x >> 1; | ASR Rd, Rm, const5 ASR Rd, Rm, Rs | Rd  Rm >> const5 Rd  Rm >> Rs | Sign extends shift: 1 - 32 | 
Rotate Right unsigned int x; x = (x>>1)¦(x<<31) ; | ROR Rd, Rm, const5 ROR Rd, Rm, Rs | Rd  Rm ror const5 Rd  Rm ror Rs | right rotate rot: 0 - 31 | 
operand 2 constant
destination
<inst>
Rd
const5
Rm
operand 1
Number of bit to shift or rotate: const5
operand 2
destination
<inst>
Rd
Rm
operand 1
Rs
Number of bit to shift or rotate: Rs
x

## Slide 45: Arithmetic Shift Right (there is no arithmetic shift left)
asr r2, r0, 8
r0 0xab ab ab 77
r2 0xff ab ab ab (see the sign extend)
asr r2, r0, 31
cmp r2, 0
beq .Lispos
//code
.Lispos:
Test for sign
0 if r0 positive
asr r2, r0, 31
cmp r2, -1
beq .Lisneg
//code
.Lisneg:
Test for sign
-1 if r0 negative
x
r0 0xab ab ab 77
r2 0xff ff ff ff
r0 0x7b ab ab 77
r2 0x00 00 00 00

## Slide 46: Logical Shift & Rotate Operations
lsr r2, r0, 8
r0 0xab ab ab 77
r2 0x00 ab ab ab
lsl r2, r0, 8
r0 0xab ab ab 77
r2 0xab ab 77 00
ror r2, r0, 8
r0 0xab ab ab 77
r2 0x77 ab ab ab
x

## Slide 47: Extracting/Isolating Unsigned Bitfields
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
next shift left = 8
r0
byte 0
byte 1
byte 3
byte 2
Move byte 2 in r0 to byte 0 in r1
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
lsr r1, r1, 24
unsigned zero-extension (all 0’s)
Extracted bit-field
r1
byte 0
byte 1
byte 3
byte 2
lsl r1, r0, 8
Next shift right = 24
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far left
pushed bits to far right
Hint: Useful for PA8

## Slide 48: Extracting Signed Bitfields
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
next shift left = 8
r0
byte 0
byte 1
byte 3
byte 2
Move byte 2 in r0 to byte 0 in r1
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
lsl r1, r0, 8
next shift right = 24
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far left
asr r1, r1, 24
signed extend (all 1’s)
Extracted
bit-field
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far right

## Slide 49: Inserting Bitfields – Inserting Source Field into Destination Field
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
r1
r0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Task: Insert source into destination
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
results in
orr r1, r1, r2
r1
r2
Approach
(1) isolate source field
(2) clear destination field
(3) Bitwise or together
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 50: Inserting Bitfields – Isolating the Source Field
r2
r0
x
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
isolate source field
lsl r2, r0, 24
lsr r2, r2, 8
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r0
r2

## Slide 51: Inserting Bitfields – Clearing the Destination Field
x
lsl r1, r1, 8
r1
r3
1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
r1
r1
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
clear the destination field
ror r1, r1, 24
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
ror r1, r1, 16

## Slide 52: Inserting Bitfields – Combining Isolated Source and Cleared Destination
x
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
inserted field
orr r1, r1, r0
r1
r2
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
isolated source
r1
r1
field cleared in destination

## Slide 53: Masking Summary
Isolate a field: Use lsr, lsl, rot to get a field surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Select a field: Use and with a mask of one's surrounded by zero's to select the bits that have a 1 in the mask, all other bits will be set to zero
Clear a field: Use and with a mask of zero's surrounded by one's to select the bits that have a 1 in the mask, all other bits will be set to zero
1 1 1 1 1 1 1 1 | 0 0 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
x
0 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 | 0 0 0 0 0 0 0 0 0 0 0 0 0 0
selects this field when used with and
selection mask
clear a field mask
clears this field when used with and
lsl to get this edge into msb
lsr to get this edge into lsb
Insert a field: Use orr with fields surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Keep these bits | 0 0 0 0 0 0 0 0 | Keep these bits

## Slide 54: Extra Slides

## Slide 55: How are I – Type Constants Encoded in the instruction?
Aarch32 provides only 8-bits for specifying an immediate constant value
Without "rotation" immediate values are limited to the range of positive 0-255
Imm8 expands to 32 bits and does a rotate right to achieve additional constant values (YUCK)
positions to
rotate X 2
unsigned value to rotate
rot4 value | 32-bit constant result
0000 | 0000 0000 0000 0000 0000 0000 1111 1111
0001 (2 bits) | 1100 0000 0000 0000 0000 0000 0011 1111
x
two bits rotated right
results are interpreted as a 2's complement number

## Slide 56: Rot4 - Imm8 Values
positions to
rotate X 2
unsigned value to rotate
00000001
x
How would 256 be encoded?
  rotate = 12, imm8 = 1
Bottom line: the assembler will do this for you
If you try and use an immediate value that it cannot generate it will give an error
There is a workaround - later
results are interpreted as a 2's complement number

## Slide 57: Branch Target Address (BTA): What Is imm24?
Previous slide: phases of execution: (1) fetch, (2) decode, (3) execute
The pc (r15) contains the address of the instruction being fetched, which is two instructions ahead or executing instruction + 8 bytes
Branch target address (or imm24) is the distance measured in the # of instructions (signed, 2's complement) from the fetch address contained in r15 when executing the branch
imm24 | 0x 00 00 02
0001042c <inloop>:
1042c: e3530061 cmp r3, 0x61
10430: ba000002 blt 10440 <store>
10434: e353007a cmp r3, 0x7a
10438: ca000000 bgt 10440 <store>
1043c: e2433020 sub r3, r3, #32
00010440 <store>:
10440: e7c13002 strb r3, [r1, r2]
10444: e2822001 add r2, r2, 0x1
10448: e7d03002 ldrb r3, [r0, r2]
1044c: e3530000 cmp r3, 0x0
10450: 1afffff5 bne 1042c <inloop>
x
executing instruction
decode instruction
fetch instruction
BTA: + 2 instructions
target address = 0x10440
fetch address = 0x10438
distance(bytes) = 0x00008
distance(instructions)= 0x8/(4 bytes/instruction)= 0x2

## Slide 58: Basic Arm Machine Code Instructions
Instructions consist of several fields that encode the opcode and arguments to the opcode
Special fields enable extended functionality - later
Several 4-bit operand fields for specifying the source and destination of the operation, usually one of the 16 registers
Embedded constants ("immediate values") of various size and "configuration"
Basic Data processing instruction formats (below)
R type instruction: add r0, r1, r2 // third operand is a register
I type instruction: add r0, r0, 1 // third operand is an immediate value
Rotate
x

## Slide 59: Program Flow – multiple branches, one cmp
There are many other ways to do this
if ((r0 > 5) {
/* condition block 1 */
// branch to endif
} else if (r0 < 5){
/* condition block 2 */
// branch to endif
} else {
/* condition block 3 */
// fall through to endif
}
// endif
r1 = 11;
cmp r0, 5
bgt .Lblk1
blt .Lblk2
// fall through
// condition block 3
b .Lendif
.Lblk1:
// condition block 1
b .Lendif
.Lblk2:
// condition block 2
b .Lendif
.Lendif:
mov r1, 5
special case: multiple branches from one cmp
x