## Slide 1
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 1.00
Lecture 15 – November 8, 2022
Aarch32 Assembly – Part 2

## Slide 2: Conditional Branch: Changing the Next Instruction to Execute
cmp r3, r4
beq .Ldone
// otherwise fall through do the add
add r1, r2, 1
// now fall through to mov
.Ldone:
mov r3, r1
x
Condition | Meaning | Flag Checked
BEQ | Equal | Z = 1
B | Always (unconditional) | 
How to implement a branch/loop guard in CSE30
Use a cmp/cmm instruction to set the condition bits
Follow the cmp/cmm with one or more variants of the conditional branch instruction
  Conditional branch instructions if evaluate to true (based on the flags set by the cmp) the next instruction will the one at the branch label
  Otherwise, execution falls through to the instruction that immediately follows the branch
You may have one or more conditional branches after a single cmp/cmm
cmp r3, r4 // r3 – r4
// if r3 != r4 sets Z = 0
if (r3 != r4)
r1 = r2 + 1;
r3 = r1;
Branch guard

## Slide 3: Examples: Guards (Conditional Tests) and their Inverse
Compare in C | "Inverse" Compare in C
== | !=
!= | ==
> | <=
>= | <
< | >=
<= | >
x

## Slide 4: Conditional Branch: Changing the Next Instruction to Execute
Branch instruction
bsuffix .Llabel
Bits in the condition field specify the conditions when the branch happens
If the condition evaluates to be true, the next instruction executed is located at .Llabel:
If the condition evaluates to be false, the next instruction executed is located immediately after the branch
Unconditional branch is when the condition is "always"
b
imm24
cond
Condition | Meaning | Flag Checked
BEQ | Equal | Z = 1
BNE | Not equal | Z = 0
BGE | Signed ≥ ("Greater than or Equal") | N = V
BLT | Signed < ("Less Than") | N ≠ V
BGT | Signed > ("Greater Than") | Z = 0 && N = V
BLE | Signed ≤ ("Less than or Equal") | Z = 1 ¦¦ N ≠ V
BHS | Unsigned ≥ ("Higher or Same") or Carry Set | C = 1
BLO | Unsigned < ("Lower") or Carry Clear | C = 0
BHI | Unsigned > ("Higher") | C = 1 && Z = 0
BLS | Unsigned ≤ ("Lower or Same") | C = 0 ¦¦ Z = 1
BMI | Minus/negative | N = 1
BPL | Plus - positive or zero (non-negative) | N = 0
BVS | Overflow | V = 1
BVC | No overflow | V = 0
B (BAL) | Always (unconditional) | 
x

## Slide 5: Eliminate unnecessary branches and labels: use Fall Throughs
x
mov r2, 0
b .Lnext // not needed, slows code
.Lnext:
add r1, r2, r3
Use fall-through!
do not branch to a Label on the next statement!
mov r2, 0
add r1, r2, r3

## Slide 6: Branching, What not to do: Spaghetti Code
x
mov r1, 1
mov r2, 2
b .Lthree
mov r5, 5
b .Lsix
.Lthree:
mov r3, 3
mov r4, 4
b .Lseven
.Lsix:
mov r6, 6
.Lseven:
mov r7, 7
mov r1, 1
mov r2, 2
mov r3, 3
mov r4, 4
mov r7, 7
Much faster and easier to read!
Observation
Using many branch commands (conditional or unconditional) is an indication you should look to reorganize your code
To the left are many unreachable sections of code

## Slide 7: Program Flow: Simple If statement, No Else
Approach: adjust the conditional test then branch around the true block
Use a conditional test that specifies the inverse of the condition used in C
cmp r0, 5
bne .Lendif
/* code */
/* then fall through */
.Lendif:
/* branch around to this code */
C source Code | Incorrect Assembly | Correct Assembly
int r0; if (r0 == 5) { //code } | cmp r0, 5 beq .Lendif //code .Lendif: | cmp r0, 5 bne .Lendif // code .Lendif:
x
If r0 != 5 true
then branch around the true block
int r0;
if (r0 == 5) {
/* code */
/* then fall through */
}
/* branch around to this code */
If r0 == 5 true
then fall through to the true block

## Slide 8: Branch Guard "Adjustment" Table Preserving Block Order In Code
if (r0 compare 5) {
/* condition true block */
/* then fall through */
}
Compare in C | "Inverse" Compare in C | "Inverse" Signed Assembly | "Inverse" Unsigned Assembly
== | != | bne | bne
!= | == | beq | beq
> | <= | ble | bls
>= | < | blt | blo
< | >= | bge | bhs
<= | > | bgt | bhi
cmp r0, 5
inverse .Lelse
// condition true block
// then fall through
.Lendif:
x

## Slide 9: When do you use a Signed or Unsigned Conditional Branch?
Condition | Suffix For Unsigned Operands: | Suffix For Signed Operands:
> | BHI (Higher Than) | BGT (Greater Than)
>= | BHS (Higher Than or Same) (BCS) | BGE (Greater Than or Equal)
< | BLO (Lower Than) (BCC ) | BLT (Less Than)
<= | BLS (Lower Than or Same) | BLE (Less Than or Equal)
== | BEQ (Equal) | 
!= | BNE (Not Equal) | 
example with 4 bits (arm is 32)
01112 > 11002 ?
Compare
7 > 12 ?
unsigned
(FALSE)
Compare
+7 > -4 ?
signed
2's complement
(TRUE)
x

## Slide 10: If statement examples – Branch Around the True block!
int r0;
if (r0 == 5) {
r1 = r2++ + r3;
}
r3 = r2;
int r0;
if (r0 <= 5) {
r1 = r2++;
}
r3 = r2;
unsigned int r0, r1;
if (r0 > r1) {
r1 = r0;
}
r3 = r2;
cmp r0, 5
bne .Lendif
add r1, r2, r3
add r2, r2, 1
.Lendif:
mov r3, r2
cmp r0, 5
bgt .Lendif
mov r1, r2
add r2, r2, 1
.Lendif:
mov r3, r2
cmp r0, r1
bls .Lendif
mov r1, r0
.Lendif:
mov r3, r2
x
If r0 == 5 false
then branch around the true block
Fall through
Fall through
Fall through

## Slide 11: Branching: Using Fall through!
Some call this "goto like" structure
Do not use unnecessary branches when a “fall through” works
You can see this by structures that have a conditional branch around an unconditional branch that immediately follows it
Do not do the following:
cmp r0, 0
beq .Lthen
b .Lendif
.Lthen:
add r1, r1, 1
.Lendif:
add r1, r1, 2
x
Do the following:
cmp r0, 0
bne .Lendif
// fall through
add r1, r1, 1
.Lendif:
add r1, r1, 2
Caution!
Two adjacent branches

## Slide 12: Anatomy of a Conditional Branch: If - Else statement
if (r0 != 5) {
/* condition block #2 */
} else {
/* condition block #1 */
/* fall through */
}
In C, when the branch guard (condition test) evaluates non-zero you fall through to the condition true block, otherwise you branch to the condition false block
Block order: (the order the blocks appear in C code) can be changed by inverting the conditional test, swapping the order of the true and false blocks
if (r0 == 5) {
/* condition block #1 */
} else {
/* condition block #2 */
/ * fall through */
}
x
Branch condition
Test (branch guard)
condition true block
condition false block
condition true block
condition false block
Branch condition
Test (branch guard)

## Slide 13: Program Flow: If with an Else
if (r0 == 5) {
/* cond. true block */
/* branch around false */
} else {
/* condition false block */
/* fall through */
}
r1 = 4;
If r0 == 5 false
then branch to false block
Make the adjustment to the conditional test to branch to the false block
When you finish the true block, you do an unconditional branch around the false block
The false block falls through to the following instructions
x
cmp r0, 5
bne .Lelse
/* cond. true block */
/*
* Now branch around the
* condition false block
*/
b .Lendif
.Lelse
// condition false block
// fall through
.Lendif:
mov r1, 4
If r0 == 5 false
then branch to false block

## Slide 14: If with an Else Examples
…
if (r0 < r1) {
r2 = 1;
// branch around else
} else {
r2 = 0;
/* fall through */
}
r4 = r2 + r4;
  cmp r0, r1
  bge .Lelse
  mov r2, 1
  b .Lendif
.Lelse:
mov r2, 0
/* fall through */
.Lendif:
add r4, r2, r4
x
If r0 < r1 false
then branch to false block
Branch condition
Test (branch guard)
condition true block
condition false block

## Slide 15: If with an Else Block order: All These Are Equivalent
if (r0 < r1) {
r2 = 1;
// now branch around else
} else {
r2 = 0;
/* fall through */
}
r4 = r2 + r4;
x
if (r0 >= r1) {
r2 = 0;
// now branch around else
} else {
r2 = 1;
/* fall through */
}
r4 = r2 + r4;
  cmp r0, r1
  blt .Lelse
mov r2, 0
  b .Lendif // around else
.Lelse:
  mov r2, 1
/* fall through */
.Lendif:
add r4, r2, r4
  cmp r0, r1
  bge .Lelse
  mov r2, 1
  b .Lendif
.Lelse:
mov r2, 0
/* fall through */
.Lendif:
add r4, r2, r4
  cmp r0, r1
  bge .Lelse
  mov r2, 1
  b .Lendif // around else
.Lelse:
mov r2, 0
/* fall through */
.Lendif:
add r4, r2, r4
Same test
swapped blocks

## Slide 16: Switch Statement
switch (r0) {
case 1:
// block 1
break;
case 2:
// block 2
break;
default:
// default 3
break;
}
cmp r0, 1
bne .Lblk2
// block 1
b .Lendsw // break
.Lblk2:
cmp r0, 2
bne .Ldefault
// block 2
b .Lendsw // break
.Ldefault:
// default 3
// fall through
// NO b .Lendsw
.Lendsw:
x
cmp r0, 1
beq .Lblk1
cmp r0, 2
beq .Lblk2
// fall through
// default 3
b .Lendsw // break
.Lblk1:
// block 1
b .Lendsw // break
.Lblk2:
// block 2
// fall through
// NO b .Lendsw
.Lendsw:
Approach 1 – Branch Block
Approach 2 – if else equiv.
Branch block

## Slide 17: Bad Style: Branching Upwards (When Not a loop)
Do not Branch "Upwards" unless it is part of a loop (later slides)
If you cannot easily write the equivalent C code for your assembly code, you may have code that is harder to read than it should be
Action: adjust your assembly code to have a similar structure as an equivalent version written in C
  cmp r3, r4
  blt .Lendif
  beq .Lelse1
  bgt .Lelse2
.Lelse1:
mov r2, 0
b .Lendif
.Lelse2:
add r4, r3, r2
b .Lesle1
.Lendif:
add r4, r2, r4
x
Upwards
branch
  cmp r3, r4
  blt .Lendif
  beq .Lelse1
add r4, r3, r2
.Lelse1:
mov r2, 0
.Lendif:
add r4, r2, r4
eliminate this branch
replace with fall through
eliminate this branch

## Slide 18: Program Flow – Short Circuit or Minimal Evaluation
In evaluation of conditional guard expressions, C uses what is called short circuit or minimal evaluation
Each expression argument is evaluated in sequence from left to right including any side effects (modified using parenthesis), before (optionally) evaluating the next expression argument
If after evaluating an argument, the value of the entire expression can be determined, then the remaining arguments are NOT evaluated (for performance)
x
if ((x == 5) || (y > 3)) // if x == 5 then y > 3 is not evaluated
if ((a != 0) && func(b)) // if a is 0, func(b) is not called
// do_something();

## Slide 19: Program Flow – If statements && compound tests - 1
if ((r0 == 5) && (r1 > 3)) {
r2 = r5; // true block
/* fall through */
}
r4 = r3;
cmp r0, 5
bne .Lendif
cmp r1, 3
ble .Lendif
mov r2, r5 // true block
// fall through
.Lendif:
mov r4, r3
If r0 == 5 false
then short circuit branch around the true block
x

## Slide 20: Program Flow – If statements && compound tests - 2
cmp r0, 5 // test 1
bne .Lelse
cmp r1, 3 // test 2
ble .Lelse
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse:
mov r5, r2 //false block
// fall through
.Lendif:
mov r4, r3
if r0 == 5 false
then short circuit branch to the false block
if ((r0 == 5) && (r1 > 3)) {
r2 = r5; // true block
// branch around else
} else {
r5 = r2; False block */
/* fall through */
}
r4 = r3;
x
if r1 > 3 false
then branch to the false block

## Slide 21: Program Flow – If statements || compound tests - 1
if ((r0 == 5) || (r1 > 3)) {
r2 = r5; // true block
/* fall through */
}
r4 = r3;
cmp r0, 5
beq .Lthen
cmp r1, 3
ble .Lendif
// fall through
.Lthen:
mov r2, r5 // true block
/* fall through */
.Lendif:
mov r4, r3
If r0 == 5 true, then branch to true block
if r1 > 3 false then branch around true block
x

## Slide 22: Program Flow – If statements || compound tests - 2
cmp r0, 5
beq .Lthen
cmp r1, 3
ble .Lelse
// fall through
.Lthen:
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse
mov r5, r2 // false block
// fall through
.Lendif:
if ((r0 == 5) || (r1 > 3)) {
r2 = r5; // true block
/* branch around else */
} else {
r5 = r2; // false block
/* fall through */
}
x
If r0 == 5 true, then branch to the true block
if r1 > 3 false then branch to false block

## Slide 23: Program Flow – Pre-test and Post-test Loop Guards
loop guard: code that must evaluate to true before the next iteration of the loop
If the loop guard test(s) evaluate to true, the body of the loop is executed again
pre-test loop guard is at the top of the loop
  If the test evaluates to true, execution falls through to the loop body
  if the test evaluates to false, execution branches around the loop body
post-test loop guard is at the bottom of the loop
  If the test evaluates to true, execution branches to the top of the loop
  If the test evaluates to false, execution falls through the instruction following the loop
x
while (i < 10) {
/* block */
i++;
}
pre-test
loop guard
loop control variable
zero or more iterations
do {
/* block */
i++;
} while (i < 10);
post-test
loop guard
one or more iterations

## Slide 24: Pre-Test Guards - While Loop
.Lwhile:
cmp r1, 10
bge .Lendw
// block
add r1, r1, 1
b .Lwhile
.Lendw:
mov r2, r1
while (r1 < 10) {
/* block */
r1++;
}
r2 = r1;
x
pre-test
loop guard
loop iteration
.Lwhile:
cmp r1, 10
bge .Lendw
cmp r2, r1
beq .Lnext
// block
.Lnext:
add r1, r1, 1
b .Lwhile
.Lendw:
mov r2, r1
while (r1 < 10) {
if (r2 != r1) {
/* block */
}
r1++;
}
r2 = r1;
pre-test
loop guard
loop iteration
inverted test
if stmt guard

## Slide 25: Post-Test Guards – Do While Loop
.Ldo:
// block
add r1, r1, 1
cmp r1, 10
blt .Ldo
mov r2, r1
.Ldo:
cmp r2, r1
beq .Lnext
// block
.Lnext
add r1, r1, 1
cmp r1, 10
blt .Ldo
move r2, r1
do {
/* block */
r1++;
} while (r1 < 10);
r2 = r1;
x
loop iteration
post-test
loop guard
do {
if (r2 != r1) {
/* block */
}
r1++;
} while (r1 < 10);
r2 = r1;
loop iteration
post-test
loop guard
test is not inverted

## Slide 26: Program Flow – Counting (For) Loop
mov r1, 0
.Lfor:
cmp r1, 10
bge .Lendfr
// block code
add r1, r1, 1
b .Lfor
.Lendfr:
A counting loop has three parts:
Pre-loop setup
Pre-test loop guard conditions
Post-loop update
Alternative:
move Pre-test loop guard before the loop
Add post-test loop guard
  converts to do while
  removes an unconditional branch
for (r1 = 0; r1 < 10; r1++) {
/* block */
}
mov r1, 0
cmp r1, 10
bge .Lendfr
.Ldo:
// block code
add r1, r1, 1
cmp r1, 10
blt .Ldo
.Lendfr:
Alternative
Pre loop setup
Pre-test
Loop guard
Post loop update
x
Post loop update
Pre loop setup
Pre-loop setup
Post loop update
Pre-test loop guard
Pre-test loop guard
Post-test loop guard

## Slide 27: Nested loops
Nest loop blocks as you would in C or Java
Do not branch into the middle of a loop, this is hard to read and is prone to errors
for (r3 = 0; r3 < 10; r3++) {
r0 = 0;
do {
r0 = r0 + r1++;
} while (r1 < 10);
// fall through
r2 = r2 + r1;
}
r5 = r0;
x
mov r3, 0
.Lfor:
cmp r3, 10 // loop guard
bge .Lendfor
mov r0, 0
.Ldo:
add r0, r0, r1
add r1, r1, 1
cmp r1, 10 // loop guard
blt .Ldo
// fall through
add r2, r2, r1
add r3, r3, 1 // loop iteration
b .Lfor
.Lendfor:
mov r5, r0

## Slide 28: Keep loops Properly Nested: Do not branch into the middle of a loop
It is hard to understand and debug loops when you branch into the middle of a loop
Keep loops proper nested
Do not do the following:
.Lloop1:
add r1, r1, 1
.Lloop2:
add r2, r2, 1
add r2, r1, r3
cmp r1, 10
blt .Lloop1
beq .Lend1
add r3, r3, 1
cmp r2, 20
ble .Lloop2
.Lend1:
x
Bad practice: branch into loop body

## Slide 29: Creating Segments, Definitions In Assembly Source
The following assembler directives indicate the start of a memory segment specification
  Remains in effect until the next segment directive is seen
Define a literal, static variable or global variable in a segment
  Label: this is the variables name
  Size_Directive tells the assembler how much space to allocate for that variable
Each optional expression specifies the contents of one memory location of .size_directive
  expression can be in decimal, hex (0x…), octal (0…), binary (0b…), ASCII (' '), string " "
Label: .size_directive expression, … expression
x
.bss
    // start uninitialized static segment variables definitions
  // does not consume any space in the executable file
.data
// start initialized static segment variables definitions
.section .rodata
// start read-only data segment variables definitions
.text
// start read-only text segment (code)

## Slide 30: Assembly Source File Template
assembly programs end in .S
  That is a capital .S
  example: test.S
Always use gcc to assemble
  _start() and C runtime
File has a complete program
  gcc file.S
File has a partial program
  gcc –c file.S
Link files together
  gcc file.o cprog.o
// File Header
.arch armv6 // armv6 architecture instructions
.arm // arm 32-bit instruction set
.fpu vfp // floating point co-processor
.syntax unified // modern syntax
// BSS Segment (only when you have initialized globals)
.bss
// Data Segment (only when you have uninitialized globals)
.data
// Read-Only Data (only when you have literals)
.section .rodata
// Text Segment – your code
.text
// Function Header .type main, %function // define main to be a function
.global main // export function name
main:
// function prologue // stack frame setup
// your code for this function here
// function epilogue //stack frame teardown
// function footer
.size main, (. – main)
// File Footer
.section .note.GNU-stack,"",%progbits // stack/data non-exec
.end
x

## Slide 31: Memory Segment Data Alignment
Word is the number of bytes necessary to store an address (32-bits on Pi-cluster) – hardware defined
The address of any sized unit of memory is always the address of the first byte
Hardware often requires Variables to be "aligned" to specific starting addresses based on type
char (1 byte)
  can start at any address
short (2 bytes) can start only at addresses ending
  b..00 or b..10 (.align 1) // last bit must be 0
int (4 bytes) can start only at address ending in
  0b..00 (.align 2) // last two bits must be 0
32-bit
units
(4 bytes)
Start
At
??
Start
at
??
Start
at
??
Start
at
??
b..00
b..00
b..00
b..00
8-bit
units
(1 Byte)
b..00100
b..00101
b..00110
b..00111
b..01000
b..01001
b..01010
b..01011
b..01100
b..01101
b..01110
b..01111
b..10000
b..10001
b..10010
b..10011
Addr.
(binary)
x
16-bit
units
(2 Bytes)
Start
at
??
Start
at
??
Start
at
??
Start
at
??
Start
at
??
Start
at
??
Start
at
??
Start
at
??
b.00
b..00
b..00
b..00
b..10
b..10
b..10
b..10

## Slide 32: Byte Ordering of Numbers In Memory: Endianness
Two different ways to place multi-byte integers in a byte addressable memory
Big-endian: Most Significant Byte (“big end”) starts at the lowest (starting) address
Little-endian: Least Significant Byte (“little end”) starts at the lowest (starting) address
Example: 32-bit integer with 4-byte data
a1
b2
c3
d4
0x100
0x101
0x102
0x103
01
23
a1
b2
c3
d4
01
23
d4
c3
b2
a1
Big-Endian
Little-Endian
MSB
Most significant byte
LSB
Least significant byte
x
0x100
0x101
0x102
0x103

## Slide 33: Byte Ordering Example
Decimal: 12345
Binary: 0011 0000 0011 1001
Hex: 3 0 3 9
int x = 12345;
// or x = 0x00003039; // show all 32 bits
39
30
00
00
IA32, ARM32 (little-endian)
30
39
00
00
(big-endian)
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
x

## Slide 34: Byte Addressable Memory Shown as 32-bit words
Observation
32-bit aligned addresses
rightmost 2 bits of the address are always 0
0x12345680
0x12345682
0x12345681
0x12345683
0x00
0x01
0x02
0x03
1 32-bit
(4 byte) word
0x12345684
0x12345686
0x12345687
0x12345685
0x04
0x05
0x06
0x07
1 byte Memory Content
One byte per row
Byte
Memory
Address
1 32-bit
(4 byte) word
Word Aligned address
Word Aligned address
x
0x04
0x05
0x06
0x07
0x00
0x01
0x02
0x03
LSByte
MSByte
0x12345680
0x12345681
0x12345682
0x12345683
Contents of Memory
One 32-bit (4 byte) word per row
0x12345680
0x12345684
Byte address
0x12345688
0x1234568C
0x12345690
0x12345694
Word
Memory
Address

## Slide 35: Defining Static Variables: Allocation and Initialization
Variable SIZE | Directive | .align | C static variable Definition | Assembler static variable Definition
8-bit char (1 byte) | .byte |  | char chx = 'A' char string[] = {’A’,’B’,’C’, 0}; | chx: .byte ’A’ string: .byte ’A’,’B’,0x42,0
16-bit int (2 bytes) | .hword .short | 1 | short length = 0x55aa; | length: .hword 0x55aa
32-bit int (4 bytes) | .word .long | 2 | int dist = 5; int *distptr = &dist; int array[] = {12,~0x1,0xCD,-1}; | dist: .word 5 distptr: .word dist array: .word 12,~0x1,0xCD,-3
strings '\0' term | .string |  | char class[] = "cse30"; | class: .string "cse30"
x
int num; // 4 bytes
int *ptr = &num; // 4 bytes
char *lit = "456"; // 4bytes, "456" string literal
char msg[] = "123"; // 4 bytes – array
.bss
num: .word 0
.data
ptr: .word num
lit: .word .Lmsg
msg: .string "123"
.section .rodata
.Lmsg: .string "456"
initializes a pointer

## Slide 36: Defining Static Array Variables
.space size, fill
Allocates size bytes, each of which contain the value fill
Both size and fill are absolute expressions
If the comma and fill are omitted, fill is assumed to be zero
.bss section: Must be used without a specified fill
In C: int int_buf[100];
int array[] = {1, 2, 3, 4, 5};
char buffer[100];
.bss
int_buf: .space 400 // convert 100 to 400 bytes
char_buf: .space 100
.data
array: .word 1, 2, 3, 4, 5
one_buf: .space 100, 1 // 100 bytes each byte filled with 1
x
Label: .size_directive expression, … expression

## Slide 37: Static Variable Alignment: Using .align
Accessing address aligned memory based on data type has the best performance
1
2 bytes
4 bytes
integer
short
char
x
SIZE | Directive | Address ends in | Align Directive
8-bit char -1 byte | .byte | 0b..0 or 0b..1 | 
16-bit int -2 bytes | .hword .short | 0b..0 | .align 1
32-bit int -4 bytes | .word .long | 0b..00 | .align 2
4
bytes
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0x0C
0x08
0x04
0x00
1
Byte
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x0C
0x0D
0x0E
0x0F
Addr.
(hex)
2
Bytes
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0x0C
0x08
0x00
0x04
0x0E
0x0A
0x06
0x02
.align n before variable definition to specify memory alignment requirements
Tells the assembler the next line that allocates memory must start at the next higher memory address where the lower n address bits are zero
At the first use of any Segment directive, alignment starts at an 8-byte aligned address (for doubles)
Easy approach: Allocate from largest size variables to smallest size variables

## Slide 38: Data Segment Variable Alignment
Output on the right side is generated by:
%gcc -c -Wa,-ahlns al1.S
.data
ch: .byte 'A','B','C','D','E'
str: .string "HIT"
ary: .hword 0, 1
a: .byte 'A'
b: .byte 'B'
xx: .word 2
% gcc -c -Wa,-ahlns al1.S
1 .data
2 0000 41424344 ch: .byte 'A','B','C','D','E'
2 45
3 0005 48495400 str: .string "HIT"
4 0009 00000100 ary: .hword 0, 1
5 000d 41 a: .byte 'A'
6 000e 42 b: .byte 'B'
8 000f 02000000 xx: .word 2
.data
xx: .word 2
ch: .byte 'A','B','C','D','E'
.align 2
str: .string "HI"
.align 1
ary: .hword 0, 1
a: .byte 'A'
b: .byte 'B'
gcc -c -Wa,-ahlns al1.S
1 .data
2 0000 02000000 xx: .word 2
3 0004 41424344 ch: .byte 'A','B','C','D','E'
3 45
4 0009 000000 .align 2
5 000c 484900 str: .string "HI"
6 000f 00 .align 1
7 0010 00000100 ary: .hword 0, 1
8 0014 41 a: .byte 'A'
9 0015 42 b: .byte 'B'
address
contents
x

## Slide 39: Load/Store: Register Base Addressing
32-bit memory
register r0
register r1 (address)
ldr r0, [r1]
Copies a 32-bit word
from the memory location
whose address is contained
in r1 (r1 is a pointer)
into register r0
r1 is being used as a pointer to a location in memory
ldr requires the use of a pointer operand
str r0, [r1]
Copies all 32 bits of the value held in register r0 to the 32-bit memory location contained in register r1 (r1 pointer)
32-bit memory
register r0
register r1 (address)
r1 is being used as a pointer to a location in memory
str requires the use of a pointer operand
x

## Slide 40: LDR/STR – Base Register + Immediate Offset Addressing
ldr/str Rd, [Rn, +- imm12] // base register pointer + offset imm12 in bytes
-4095 <= imm12 <= 4095 (bytes)
ldr/str Rd, [Rn] // base register pointer + 0 offset (imm12 is 0)
Register Base Addressing:
  Pointer Address: Rn; source/destination data: Rd
  Unsigned pointer address in stored in the base register
Register Base + immediate offset Addressing:
  Pointer Address = register content + immediate offset
  Unsigned offset integer immediate value (bytes) is added or subtracted (U bit above says to add or subtract) from the pointer address in the base register
unsigned immediate offset
Rd – source/dest register
ldr/str
Rd
imm12
Rn
Rn – base register contains address (pointer)
U
+/- offset
x

## Slide 41: ldr/str Register Base and Register + Immediate Offset Addressing
Syntax | Address | Examples
ldr/str Rd, [Rn +/- constant] constant is in bytes | Rn + or – constant same | ldr r0, [r5,100] str r1, [r5, 0] str r1, [r5]
ldr/str
Rd
imm12
Rn
U
+ -
0 subtract
1 add
Memory Address
Instruction
Source for str
Destination for ldr
x

## Slide 42: Example Base Register Addressing Load – Modify – Store
x = x + 1;
ldr r0, [r1] // r0 = *r1 (read x)
add r0, r0, 1 // r0 = r0 + 1 (x++)
str r0, [r1] // *r1 = r0 write x
Memory assigned to x
register r0
register r1 (address)
+ 1
0b..0000100
Notice: word aligned!
(last two bits are 0's)
..00000000
..00000001
n-bit Memory
Address
binary
..00000010
..00000011
..00000100
..00000101
..00000110
..00000111
01010101
10101010
01010101
10101010
01010101
10101010
01010101
10101010
1 byte
contents
X starting address
x
x = x + 1
Where x is in memory
r1 is a pointer

## Slide 43: How to get a memory pointer into a register?
x
0xFF…FF
0x00…00
32-bit Address space
OS kernel [protected]
Stack
Heap
Static Data (+BSS)
Shared Libraries
Read Only Data
Read Only Text Segment
Assembler creates a table of pointers in the text segment called the literal table
For each variable in one of the data segments you reference in a special form of the ldr instruction (next slide), the assembler makes an entry for that variable whose contents is the 32-bit Label address
.data
x: .word 200
.bss
y: .space 4ç
.text
// your code
// last line of your code
// below is created by the assembler
.word y // contents: 32-bit address of y
.word x // contents: 32-bit address of x

## Slide 44: Loading and using pointers in registers
.text
// function header
main:
// load the address, then contents
// using r2
ldr r2, =x // int *r2 = &x
ldr r2, [r2] // r2 = *r2;
// &x was only needed once above
// Note: r2 was a pointer then an int
// no "type" checking in assembly!
// store the contents of r2
ldr r1, =y // int *r1 = &y
str r2, [r1] // *r1 = r2
…
x
.data
x: .word 200
two step to load a memory variable
  load the pointer to the memory
  read (load) from *pointer
Tell the assembler to create and USE a literal table to obtain the address (Lvalue) of a label into a register:
  ldr/str Rd, =Label // Rd = address
Example to the right: y = x;
.bss
y: .space 4
two steps store to a memory variable
  load the pointer to the memory
  write (store) to *pointer

## Slide 45: How to use the literal table to get a big constant into a register
In data processing instructions, the field imm8 + rotate 4 bits is too small to store many numbers outside of the range of -256 to 255, how do you get larger immediate values into a register?
Answer: use ldr instruction with the constant as an operand: =constant
Assembler creates a literal table entry with the constant
mov r0, 1023
xxx.s:24: Error: invalid constant (3ff) after fixup
ldr r0, =1023
fails
replacement
mov
Rd
rot4
imm8
x
ldr Rd, =constant // =constant
ldr r1, =0x2468abcd // loads the constant 0x246abcd into r1

## Slide 46: Loading and Storing: Variations List
Load and store have variations that move 8-bits, 16-bits and 32-bits
Load into a register with less than 32-bits will set the upper bits not filled from memory differently depending on which variation of the load instruction is used
Store will only select the lower 8-bit, lower 16-bits or all 32-bits of the register to copy to memory
Instruction | Meaning | Sign Extension | Memory Address Requirement
ldrsb | load signed byte | sign extension | none (any byte)
ldrb | load unsigned byte | zero fill (extension) | none (any byte)
ldrsh | load signed halfword | sign extension | halfword (2-byte aligned)
ldrh | load unsigned halfword | zero fill (extension) | halfword (2-byte aligned)
ldr | load word | --- | word (4-byte aligned)
strb | store low byte (bits 0-7) | --- | none (any byte)
strh | store halfword (bits 0-15) | --- | halfword (2-byte aligned)
str | store word (bits 0-31) | --- | word (4-byte aligned)
x

## Slide 47: Loading 32-bit Registers From Memory Variables < 32-Bits Wide
Unsigned
Zero-Extend: Add leading 0’s
example ldrb
Instructions that zero-extend:
ldrb, ldrh
0b 1110 0001
0x00
0x00
0x00
0xe1
memory
r0
Overwrite the upper three bytes with 0
Signed (2’s complement)
Sign-Extend: Replicate sign bit
example ldrsb
Instructions that sign-extend:
ldrsb, ldrsh
0xff
0xff
0xff
0xe1
memory
r0
Overwrite the upper three bytes with 1
0b 1110 0001
x

## Slide 48: Load a Byte, Half-word, Word
0x00
0x00
0x00
0x00
0
31
Load a byte
ldrb r1, [r0]
r1
0
31
r1
Load a word
ldr r1, [r0]
observe the zero fill
x
0x0a
0x0b
0x0c
0x0d
0xe1
0xe3
0x65
0x87
0x00
0x00
0x00
0x10
r0
0001 0000
0001 0001
0001 0010
0001 0011
0001 0000
Byte Address Byte
.align 2 word aligned
0x87
0x65
0xe3
0xe1
0x00
0x00
0
31
r1
Load a halfword
ldrh r1, [r0]
0x00
0x00
0xe3
0xe1
observe the zero fill
0xe1

## Slide 49: Signed Load a Byte, Half-word, Word
0x00
0x00
0x00
0x00
0
31
Load a byte
ldrsb r1, [r0]
r1
0
31
r1
Load a word (no change)
ldr r1, [r0]
observe the sign extend
x
0x0a
0x0b
0x0c
0x0d
1110 0001
1110 0011
0x65
0x87
0x00
0x00
0x00
0x10
r0
0001 0000
0001 0001
0001 0010
0001 0011
0001 0000
Byte Address Byte
.align 2 word aligned
0x87
0x65
1110 0011
1110 0001
0x00
0x00
0
31
r1
Load a halfword
ldrsh r1, [r0]
0x00
0x00
observe the sign extend
1110 0011
1110 0001
0xff
0xff
1110 0001
0xff
0xff
0xff

## Slide 50: Signed Load a Byte, Half-word, Word
0x00
0x00
0x00
0x00
0
31
Load a byte
ldrsb r1, [r0]
r1
0
31
r1
Load a word (no change)
ldr r1, [r0]
observe the sign extend
x
0x0a
0x0b
0x0c
0x0d
0110 0001
0110 0011
0x65
0x87
0x00
0x00
0x00
0x10
r0
0001 0000
0001 0001
0001 0010
0001 0011
0001 0000
Byte Address Byte
.align 2 word aligned
0x87
0x65
0110 0011
1110 0001
0x00
0x00
0
31
r1
Load a halfword
ldrsh r1, [r0]
0x00
0x00
0110 0011
1110 0001
observe the sign extend
0110 0001

## Slide 51: Storing 32-bit Registers To Memory 8-bit, 16-bit, 32-bit
strb
0x00
0x00
0xe2
0xe1
memory
r0
0x??
0x??
0x??
0xe1
Not Changed
strh
0x00
0x00
0xe2
0xe1
memory
r0
0x??
0x??
0xe2
0xe1
Not Changed
x
str
0x04
0x03
0xe2
0xe1
memory
r0
0x04
0x03
0xe2
0xe1

## Slide 52: Store a Byte, Half-word, Word
0x20
0x00
0x00
0x00
initial value in r0
0
31
Store a byte
strb r1, [r0]
r1
0x87
0x65
0xe3
0xe1
0x11
0x22
0x33
0x20000000
0x20000001
0x20000002
0x20000003
observe other bytes NOT altered
Byte Address Byte
x
0x00
0xe1
0
31
r1
Store a halfword
strh r1, [r0]
0x87
0x65
0xe3
0xe1
0x22
0x33
0x20000000
0x20000001
0x20000002
0x20000003
Byte Address Byte
0x11
0x00
0xe1
0xe3
0
31
0x87
0x65
0xe3
0xe1
r1
Store a word
str r1, [r0]
0x20000000
0x20000001
0x20000002
0x20000003
Byte Address Byte
0x11
0x22
0x33
0x00
0xe1
0xe3
0x65
0x87

## Slide 53: ldr/str Base Register + Register Offset Addressing
Syntax | Address | Examples
ldr/str Rd, [Rn +/- Rm ] | Rn + or – Rm | ldr r0, [r5, r4] str r1, [r5, r4]
ldr/str
Rd
Rn
U
+ -
0 subtract
1 add
Memory Address
Instruction
Source for str
Destination for ldr
Rm
x
Pointer Address = Base Register + Register Offset
  Unsigned offset integer in a register (bytes) is either added/subtracted from the pointer address in the base register

## Slide 54: Reference: Addressing Mode Summary for use in CSE30
index Type | Example | Description
Pre-index immediate | ldr r1, [r0] | r1  memory[r0] r0 is unchanged
Pre-index immediate | ldr r1, [r0, 4] | r1  memory[r0 + 4] r0 is unchanged
Pre-index immediate | str r1, [r0] | memory[r0]  r1 r0 is unchanged
Pre-index immediate | str r1, [r0, 4] | memory[r0 + 4]  r1 r0 is unchanged
Pre-index register | ldr r1, [r0, +-r2] | r1  memory[r0 +- r2] r0 is unchanged
Pre-index register | str r1, [r0, +-r2] | memory[r0 +- r2]  r1 r0 is unchanged
x

## Slide 55: Array addressing with ldr/str
Array element | Base addressing | Immediate offset | register offset
ch[0] | ldrb r2, [r0] | ldrb r2, [r0, 0] | mov r4, 0 ldrb r2, [r0, r4]
ch[1] | add r0, r0, 1 ldrb r2, [r0] | ldrb r2, [r0, 1] | mov r4, 1 ldrb r2, [r0, r4]
ch[2] | add r0, r0, 2 ldrb r2, [r0] | ldrb r2, [r0, 2] | mov r4, 2 ldrb r2, [r0, r4]
x[0] | ldr r2, [r1] | ldr r2, [r1, 0] | mov r4, 0 ldr r2, [r1, r4]
x[1] | add r1, r1, 4 ldrb r2, [r1] | ldrb r2, [r1, 4] | mov r4, 4 ldrb r2, [r1, r4]
x[2] | add r1, r1, 8 ldrb r2, [r0] | ldrb r2, [r1, 8] | mov r4, 8 ldrb r2, [r1, r4]
0x41
0x42
0x43
0x44
0x45
0x00
0x00
0x00
0000
0001
0010
0011
0100
0101
0110
0x00
0111
1000
0x00
0x00
0x01
1001
1010
1011
.data
ch: .byte 0x41, 0x42, 0x43, 0x44
x: .word 0x00000045
.word 0x01000000
.word 0x01020304
.text
ldr r0, =ch
ldr r1, =x
0x00
1100
0x00
0x00
0x01
1101
1110
1111
0000
r0
0100
r1
table rows are
independent instructions

## Slide 56: ldr/str practice - 1
r1 contains the Address of X (defined as int X) in memory; r1 points at X
r2 contains the Address of Y (defined as int *Y) in memory; r2 points at Y
write Y = &X;
str r1, [r2] // y  &x
address of y
0x0100c
r1
r2
X contents
x
??
Y contents
??
0x01008
0x0100c // this is y
0x01004 // this is x
0x01000
address of x
0x01004
??
0x01010
0x01004

## Slide 57: ldr/str practice - 2
r1 contains the Address of X (defined as int *X) in memory r1 points at X
r2 contains the Address of Y (defined as int Y) in memory; r2 points at Y
write Y = *X;
ldr r3, [r1] // r3  x (read 1)
ldr r0, [r3] // r0  *x (read 2)
str r0, [r2] // y  *x
x
address of y
0x0100c
r1
r2
X = 0x01010
??
Y contents
??
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
55
0x01010
55
?
r3
0x01010
r0
?
55

## Slide 58: ldr/str practice - 3
r1 contains Address of X (defined as int *X) in memory; r1 points at X
r2 contains Address of Y (defined as int Y[2]) in memory; r2 points at &(Y[0])
write *X = Y[1];
ldr r0, [r2, 4] // r0  y[1]
ldr r3, [r1] // r3  x
str r0, [r3] // *x  y[1]
x
address of y
0x0100c
r1
r2
X = 0x01000
??
Y[0] contents
??
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
Y[1] contents
0x01010
Y[1] contents
?
r3
r0
?
0x01000
Y[1] contents
+4

## Slide 59: ldr/str practice - 4
r1 contains Address of X (defined as int X[2]) in memory; r1 points at &(x[0])
r2 contains Address of Y (defined as int Y) in memory; r2 points at Y
r3 contains a 4
write Y = X[1];
ldr r0, [r1, r3] // r0  x[1]
str r0, [r2] // y  x[1]
x
address of y
0x0100c
r1
r2
??
x[0] contents
Y contents
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
x[1] contents
0x01010
x[1] contents
4
r3
r0
?
x[1] contents
+4

## Slide 60: Label (Address) Math
You can have the assembler calculate some useful values for you
One common use is calculating the distance in bytes between two labels
The dot (.) refers to the address on the current line (the next byte after a previous space allocation)
.section .rodata
.Lst: .string "The value of x is %d\n"
.equ STSZ, (. – .Lst) // number of bytes in .Lst includes \0
.equ STLEN, STSZ – 1 // string length of .Lst
x

## Slide 61: Example: Base Register Addressing with Arrays
#include <stdio.h>
#include <stdlib.h>
char msg[] ="Hello CSE30! We Are CountinG UpPER cASe letters!";
int
main(void)
{
int cnt = 0;
char *endpt = msg + sizeof(msg)/sizeof(*msg);
char *ptr = msg;
while(ptr < endpt) {
if ((*ptr >= 'A') && (*ptr <= 'Z'))
cnt++;
ptr++;
}
return EXIT_SUCCESS;
}
x
0 | 1 | 2 | 3 | 4 | 5 | 
'H' | 'e' | 'l' | 'l' | 'o' | '\0' | 
ptr
endptr

## Slide 62: Example: Base Register Addressing with Arrays
Iterates a pointer (r2) through the array
r3 contains the address +1 past the end of the string
MSGSZ is the size of the array (including the '\0) if you wanted to excluded the '\0', then subtract 1 from MSGSZ
Use ldrb as msg is an array of chars
.data // segment
msg:.string "Hello CSE30! We Are CountinG UpPER cASe letters!"
.equ MSGSZ, (. - msg) // number of bytes in msg
.section .rodata
mov r1, 0 // initialize cnt
ldr r2, =msg // ptr point to &msg
add r3, r2, MSGSZ // endpt points after end
.Lwhile:
cmp r2, r3 // at end of buffer yet?
bge .Lexit
ldrb r0, [r2] // get next char (base addressing)
cmp r0, 'A' // is it less than an 'A" ?
blt .Lendif // if so, not CAP (short circuit)
cmp r0, 'Z' // is it greater than a 'Z"?
bgt .Lendif // if so, not CAP
add r1, r1, 1 // it is a CAP, so increment cnt
.Lendif:
add r2, r2, 1 // move to next char
b .Lwhile //go to loop guard at top of while
.Lexit:
x
'H' | 'e' | 'l' | 'l' | 'o' | '\0' | 
r2
r3
loop guard

## Slide 63: Example: Base Register + Offset Register
mov r1, 0 // initialize cnt
ldr r2, =msg // ptr point to &msg
add r3, r2, MSGSZ // endpt points after end
.Lwhile:
cmp r2, r3 // at end of buffer yet?
bge .Lexit
ldrb r0, [r2] // get next char
cmp r0, 'A' // is it less than an 'A" ?
blt .Lendif // if so, not CAP
cmp r0, 'Z' // is it greater than a 'Z"?
bgt .Lendif // if so, not CAP
add r1, r1, 1 // is a CAP increment
.Lendif:
add r2, r2, 1 // move to next char
b .Lwhile //go to loop guard while top
.Lexit:
x
Using Base register pointer with an end pointer
mov r1, 0
ldr r2, =msg
mov r3, 0 // index reg
.Lwhile:
cmp r3, MSGSZ // are we done?
bge .Lexit
ldrb r0, [r2, r3]
cmp r0, 'A'
blt .Lendif
cmp r0, 'Z'
bgt .Lendif
add r1, r1, 1
.Lendif:
add r3, r3, 1 // index++
b .Lwhile
.Lexit:
Using Base register pointer + Offset register

## Slide 64: Example: Base Register + Register Offset Two Buffers
Make sure to index by bytes and increment the index register by sizeof(int) = 4
#include <stdio.h>
#include <stdlib.h>
#define SZ 6
int src[SZ] = {1, 3, 5, 7, 9, 11};
int dest[SZ];
int
main(void)
{
for (int i = 0; i < SZ; i++)
dest[i] = src[i];
return EXIT_SUCCESS;
}
x
.data // segment
src:.word 1, 3, 5, 7, 9, 11
.equ SZ, (. - src) // bytes msg
dest:.space SZ
.equ INT_STEP, 4
…
ldr r0, =src // ptr to src
ldr r1, =dest // ptr to dest
mov r2, 0
.Lfor:
cmp r2, SZ // in bytes!
bge .Lexit
ldr r3, [r0, r2]
str r3, [r1, r2]
add r2, r2, INT_STEP
b .Lfor
.Lexit:
one increment covers both arrays

## Slide 65: What is a Bitwise Operation?
Bitwise operators are applied to each of the corresponding bit positions in each variable
Each bit position of the result depends only on bits in the same bit position within the operands
a = | a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
 | <op> | <op> | <op> | <op> | <op> | <op> | <op> | <op>
b = | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
result = | c7 | c6 | c5 | c4 | c3 | c2 | c1 | c0
x

## Slide 66: Bitwise Not (vs Boolean Not)
a | ~a
0 | 1
1 | 0
in C
int output = ~a;
x
Boolean operators act on the entire value not the individual bits
Meaning | Operator | Operator | Meaning
Boolean NOT | !b | ~b | Bitwise NOT
 | Bitwise Not
number | 0101 1010 0101 1010 1111 0000 1001 0110
~number | 1010 0101 1010 0101 0000 1111 0110 1001
Type | Operation | result
bitwise | ~0x01 | 1111 1111 1111 1111 1111 1111 1111 1110
Boolean | !0x01 | 0000 0000 0000 0000 0000 0000 0000 0000
~ 1100
----
0011
Bitwise NOT

## Slide 67: First Look: Copying Values To Registers – MVN (not)
A bitwise NOT operation
mvn r0, r1
// Copies all 32 bits
// of the value held
// in register r1 into
// the register r0
// then does a bitwise NOT
register r0
register r1
mvn r0, 12
// Expands an imm8 value 0x0c
// stored in the instruction
// into a register then does
// a bitwise NOT
0xffff fff3
0x0c
x
~ 1100
----
0011
Bitwise NOT
register r0
0xfffffff3
0x 0c
imm8 expansion
0x0000000c
bitwise not

## Slide 68: mvn – Copies NOT (~) of Register content between registers
constant (immediate value)
destination register
mvn
Rd
source register
mvn
Rd
Rm
destination register
bitwise NOT operation. Immediate (constant) version copies to 32-bit register, then does a bitwise NOT
mvn r1, 4 // x = ~4
mvn r1, r5 // x = ~y in C
mvn r1, 0 // x = -1
imm8 | extended imm8 | inverted imm8 | signed base 10
0x00 | 0x00 00 00 00 | 0xff ff ff ff | -1
0xff | 0x00 00 00 ff | 0xff ff ff 00 | -256
0xfffffffb
r1
0x4
invert the bits
0x00000004
copy into 32 bits zero extend
0xaaaaaaaa
0x55555555
r5
r1
rot4
imm8
~ 1100
----
0011
Bitwise NOT
x
mvn Rd, constant // Rd = constant
mvn Rd, Rm // Rd = Rm
0x0
0x11111111
r1

## Slide 69: Bitwise (Bit to Bit) Operators in C
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
output = a | b;
| with 1 to set a bit to 1
| with 0 to let a bit through
a | ~a
0 | 1
1 | 0
output = ~a;
a | b | a ^ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
output = a ^ b; //EOR
^ with 1 will flip the bit
^ with 0 to let a bit through
a | b | a & b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
output = a & b;
& with 1 to let a bit through
& with 0 to set a bit to 0
0110
& 1100
----
0100
Bitwise
AND
0110
| 1100
----
1110
Bitwise
OR
0110
^ 1100
----
1010
Bitwise
EOR
~ 1100
----
0011
Bitwise
NOT
x

## Slide 70: Bitwise Instructions
<op> Rd, Rn, constant // Rd = Rn <op> constant
<op> Rd, constant // Rd = Rd <op> constant
<op> Rd, Rn, Rm // Rd = Rn <op> Rm
Operand 2 constant
destination
<op>
Rd
rot4
imm8
Rn
operand 1
Operand 2
destination
<op>
Rd
Rn
operand 1
Rm
Bytes: 0 <= imm8 <= 255 + values from "rotating" rot 4 bits
Bitwise <op> description | <op> Syntax | Operation
Bitwise AND | and Rd, Rn, Op2 | Rd  Rn & Op2
Bit Clear each bit in Op2 that is a 1, the same bit in Rd, is cleared | bic Rd, Rn, Op2 | Rd  Rn & ~Op2
Bitwise OR | orr Rd, Rn, Op2 | Rd  Rn ¦ Op2
Exclusive OR | eor Rd, Rn, Op2 | Rd  Rn ^ Op2
x

## Slide 71: Bit Masks: Masking - 1
Bit masks access/modify specific bits in memory
Masking act of applying a mask to a value
or: 0 passes bit unchanged, 1 sets bit to 1
eor: 0 passes bit unchanged, 1 inverts the bit
bic: 0 passes bit unchanged, 1 clears it
and: 0 clears the bit, 1 passes bit unchanged
mask force lower 16 bits to 1 "mask on" operation
orr r1, r2, r3
DATA: r2 0xab ab ab 77
MASK: r3 0x00 00 ff ff lower half to 1
RSLT: r1 0xab ab ff ff
x
mask to invert the lower 8-bits "bit toggle" operation
eor r1, r2, r3
DATA: r2 0xab ab ab 77
MASK: r3 0x00 00 00 ff flip LSB bits
RSLT: r1 0xab ab ab 88
MASK: r3 0x00 00 00 ff apply a 2nd time
RSLT: r1 0xab ab ab 77 original value!

## Slide 72: Bit Masks: Masking - 2
x
clear bit 5 to a 0 without changing the other bits
bic r1, r2, r3
DATA: r2 0xab ab ab 77
MASK: r3 0x00 00 00 20 clear bit 5 (0010)
RSLT: r1 0xab ab ab 57
mask to extract top 8 bits of r2 into r1
and r1, r2, r3
DATA: r2 0xab ab ab 77
MASK: r3 0xff 00 00 00
RSLT: r1 0xab 00 00 00
mask to force lower 8 bits to 0 "mask off" operation
and r1, r2, r3
DATA: r2 0xab ab ab 77
MASK: r3 0xff ff ff 00 clear LSB
RSLT: r1 0xab ab ab 00
mask to query the status of a bit "bit status" operation
and r1, r2, r3
DATA: r2 0xab ab ab 77
MASK: r3 0x00 00 00 01 is bit 0 set?
RSLT: r1 0x00 00 00 01 (0 if not set)

## Slide 73: Bit Masks: Masking - 3
remainder (mod): num % d where n ≥ 0 and d = 2k
mask = 2k -1 so for mod 16, mask = 16 -1 = 15
and r1, r2, r3
DATA: r2 0xab ab ab 77
MASK: r3 0x00 00 00 0f (mod 16)
RSLT: r1 0xab 00 00 07 (if 0: divisible by)
remainder (mod): num % d where n ≥ 0 and d = 2k
mask = 2k - 1 so for mod 2, mask = 2 -1 = 1
and r1, r2, r3
DATA: r2 0xab ab ab 77
MASK: r3 0x00 00 00 01 (mod 2 even or odd)
RSLT: r1 0x00 00 00 01 (odd)
x
mask to get 1's complement operation
(like mvn)
eor r1, r2, r3
DATA: r2 0xab ab ab 77
MASK: r3 0xff ff ff ff
RSLT: r1 0x54 54 54 88

## Slide 74: Shift and Rotate Instructions
Instruction | Syntax | Operation | Notes | Diagram
Logical Shift Left | LSL Rd, Rm, const5 LSL Rd, Rm, Rs | Rd  Rm << const5 Rd  Rm << Rs | Zero fills shift: 0 - 31 | 
Logical Shift Right | LSR Rd, Rm, const5 LSR Rd, Rm, Rs | Rd  Rm >> const5 Rd  Rm >> Rs | Zero fills shift: 1 - 32 | 
Arithmetic Shift Right | ASR Rd, Rm, const5 ASR Rd, Rm, Rs | Rd  Rm >> const5 Rd  Rm >> Rs | Sign extends shift: 1 - 32 | 
Rotate Right | ROR Rd, Rm, const5 ROR Rd, Rm, Rs | Rd  Rm ror const5 Rd  Rm ror Rs | right rotate rot: 0 - 31 | 
operand 2 constant
destination
<inst>
Rd
const5
Rm
operand 1
Number of bit to shift or rotate: const5
operand 2
destination
<inst>
Rd
Rm
operand 1
Rs
Number of bit to shift or rotate: Rs
x

## Slide 75: Shift & Rotate Operations
asr r2, r0, 8
r0 0xab ab ab 77
r2 0xff ab ab ab (see the sign extend)
asr r2, r0, 31
r0 0x7b ab ab 77
r2 0x00 00 00 00
Test for sign
0 if r0 positive
asr r2, r0, 31
r0 0xab ab ab 77
r2 0xff ff ff ff
Test for sign
-1 if r0 negative
x

## Slide 76: Shift & Rotate Operations
lsr r2, r0, 8
r0 0xab ab ab 77
r2 0x00 ab ab ab
lsl r2, r0, 8
r0 0xab ab ab 77
r2 0xab ab 77 00
ror r2, r0, 8
r0 0xab ab ab 77
r2 0x77 ab ab ab
x

## Slide 77: Extracting Unsigned Bitfields
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
next shift left = 8
r0
byte 0
byte 1
byte 3
byte 2
Move byte 2 in r0 to byte 0 in r1
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
lsr r1, r1, 24
unsigned zero-extension (all 0’s)
Extracted bit-field
r1
byte 0
byte 1
byte 3
byte 2
lsl r1, r0, 8
Next shift right = 24
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far left
pushed bits to far right
Hint: Useful for PA8

## Slide 78: Extracting Signed Bitfields
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
next shift left = 8
r0
byte 0
byte 1
byte 3
byte 2
Move byte 2 in r0 to byte 0 in r1
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
lsl r1, r0, 8
next shift right = 24
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far left
asr r1, r1, 24
signed extend (all 1’s)
Extracted
bit-field
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far right

## Slide 79: Inserting Bitfields – Inserting Source Field into Destination Field
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
r1
r0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Task: Insert source into destination
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
results in
orr r1, r1, r2
r1
r2
Approach
(1) isolate source field
(2) clear destination field
(3) Bitwise or together
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 80: Creating a Mask
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Create a 1 mask
ldr r3, =0x00ffff0000
Create a 0 mask
ldr r3, =0xff0000ffff
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 81: Inserting Bitfields – Isolating the Source Field
r2
r0
x
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
isolate source field
lsl r2, r0, 24
lsr r2, r2, 8
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r0
r2

## Slide 82: Inserting Bitfields – Clearing the Destination Field
x
clear the destination field
bic r1, r1, r3
r1
r3
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
r1
r1
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
create a 1 mask

## Slide 83: Inserting Bitfields – Combining Isolated Source and Cleared Destination
x
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
inserted field
orr r1, r1, r0
r1
r2
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
isolated source
r1
r1
field cleared in destination

## Slide 84: Isolating Bitfields
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
next shift left = 8
r0
byte 0
byte 1
byte 3
byte 2
You can use ror to move the field to the desired location
Alternative: If you can create an immediate value mask with a data operation like: movn, mov, add, or sub that is often faster
x
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
lsr r1, r1, 24
unsigned zero-extension (all 0’s)
Isolated bit-field
r1
byte 0
byte 1
byte 3
byte 2
lsl r1, r0, 8
Next shift right = 24
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far left
pushed bits to far right
Hint: Useful for PA8

## Slide 85: Masking Summary
Isolate a field: Use lsr, lsl, rot to get a field surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Select a field: Use and with a mask of one's surrounded by zero's to select the bits that have a 1 in the mask, all other bits will be set to zero
Clear a field: Use and with a mask of zero's surrounded by one's to select the bits that have a 1 in the mask, all other bits will be set to zero
1 1 1 1 1 1 1 1 | 0 0 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
x
0 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 | 0 0 0 0 0 0 0 0 0 0 0 0 0 0
selects this field when used with and
selection mask
clear a field mask
clears this field when used with and
lsl to get this edge into msb
lsr to get this edge into lsb
Insert a field: Use orr with fields surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Keep these bits | 0 0 0 0 0 0 0 0 | Keep these bits

## Slide 86: Extra Slides

## Slide 87: Reference: LDR/STR – Register To/From Memory Copy
ldr/str Rd, [Rn, +- imm12] // base register pointer + offset imm12 in bytes
-4095 <= imm12 <= 4095 (bytes)
ldr/str Rd, [Rn] // base register pointer + 0 (imm12 is 0)
ldr/str Rd, [Rn, +- Rm] // base register pointer +- offset register
offset constant
Rd – destination register
ldr/str
Rd
imm12
Rn
Rn – base register contains address
U
+/- offset
Offset/index Register
Rd – destination register
ldr/str
Rd
Rn
Rn – base register contain address
Rm
U
+/- offset
ldr r1, =var_x // r1 = &var_x
str r1, =mylabel+4 // *(mylabel+4) = r1
ldr r1, =0x246abcd // load an immediate into r1
ldr r1, [r3] // y = *r3 (4 bytes)
str r1, [r0] // *r0 = r1
ldr r1, [r3, -4] // y = *(r3 – 4) (4 bytes)
str r1, [r0, r2] // *(r0 + r2) = r1
x

## Slide 88: How are I – Type Constants Encoded in the instruction?
Aarch32 provides only 8-bits for specifying an immediate constant value
Without "rotation" immediate values are limited to the range of positive 0-255
Imm8 expands to 32 bits and does a rotate right to achieve additional constant values (YUCK)
positions to
rotate X 2
unsigned value to rotate
rot4 value | 32-bit constant result
0000 | 0000 0000 0000 0000 0000 0000 1111 1111
0001 (2 bits) | 1100 0000 0000 0000 0000 0000 0011 1111
x
two bits rotated right
results are interpreted as a 2's complement number

## Slide 89: Rot4 - Imm8 Values
positions to
rotate X 2
unsigned value to rotate
00000001
x
How would 256 be encoded?
  rotate = 12, imm8 = 1
Bottom line: the assembler will do this for you
If you try and use an immediate value that it cannot generate it will give an error
There is a workaround - later
results are interpreted as a 2's complement number

## Slide 90: Branch Target Address (BTA): What Is imm24?
Previous slide: phases of execution: (1) fetch, (2) decode, (3) execute
The pc (r15) contains the address of the instruction being fetched, which is two instructions ahead or executing instruction + 8 bytes
Branch target address (or imm24) is the distance measured in the # of instructions (signed, 2's complement) from the fetch address contained in r15 when executing the branch
imm24 | 0x 00 00 02
0001042c <inloop>:
1042c: e3530061 cmp r3, 0x61
10430: ba000002 blt 10440 <store>
10434: e353007a cmp r3, 0x7a
10438: ca000000 bgt 10440 <store>
1043c: e2433020 sub r3, r3, #32
00010440 <store>:
10440: e7c13002 strb r3, [r1, r2]
10444: e2822001 add r2, r2, 0x1
10448: e7d03002 ldrb r3, [r0, r2]
1044c: e3530000 cmp r3, 0x0
10450: 1afffff5 bne 1042c <inloop>
x
executing instruction
decode instruction
fetch instruction
BTA: + 2 instructions
target address = 0x10440
fetch address = 0x10438
distance(bytes) = 0x00008
distance(instructions)= 0x8/(4 bytes/instruction)= 0x2

## Slide 91: Basic Arm Machine Code Instructions
Instructions consist of several fields that encode the opcode and arguments to the opcode
Special fields enable extended functionality - later
Several 4-bit operand fields for specifying the source and destination of the operation, usually one of the 16 registers
Embedded constants ("immediate values") of various size and "configuration"
Basic Data processing instruction formats (below)
R type instruction: add r0, r1, r2 // third operand is a register
I type instruction: add r0, r0, 1 // third operand is an immediate value
Rotate
x

## Slide 92: Program Flow – multiple branches, one cmp
There are many other ways to do this
if ((r0 > 5) {
/* condition block 1 */
// branch to endif
} else if (r0 < 5){
/* condition block 2 */
// branch to endif
} else {
/* condition block 3 */
// fall through to endif
}
// endif
r1 = 11;
cmp r0, 5
bgt .Lblk1
blt .Lblk2
// fall through
// condition block 3
b .Lendif
.Lblk1:
// condition block 1
b .Lendif
.Lblk2:
// condition block 2
b .Lendif
.Lendif:
mov r1, 5
special case: multiple branches from one cmp
x

## Slide 93: Literal Table (Array) each entry is a pointer to a different Label
Assembler automatically inserts into the text segment an array (table) of pointers
Each entry contains a 32-bit address of one of the labels
Uses r15 (PC) as base register to load the entry into a reg
x
.data
x: .word 200
.bss
y: .space 4
.section .rodata
.Lmsg: .string "Hello World"
.text
main:
ldr r0, [PC, displacement] // replaces: ldr r0, =y
<last line of your assembly, typically a function return>
.word y // entry #1 32-bit address for y
.word x // entry #2 32-bit address for x
.word .Lmesg // entry #3 32-bit address for .Lmesg
(address)
displacement (bytes) - 8
The assembler creates this table before generating the .o file

## Slide 94: Literal Table (Array) each entry is a pointer to a different Label
x
.data
x: .word 200
.bss
y: .space 4
.section .rodata
.Lmsg: .string "Hello World"
.text
main:
ldr r0, [PC, displacement1] // replaces: ldr r0, =y
ldr r0, [PC, displacement2] // replaces: ldr r0, =y
<last line of your assembly, typically a function return>
.word y // entry #1 32-bit address for y
.word x // entry #2 32-bit address for x
.word .Lmesg // entry #3 32-bit address for .Lmesg
(address)
displacement2 - 8
(address)
displacement1 - 8
The displacement is different for each use.
As the PC is different at each instruction

## Slide 95: ARM Assembly Source File: Header
.arch <architecture>
  Specifies the target architecture to generate machine code
  Typically specify oldest ARM arch you want the code to run on – most arm CPUs are backwards compatible
.arm
  Use the 32-bit ARM instructions, There is an alternative 16-bit instruction set called thumb that we will not be using
.fpu <version>
  Specify which floating point co-processor instructions to use (OPTIONAL we will not be using floating point)
.arch armv6 // armv6 architecture
.arm // arm 32-bit instruction set
.fpu vfp // floating point co-processor
.syntax unified // modern syntax
File Header
At the top of every ARM source file
// Contents of the other memory segment include .text (your code)
x

## Slide 96: ARM Assembly Source File: Header and Footer
.syntax unified
  use the standard ARM assembly language syntax called Unified Assembler Language (UAL)
.section .note.GNU-stack,"",%progbits
  tells the linker to make the stack and all data segments not-executable (no instructions in those sections) – security measure
.end
  at the end of the source file, everything written after the .end is ignored
.arch armv6 // armv6 architecture
.arm // arm 32-bit instruction set
.fpu vfp // floating point co-processor
.syntax unified // modern syntax
File Header
At the top of every ARM source file
.section .note.GNU-stack,"",%progbits // set stack/data non-exec
.end
// everything past the .end is ignored!
// Debugging notes etc
File Footer
At the bottom of every ARM source file
// Contents of the other memory segment include .text (your code)
x

## Slide 97: Function Header and Footer Assembler Directives
.global function_name
  Exports the function name to other files. Required for main function, optional for others
.type name, %function
  The .type directive sets the type of a symbol/label name
  %function specifies that name is a function (name is the address of the first instruction)
equ FP_OFF, 4
  Used for basic stack frame setup; the number 4 will change – later slides
.size name, bytes
  The .size directive is used to set the size associated with a symbol
  Used by the linker to exclude unneeded code and/or data when creating an executable file
  It is also used by the debugger gdb
  bytes is best calculated as an expression: (period is the current address in a memory segment)
  In CSE30 required use: .size name, (. – name)
.text
.global myfunc // make myfunc global for linking
.type myfunc, %function // define myfunc to be a function
.equ FP_OFF, 4 // fp offset in main stack frame
myfunc:
// function prologue, stack frame setup
    // your code
// function epilogue, stack frame teardown
.size myfunc, (. – myfunc)
function entry point
address of the first instruction in the function
Must not be a local label (does not start with .L)
Function Header
Function Footer
x