## Slide 1
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 1.00
Review Session

## Slide 2: Five Step Workflow in the Linux Environment, Single Source File
arm32 Assembly (.s)
prog.s
gcc compile
Object file (.o)
arm32 machine code
partial missing libraries
prog.o
gcc (gas) Assembler
include files have function prototype and other declaration (later slides)
contents of included .h files are inserted/expanded by cpp (c pre-processor phase of gcc) into files prior to compilation start at their position in the file
prog.c
<stdio.h>
<stdlib.h>
#include <stdio.h>
#include <stdlib.h>
/* A simple C Program */
int
main(void)
{
printf("Hello World\n");
return EXIT_SUCCESS;
}
x
Linux Loader
Create a linux process
Load into memory & Execute a.out
ld Linkage Editor
a.out
Links in already compiled standard c library
Executable in machine code file
libc
Source to Execution
Five Step Process
Compile
Assemble
Link
Load
Execute
cpp
% gcc –Wall –Wextra –Werror prog.c

## Slide 3: Background: What is a Definition in a program language?
Definition: creates an instance of a thing
There must be exactly one definition of each function or variable (no duplicates)
In C you must define a variable or a function before first use in your code
Function definition (compiler actions)
  creates code you wrote in the functions body
  allocates memory to store the code
  binds the function name to the allocated memory
Variable definitions (compiler actions)
  allocates memory: generate code to allocate space for local variables
  initialize memory: generate code to initialize the memory for local variables
  binds (or associates) the variable name to the allocated memory
x

## Slide 4: Background What is a Declaration in programming language?
Declaration: describes a thing – specifies types, does not create an instance
Function prototype describes (more in a few slides …)
  The type of the function return value
  The types of each of the parameters
Variable declaration describes
  The type of a variable that is defined elsewhere
Derived and defined type description
  Later slides:(enums, struct, arrays, unions)
In C, you must declare a function or variable before you use it
  Use before declaration will implicitly default to int (and a compiler warning/error – not good)
An identifier can be declared multiple times, but only defined once
A definition is also a declaration in C
x

## Slide 5: C Library Function API : Simple Character I/O – Used in PA3
#include <stdio.h> // import the API declarations
int putchar(int c);
  writes c (demoted to a char) to stdout
  returns either: c on success OR EOF (a macro often defined as -1) on failure
  see % man 3 putchar
int getchar(void);
  returns the next input character (if present) promoted to an int read from stdin
  see % man 3 getchar
Make sure you use int variables with putchar() and putchar()
Both functions return an int because they must be able to return both valid chars and indicate the EOF condition (-1) is outside the range of valid characters
Operation | Usage Examples
Write a char | int status; int c; status = putchar(c); /* Writes to screen stdout */
Read a char | int c; c = getchar(); /* Reads from keyboard stdin */
x
Why is character I/O using an int?
Answer: Needs to indicate an EOF (-1) condition that is not a valid char

## Slide 6: Hex to Binary (group 4 bits per digit from the right)
1111 1010 0101 0011
0x f
a
5
3
0b1111101001010011
binary start with a 0b in C
x
Each Hex digit is 4 bits in base 2 =

## Slide 7: Unsigned Decimal to Unsigned Binary Conversion
x
dividend 249 | Quotient | Remainder | Bit Position
249/2 | 124 | 1 | b0
124/2 | 62 | 0 | b1
62/2 | 31 | 0 | b2
31/2 | 15 | 1 | b3
15/2 | 7 | 1 | b4
7/2 | 3 | 1 | b5
3/2 | 1 | 1 | b6
1/2 | 0 | 1 | b7
249(base 10) =
11111001 = (1x128) + (1x64) + (1x32) + (1x16) + (1x8) + 1 = 249

## Slide 8: Unsigned Binary to Unsigned Decimal Conversion
What is 0 1 1 0 0 1 0 1(base 2) in decimal (N)?
101(base 10) = (1x64) + (1x32) + (1x4) + 1 (checking the conversion)
x
Product Shift Left | Addend | Bit Position | Product
0 | + 0 | b7 | 0
0 | + 1 | b6 | 1
2 x 1 = 2 | + 1 | b5 | 3
2 x 3 = 6 | + 0 | b4 | 6
2 x 6 = 12 | + 0 | b3 | 12
2 x 12 = 24 | + 1 | b2 | 25
2 x 25 = 50 | + 0 | b1 | 50
2 x 50 = 100 | + 1 | b0 | 101

## Slide 9: Unsigned Integers (positive numbers) Impact of Fixed # of Bits
4 bits is = ONLY 16 distinct values
Modular (C operator: %) or clock math
  Numbers start at 0 and “wrap around” after 15 and go back to 0
Keep adding 1
wraps (clockwise)
  0000 -> 0001 … -> 1111 -> 0000
Keep subtracting 1
wraps (counter-clockwise)
  1111 -> 1110 … -> 0000 -> 1111
Addition and subtraction use normal "carry" and "borrow" rules, just operate in binary
x

## Slide 10: Overflow: Going Past the Boundary Between max and min
min
max
Overflow: Occurs when an arithmetic result (from addition or subtraction for example) is is more than min or max limits
Example shown is for a 4-bit number
x
C (and Java) ignore overflow exceptions
You end up with a bad value in your program and absolutely no warning or indication… happy debugging!….

## Slide 11: Unsigned Integer Number Overflow: Addition in 8 bits
1 0 1 0 0 0 0 1
0 1 0 1 1 1 1 1
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
+
carries
sum
161
95
256
Carry
Bit
Rule: When Carry Bit != 0, overflow has occurred for unsigned integers!
only 8 bits for numbers in this example carry bit is always dropped from result
x

## Slide 12: 2's Complement Signed Integer Method
Positive numbers encoded same as unsigned numbers
All negative values have a one in the leftmost bit
All positive values have a zero in the leftmost bit
  This implies that 0 is a positive value
Only one zero
For n bits, Number range is) to - 1)
  Negative values “go 1 further” than the positive values
Example: the range for 8 bits: -128, -127, .. 0, .. 126, +127
Example the range for 32 bits: -2147483648 .. 0, .. +2147483647
Arithmetic is the same as with unsigned binary!
x

## Slide 13: Two’s Complement: The MSB Has a Negative Weight
4-bit (w = 4) weight = = -23 = -8
  10102 unsigned: 1x23 + 0x22 + 1x21 + 0x20 = 10
  10102 two’s complement: -1x23 + 0x22 + 1x21 + 0x20 = -8 + 2 = –6
  -8 in two’s complement: 10002 = -23 + 0 = -8
  -1 in two’s complement: 11112 = -23 + (23 – 1) = -8 + 7 = -1
weight is ), all other bits: have positive weights )
. . .
b0
bn-1
bn-2
x

## Slide 14: Summary: Min, Max Values: Unsigned and Two’s Complement
Two’s Complement Unsigned for n bits
Unsigned Value Range
  UMin = 0b00…00 =
  UMax = 0b11…11 =
Two’s Complement Range
  SMin = 0b10…00 =
  SMax = 0b01…11 =
For n=4
x

## Slide 15: Signed Decimal to Two's Complement Conversion
x
dividend -102 | Quotient | Remainder | Bit Position
102/2 | 51 | 0 | b0
51/2 | 25 | 1 | b1
25/2 | 12 | 1 | b2
12/2 | 6 | 0 | b3
6/2 | 3 | 0 | b4
3/2 | 1 | 1 | b5
1/2 | 0 | 1 | b6
0/2 | 0 | 0 | b7
102(base 10) =
Get the two complement of 01100110 is 10011010

## Slide 16: Two's Complement to Signed Decimal Conversion - Positive
What is 0 1 1 0 0 1 0 1(base 2) in decimal (N)?
Signed Bit Bias | Bit | Bit Position | Bias
-2W-1 = -28-1 = -128 | x 0 | b7 | 0
Product Shift Left | Addend | Bit Position | Product
0 | + 1 | b6 | 1
2 x 1 = 2 | + 1 | b5 | 3
2 x 3 = 6 | + 0 | b4 | 6
2 x 6 = 12 | + 0 | b3 | 12
2 x 12 = 24 | + 1 | b2 | 25
2 x 25 = 50 | + 0 | b1 | 50
2 x 50 = 100 | + 1 | b0 | SUM = 101
 |  | Bias + SUM: | 0 + 101 = 101
x

## Slide 17: Two’s Complement Positive Overflow
4-bit Two’s complement numbers (positive overflow)
0 1 0 1 5
+ 0 1 1 0 6
1 0 1 1 -5 != 11
Cout
0
0
1
0
SMIN
SMAX
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
0
+ 1
+ 2
+ 3
+ 4
+ 5
+ 6
+ 7
– 8
– 7
– 6
– 5
– 4
– 3
– 2
– 1
Two’s Complement
Overflow: Occurs when an arithmetic result is beyond the min or max limits
x
signed numbers: overflow occurs if
operands have same sign and result’s sign is different

## Slide 18: Sign Extension (how type promotion works)
Sometimes you need to work with integers encoded with different number of bits
8 bits (char) -> (16 bits) short -> (32 bits) int
Sign extension increases the number of bits: -bit wide signed integer , EXPANDS to a wider n + -bit signed integer where both have the same value
Unsigned
Just add leading zeroes to the left side
Two’s Complement Signed:
If positive, add leading zeroes on the left
  Observe: Positive stay positive
If negative, add leading ones on the left
  Observe: Negative stays negative
• • •
• • •
• • •
• • •
n
original
copies of MSB
x

## Slide 19: Example: Two’s Complement Sign or bit Extension - 1
Adding 0's in front of a positive numbers does not change its value
7 = 0111
extend to
8 bits
00000111
Number is still 7
x
1 = 0001
extend to
8 bits
00000001
Number is still 1

## Slide 20: Each use of a * operator results in one additional read -2
Each * when used as a dereference operator in a statement (Lside and Rside) generates an additional read
x
int z = 2, y = 1; int *x;
int *w;
x = &y;
w = &z;
*x = *w;
int z = 2, y = 1;
int *x;
x = &y;
*x = z;
x
2
z
2
read
write
read address
y
x
2
z
2
y
w
read address
read address
read
write

## Slide 21: Recap: Lside, Rside, Lvalue, Rvalue
x
int x = 2, y = 1;
x = y;
0x1
Constant Lvalue Rvalue
Var Name address Contents
y 0x108
0x1
x 0x104
read
write
x 0x10c
y 0x108
z 0x104
w 0x100
int z = 2, y = 1; int *x;
int *w;
x = &y;
w = &z;
*x = *w;
0x108
0x1
0x2
0x104
read (address)
read
read (address)
write
Constant Lvalue Rvalue
Var Name address Contents
*x on Lside is 0x108
w on Rside is 0x100
*w on Rside is 2
0x2

## Slide 22: Background: Different Ways to Pass Parameters
Call-by-reference (or pass by reference)
  Parameter in the called function is an alias (references the same memory location) for the supplied argument
  Modifying the parameter modifies the calling argument
Call-by-value (or pass by value) (C)
  What Called Function Does
    Passed Parameters are used like local variables
    Modifying the passed parameter in the function is allowed just like a local variable
    So, writing to the parameter, only changes the copy
The return value from a function in C is by value
x

## Slide 23: Example Using Output Parameters
void inc(int *p);
int
main(void)
{
int x = 5;
inc(&x);
printf("%d\n", x);
return EXIT_SUCCESS;
}
void
inc(int *p)
{
if (p != NULL)
*p += 1; // or (*p)++
}
At the Call to inc() in main()
Allocate space for p
Copy x's address into p
Pass the address of x (&x)
Receive an address copy (int *p)
x
5
0x1014
Word address
0x1000
0x1004
0x1008
0x100c
0x1010
0x1014
p
x
6
Write to the output variable (*p)
With a pointer to X,
inc() can change x in main()
this is called a side effect
p just like any other local variable

## Slide 24: Arrays As Parameters: What is the size of the array?
It’s tricky to use arrays as parameters, as they are passed as pointers to the start of the array
  In C, Arrays do not know their own size and at runtime there is no “bounds” checking on indexes
int sumAll(int a[]);
int main(void)
{
int numb[] = {9, 8, 1, 9, 5};
int sum = sumAll(numb);
return EXIT_SUCCESS;
}
int sumAll(int a[])
{
int i, sum = 0;
int sz = (int) (sizeof(a)/sizeof(*a));
for (i = 0; i < sz; i++) // this does not work
sum += a[i];
}
}
the name is the address, so this is
passing a pointer to the start of the array
“inside” the body of sumAll(), the question is:
how big is that array? all I have is a POINTER to the first element…..
sz is a 1 on 32 bit arm
x

## Slide 25: Arrays As Parameters, Approach 2: Use a sentinel element
A sentinel is an element that contains a value that is not part of the normal data range
  Forms of 0 are often used (like with strings). Examples: '\0', NULL
int strlen(char *a);
int main(void)
{
char buf[] = {'a', 'b', 'c', 'd', 'e', '\0'}; // string
printf("Number of chars is: %d\n", strlen(buf));
return EXIT_SUCCESS;
}
x
0x104
0x103
0x102
0x101
0x100
1 byte
'a'
'b'
'c'
'd'
'e'
'\0'
0x??
p
s
0x100
0x105
buf
address
/* Assumes parameter is a terminated string */
int strlen(char *s)
{
char *p = s;
if (p == NULL)
return 0;
while (*p++)
;
return (p – s - 1);
}
same as:
while (*p != '\0')
p = p + 1;
return (p – s);

## Slide 26: Array of Pointers: main() : argc, argv Character Address
x
argv+0
argv+1
argv+2
argc
2
argv
.% ./extract –c3
(no space between c and 3)
These are the addresses
NULL
.
/
e
x
t
r
a
c
t
\0
-
c
\0
3
*argv + 8
*argv or *(argv + 0)
*(argv + 1) + 2
*(argv + 1)

## Slide 27: main() Command line arguments: argc, argv
x
argv+0
argv+1
argv+2
argc
3
argv
.% ./extract –c 3
(space between c and 3)
argv+3
NULL
.
/
e
x
t
r
a
c
t
\0
-
c
\0
3
\0
*(*argv + 8)
**argv
**(argv + 2)
*(*(argv + 1) + 1)
argv+0
argv+1
argv+2
argc
2
argv
.% ./extract –c3
(No space between c and 3)
NULL
.
/
e
x
t
r
a
c
t
\0
-
c
\0
3
*(*argv + 8)
**argv
*(*(argv + 1)+2)

## Slide 28: Process Memory Under Linux
When your program is running it has been loaded into memory and is called a process
Stack segment: Stores Local variables
  Allocated and freed at function call entry & exit
Data segment + BSS: Stores Global and static variables
  Allocated/freed when the process starts/exits
  BSS - Static variables with an implicit initial value
  Static Data - Initialized with an explicit initial value
Heap segment: Stores dynamically-allocated variables
  Allocated with a function call
  Managed by the stdio library malloc() routines
Read Only Data: Stores immutable Literals
Text: Stores your code in machine language + libraries
0xFF…FF
0x00…00
per process address space
OS kernel [protected]
Stack
Heap
BSS
Shared Libraries
Read Only Data
Read Only Text Segment
Data
x

## Slide 29: Returning a Pointer To a Local Variable (Dangling Pointer)
There are many situations where a function will return a pointer, but a function must never return a pointer to a memory location that is no longer valid such as:
Address of a passed parameter copy as the caller may or will deallocate it after the call
Address of a local variable (automatic) that is invalid on function return
These errors are called a dangling pointer
int *bad_idea(int n)
{
return &n; // NEVER do this
}
n is a parameter with the scope of bad_idea
it is no longer valid after the function returns
a is an automatic (local) with a scope and lifetime within bad_idea2
a is no longer a valid location after the function returns
int *bad_idea2(int n)
{
int a = n * n; return &a; // NEVER do this
}
/*
* this is ok to do
* it is NOT a dangling
* pointer
*/
int *ok(int n)
{
static int a = n * n; return &a; // ok
}
x

## Slide 30: Heap Memory "Leaks"
A memory leak is when you allocate memory on the heap, but never free it
Your program is responsible for cleaning up any memory it allocates but no longer needs
  If you keep allocating memory, you may run out of memory in the heap!
Memory leaks may cause long running programs to fault when they exhaust OS memory limits
  Make sure you free memory when you no longer need it
Valgrind is a tool for finding memory leaks (not pre-installed in all linux distributions though!)
void
leaky_memory (void)
{
char *bytes = malloc(BLKSZ * sizeof(*bytes));
…
/* code that never passes the pointer in bytes to anything */
return;
}
x

## Slide 31: More Dangling Pointers: Reusing "freed" memory
When a pointer points to a memory location that is no longer “valid”
Really hard to debug as the use of the return pointers may not generate a seg fault
dangling_freed_heap() type code often causes the allocators (malloc()and friends) to seg fault
  Because it corrupts data structures the heap code uses to manage the memory pool
char *dangling_freed_heap(void)
{
char *buff = malloc(BLKSZ * sizeof(*buff));
…
free(buff);
return buff;
}
x

## Slide 32: Copying Structs
You can assign the member value(s) of the whole struct from a struct of the same type – this copies the entire contents!
Individual fields can also be copied
struct date first = {1, 1};
struct date final = {.day= 31, .month= 12};
struct date *pt1 = &first;
struct date *pt2 = &final;
final.day = first.day; // both day are 1
final = first; // copies whole struct
pt2->month = 3;
*pt1 = *pt2; // copies whole struct
pt2->day = 7;
pt1->day = pt2->day; // both days are now 7
x
ptr1
1
low address
month
day
1
first
ptr2
12
low address
month
day
31
final
1
1
3
3
7
7

## Slide 33: Struct: Copy and Member Pointers
When you assign one struct to another it just copies the member fields!
name2 = name; // copies members Only
struct vehicle {
char *state;
char *plate;
};
x
state
plate
"UCSD CSE"
"CA"
name
struct vehicle name = {"CA", "UCSD CSE"};
struct vehicle name2;
state
plate
"CA"
"UCSD CSE"
name
state
plate
name2
name2.plate = "UCSD ECE";
"UCSD ECE"
immutable strings
(read only data)
Warning
Be very careful with "shallow copies" in C
when pointers are involved

## Slide 34: Struct: Copy and Member Pointers --- "Deep Copy"
Use strdup() to copy the strings
struct vehicle {
char *state;
char *plate;
};
x
state
plate
"UCSD CSE"
"CA"
name
state
plate
name2
struct vehicle name = {"CA", "UCSD CSE"};
struct vehicle name2;
name2.plate = strdup(name.plate);
name2.state = strdup(name.state);
……
name.plate = "UCSD ECE";
"UCSD ECE"
"CA"
"UCSD CSE"
mutable strings (heap memory)
immutable strings (read-only data)

## Slide 35: Creating a Node & Inserting it at the Front of the List
struct node {
int year;
char *name;
struct node *next;
};
// create node; insert at front when passed head
struct node *
creatNode(int year, char *name, struct node *link)
{
struct node *ptr = malloc(sizeof(*ptr));
if (ptr != NULL) {
if ((ptr->name = strdup(name)) == NULL) {
free(ptr);
return NULL;
}
ptr->year = year;
ptr->next = link;
}
return ptr;
}
// calling function body
struct node *head = NULL; // insert at front
struct node *ptr;
char buf[BUFSZ];
if (fgets(buf, BUFSZ, stdin) != NULL) { // reads joe
if ((ptr = creatNode(2020, buf, head)) != NULL) {
head = ptr; // error handling not shown
}
}
if (fgets(buf, BUFSZ, stdin) != NULL) { // reads sam
if ((ptr = creatNode(1955, buf, head)) != NULL) {
head = ptr; // error handling not shown
}
}
head
x
head
2020
"Joe"
NULL
head
2020
"Joe"
NULL
1955
"Sam"
Must duplicate the string because of buffer reuse

## Slide 36: Creating a Node & Inserting it at the End of the List
// create a node and insert at the end of the list
struct node *
insertEnd(int year, char *name, struct node *head)
{
struct node *ptr = head;
struct node *prev = NULL; // base case
struct node *new;
if ((new = creatNode(year, name, NULL)) == NULL)
return NULL;
while (ptr != NULL) {
prev = ptr;
ptr = ptr->next;
}
if (prev == NULL)
return new;
prev->next = new;
return head;
}
struct node *head = NULL; // insert at end
struct node *ptr;
if ((ptr = insertEnd(2020, "Joe", head)) != NULL)
head = ptr;
if ((ptr = insertEnd(1955, "Sam", head)) != NULL)
head = ptr;
x
head
head
2020
"Joe"
NULL
head
1955
"Sam"
NULL
2020
"Joe"

## Slide 37: How to Access Memory?
31 | 0
Address of a location in memory | 
Consider a = b + c are operands are in memory
  Operation code: add Destination: a
  Operand 1: b Operand 2: c
Aarch32 Instructions are always word size: 32 bits wide
  Some bits must be used to specify the operation code
  Some bits must be used to specify the destination
  Some bits must be used to specify the operands
Address space is 32 bits wide so put a POINTER in a register
31 |  |  | 0 | 
Opcode
Destination
NOT ENOUGH BITS for FULL Addresses to be stored in the instruction
32 bits wide
x
Operand 1
Operand 2
0xFF…FF
0x00…00
32-bit Address space
OS kernel [protected]
Stack
Heap
Static Data (+BSS)
Shared Libraries
Read Only Data
Read Only Text Segment

## Slide 38: R (register) Type Data Processing: Machine Code
Instructions that process data using three-register arguments
The general instruction format is (not all fields will be in every instruction)
opcode Rd (destination), Rn (operand 1), Rm (operand 2)
add r0, r1, r3
1110 0000 1000 0001 0000 0000 0000 0011
0xe0810003
is encoded as
in hex is
x

## Slide 39: Arm Register Summary
16 Named registers r0 – r15
The operands of almost all instructions are registers
To operate on a variable in memory do the following:
  Load the value(s) from memory into a register
  Execute the instruction
  Store the result back into memory (only if needed!)
Going to/from memory is expensive
  4X to 20X+ slower than accessing a register
Strategy: Keep variables in registers as much as possible
x

## Slide 40: Assembler Directives: .equ and .equiv
.equ <symbol>, <expression>
  Defines and sets the value of a symbol to the evaluation of the expression
  Used for specifying constants, like a #define in C
  You can (re)set a symbol many times in the file, last one seen applies
  .equ BLKSZ, 10240 // buffer size in bytes
  // other lines
  .equ BLKSZ, 1024 // buffer size in bytes
.equiv <symbol>, <expression>
  .equiv directive is like .equ except that the assembler will signal an error if symbol is already defined
.equ BLKSZ, 10240 // buffer size in bytes
.equ BUFCNT, 100*4 // buffer for 100 ints
.equiv STRSZ, 128 // buffer for 128 bytes
.equiv STRSZ, 1280 // ERROR! already defined!
.equ BLKSZ, STRSZ * 4 // redefine BLKSZ from here
x

## Slide 41: Program Flow: Simple If statement, No Else
Approach: adjust the conditional test then branch around the true block
Use a conditional test that specifies the inverse of the condition used in C
cmp r0, 5
bne .Lendif
/* condition true block */
/* then fall through */
.Lendif:
/* branch around to this code */
C source Code | Incorrect Assembly | Correct Assembly
int r0; if (r0 > 10) | cmp r0, 10 bgt .Lendif .Lendif: | cmp r0, 10 ble .Lendif .Lendif:
x
If r0 == 5 false
then branch around the true block
int r0;
if (r0 == 5) {
/* condition true block */
/* then fall through */
}
/* branch around to this code */
If r0 == 5 true
then fall through to the true block

## Slide 42: If with an Else Examples
…
if (r0 < r1) {
r2 = 1;
// branch around else
} else {
r2 = 0;
/* fall through */
}
r4 = r2 + r4;
  cmp r0, r1
  bge .Lelse
  mov r2, 1
  b .Lendif
.Lelse:
mov r2, 0
/* fall through */
.Lendif:
add r4, r2, r4
x
If r0 < r1 false
then branch to false block
Branch condition
Test (branch guard)
condition true block
condition false block

## Slide 43: Program Flow – Short Circuit or Minimal Evaluation
In evaluation of conditional guard expressions, C uses what is called short circuit or minimal evaluation
Each expression argument is evaluated in sequence from left to right including any side effects (modified using parenthesis), before (optionally) evaluating the next expression argument
If after evaluating an argument, the value of the entire expression can be determined, then the remaining arguments are NOT evaluated (for performance)
x
if ((x == 5) || (y > 3)) // if x == 5 then y > 3 is not evaluated
if ((a != 0) && func(b)) // if a is 0, func(b) is not called
// do_something();

## Slide 44: Program Flow – If statements && compound tests - 2
cmp r0, 5 // test 1
bne .Lelse
cmp r1, 3 // test 2
ble .Lelse
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse:
mov r5, r2 //false block
// fall through
.Lendif:
mov r4, r3
if r0 == 5 false
then short circuit branch to the false block
if ((r0 == 5) && (r1 > 3)) {
r2 = r5; // true block
// branch around else
} else {
r5 = r2; False block */
/* fall through */
}
r4 = r3;
x
if r1 > 3 false
then branch to the false block

## Slide 45: Program Flow – If statements || compound tests - 2
cmp r0, 5
beq .Lthen
cmp r1, 3
ble .Lelse
// fall through
.Lthen:
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse
mov r5, r2 // false block
// fall through
.Lendif:
if ((r0 == 5) || (r1 > 3)) {
r2 = r5; // true block
/* branch around else */
} else {
r5 = r2; // false block
/* fall through */
}
x
If r0 == 5 true, then branch to the true block
if r1 > 3 false then branch to false block

## Slide 46: Program Flow – Pre-test and Post-test Loop Guards
loop guard: code that must evaluate to true before the next iteration of the loop
If the loop guard test(s) evaluate to true, the body of the loop is executed again
pre-test loop guard is at the top of the loop
  If the test evaluates to true, execution falls through to the loop body
  if the test evaluates to false, execution branches around the loop body
post-test loop guard is at the bottom of the loop
  If the test evaluates to true, execution branches to the top of the loop
  If the test evaluates to false, execution falls through the instruction following the loop
x
while (i < 10) {
/* block */
i++;
}
pre-test
loop guard
loop control variable
zero or more iterations
do {
/* block */
i++;
} while (i < 10);
post-test
loop guard
one or more iterations

## Slide 47: Pre-Test Guards - While Loop
.Lwhile:
cmp r1, 10
bge .Lendw
// block
add r1, r1, 1
b .Lwhile
.Lendw:
mov r2, r1
while (r1 < 10) {
/* block */
r1++;
}
r2 = r1;
x
pre-test
loop guard
loop iteration
.Lwhile:
cmp r1, 10
bge .Lendw
cmp r2, r1
beq .Lnext
// block
.Lnext:
add r1, r1, 1
b .Lwhile
.Lendw:
mov r2, r1
while (r1 < 10) {
if (r2 != r1) {
/* block */
}
r1++;
}
r2 = r1;
pre-test
loop guard
loop iteration
inverted test
if stmt guard

## Slide 48: Post-Test Guards – Do While Loop
.Ldo:
// block
add r1, r1, 1
cmp r1, 10
blt .Ldo
mov r2, r1
.Ldo:
cmp r2, r1
beq .Lnext
// block
.Lnext
add r1, r1, 1
cmp r1, 10
blt .Ldo
move r2, r1
do {
/* block */
r1++;
} while (r1 < 10);
r2 = r1;
x
loop iteration
post-test
loop guard
do {
if (r2 != r1) {
/* block */
}
r1++;
} while (r1 < 10);
r2 = r1;
loop iteration
post-test
loop guard
test is not inverted

## Slide 49: Program Flow – Counting (For) Loop
mov r1, 0
.Lfor:
cmp r1, 10
bge .Lendfr
// block code
add r1, r1, 1
b .Lfor
.Lendfr:
A counting loop has three parts:
Pre-loop setup
Pre-test loop guard conditions
Post-loop update
Alternative:
move Pre-test loop guard before the loop
Add post-test loop guard
  converts to do while
  removes an unconditional branch
for (r1 = 0; r1 < 10; r1++) {
/* block */
}
mov r1, 0
cmp r1, 10
bge .Lendfr
.Ldo:
// block code
add r1, r1, 1
cmp r1, 10
blt .Ldo
.Lendfr:
Alternative
Pre loop setup
Pre-test
Loop guard
Post loop update
x
Post loop update
Pre loop setup
Pre-loop setup
Post loop update
Pre-test loop guard
Pre-test loop guard
Post-test loop guard

## Slide 50: Nested loops
Nest loop blocks as you would in C or Java
Do not branch into the middle of a loop, this is hard to read and is prone to errors
for (r3 = 0; r3 < 10; r3++) {
r0 = 0;
do {
r0 = r0 + r1++;
} while (r1 < 10);
// fall through
r2 = r2 + r1;
}
r5 = r0;
x
mov r3, 0
.Lfor:
cmp r3, 10 // loop guard
bge .Lendfor
mov r0, 0
.Ldo:
add r0, r0, r1
add r1, r1, 1
cmp r1, 10 // loop guard
blt .Ldo
// fall through
add r2, r2, r1
add r3, r3, 1 // loop iteration
b .Lfor
.Lendfor:
mov r5, r0

## Slide 51: Bitwise Not (vs Boolean Not)
a | ~a
0 | 1
1 | 0
in C
int output = ~a;
x
Boolean operators act on the entire value not the individual bits
Meaning | Operator | Operator | Meaning
Boolean NOT | !b | ~b | Bitwise NOT
 | Bitwise Not
number | 0101 1010 0101 1010 1111 0000 1001 0110
~number | 1010 0101 1010 0101 0000 1111 0110 1001
Type | Operation | result
bitwise | ~0x01 | 1111 1111 1111 1111 1111 1111 1111 1110
Boolean | !0x01 | 0000 0000 0000 0000 0000 0000 0000 0000
~ 1100
----
0011
Bitwise NOT

## Slide 52: Bitwise versus C Boolean Operators
Boolean operators act on the entire value not the individual bits
& versus &&
0x10 & 0x01 = 0x00 (bitwise)
0x10 && 0x01 = 0x01 (Boolean)
! versus ~
~0x01 = 0xfffffffe (bitwise)
!0x01 = 0x0 (Booelan)
Meaning | Operator | Operator | Meaning
Boolean AND | a && b | a & b | Bitwise AND
Boolean OR | a ¦¦ b | a ¦ b | Bitwise OR
Boolean NOT | !b | ~b | Bitwise NOT
x

## Slide 53: Bitwise Instructions
<op> Rd, Rn, constant // Rd = Rn <op> constant
<op> Rd, constant // Rd = Rd <op> constant
<op> Rd, Rn, Rm // Rd = Rn <op> Rm
Operand 2 constant
destination
<op>
Rd
rot4
imm8
Rn
operand 1
Operand 2
destination
<op>
Rd
Rn
operand 1
Rm
Bytes: 0 <= imm8 <= 255 + values from "rotating" rot 4 bits
Bitwise <op> description | C Syntax | Arm <op> Syntax Op2: either register or constant value | Operation
Bitwise AND | a & b | and Rd, Rn, Op2 | Rd = Rn & Op2
Bit Clear each bit in Op2 that is a 1, the same bit in Rd, is cleared | a & ~b | bic Rd, Rn, Op2 | Rd = Rn & ~Op2
Bitwise OR | a ¦ b | orr Rd, Rn, Op2 | Rd = Rn ¦ Op2
Exclusive OR | a ^ b | eor Rd, Rn, Op2 | Rd = Rn ^ Op2
x

## Slide 54: The act (operation) of Masking
Bit masks access/modify specific bits in memory
Masking act of applying a mask to a value with a specific op:
orr: 0 passes bit unchanged, 1 sets bit to 1 (a = b | c; // in C)
eor: 0 passes bit unchanged, 1 inverts the bit (a = b ^ c; // in C)
bic: 0 passes bit unchanged, 1 clears it (a = b & ~c; // in C)
and: 0 clears the bit, 1 passes bit unchanged (a = b & c; // in C)
x
a = | a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
 | <op> | <op> | <op> | <op> | <op> | <op> | <op> | <op>
b = | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
result = | c7 | c6 | c5 | c4 | c3 | c2 | c1 | c0

## Slide 55: Extracting (Isolate) a Field of Bits with a mask
x
extract top 8 bits of r2 into r1
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, r3
DATA: r2 0xab ab ab 77
and
MASK: r3 0xff 00 00 00
RSLT: r1 0xab 00 00 00
forces to a 0
unchanged
extract top 8 bits of r2 into r1
DATA: r2 0xab ab ab 77
and r1, r2, 0xff000000
RSLT: r1 0xab 00 00 00
r1 = r2 & 0xff000000; // in C

## Slide 56: MOD %<power of 2>
remainder (mod): num % d where num ≥ 0 and d = 2k
mask = 2k -1 so for mod 16, mask = 16 -1 = 15
and r1, r2, r3
x
Example: %2
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 01 (mod 2 even or odd)
RSLT: r1 0x00 00 00 01 (odd)
forces to a 0
unchanged
Example: Mod 16
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 0f (mod 16)
RSLT: r1 0xab 00 00 07
forces to a 0
unchanged

## Slide 57: Flipping bits: bit toggle Used in PA8
x
invert (flip) bits "bit toggle" operation
  1 will flip the bit
  0 to let a bit through
eor r1, r2, r3
Observation: When applied twice, it returns the original value (symmetric encoding)
With a mask of all 1's is a 1's compliment
Example: invert (flip) the lower 8-bits
DATA: r2 0xab ab ab 77
eor
MASK: r3 0x00 00 00 ff
RSLT: r1 0xab ab ab 88
inverts (flips)
unchanged
88: 1000 1000
DATA: r1 0xab ab ab 88
eor
MASK: r3 0x00 00 00 ff apply a 2nd time
RSLT: r1 0xab ab ab 77 original value!
inverts (flips)
77: 0111 0111
Example: flip the lower 8-bits
eor r1, r2, 0xff
unsigned int r1, r2;
r1 = r2 ^ 0xff;

## Slide 58: Extracting/Isolating Unsigned Bitfields
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
next shift left = 8
r0
byte 0
byte 1
byte 3
byte 2
Move byte 2 in r0 to byte 0 in r1
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
lsr r1, r1, 24
r1 = r1 >> 24;
unsigned zero-extension (all 0’s)
Extracted bit-field
r1
byte 0
byte 1
byte 3
byte 2
lsl r1, r0, 8
unsigned int r0,r1;
r1 = r0 << 8;
Next shift right = 24
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far left
pushed bits to far right
Hint: Useful for PA8

## Slide 59: Inserting Bitfields – Inserting Source Field into Destination Field
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
r1
r0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Task: Insert source into destination
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
results in
orr r1, r1, r2
r1 = r1 | r2;
r1
r2
Approach
(1) isolate source field
(2) clear destination field
(3) Bitwise or together
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 60: Loading and Storing: Variations List
Load and store have variations that move 8-bits, 16-bits and 32-bits
Load into a register with less than 32-bits will set the upper bits not filled from memory differently depending on which variation of the load instruction is used
Store will only select the lower 8-bit, lower 16-bits or all 32-bits of the register to copy to memory, register contents are not altered
Instruction | Meaning | Sign Extension | Memory Address Requirement
ldrsb | load signed byte | sign extension | none (any byte)
ldrb | load unsigned byte | zero fill (extension) | none (any byte)
ldrsh | load signed halfword | sign extension | halfword (2-byte aligned)
ldrh | load unsigned halfword | zero fill (extension) | halfword (2-byte aligned)
ldr | load word | --- | word (4-byte aligned)
strb | store low byte (bits 0-7) | --- | none (any byte)
strh | store halfword (bits 0-15) | --- | halfword (2-byte aligned)
str | store word (bits 0-31) | --- | word (4-byte aligned)
x

## Slide 61: Loading 32-bit Registers From Memory Variables < 32-Bits Wide
Unsigned
Zero-Extend: Add leading 0’s
example ldrb
Instructions that zero-extend:
ldrb, ldrh
0b 1110 0001
0x00
0x00
0x00
0xe1
memory
r0
Overwrite the upper three bytes with 0
Signed (2’s complement)
Sign-Extend: Replicate sign bit
example ldrsb
Instructions that sign-extend:
ldrsb, ldrsh
0xff
0xff
0xff
0xe1
memory
r0
Overwrite the upper three bytes with 1
0b 1110 0001
x

## Slide 62: Storing 32-bit Registers To Memory 8-bit, 16-bit, 32-bit
strb
0x00
0x00
0xe2
0xe1
memory
r0
0x??
0x??
0x??
0xe1
Not Changed
strh
0x00
0x00
0xe2
0xe1
memory
r0
0x??
0x??
0xe2
0xe1
Not Changed
x
str
0x04
0x03
0xe2
0xe1
memory
r0
0x04
0x03
0xe2
0xe1

## Slide 63: Array addressing with ldr/str
Array element | Base addressing | Immediate offset | register offset
char ch[0] | ldrb r2, [r0] | ldrb r2, [r0, 0] | mov r4, 0 ldrb r2, [r0, r4]
char ch[1] | add r0, r0, 1 ldrb r2, [r0] | ldrb r2, [r0, 1] | mov r4, 1 ldrb r2, [r0, r4]
char ch[2] | add r0, r0, 2 ldrb r2, [r0] | ldrb r2, [r0, 2] | mov r4, 2 ldrb r2, [r0, r4]
int x[0] | ldr r2, [r1] | ldr r2, [r1, 0] | mov r4, 0 ldr r2, [r1, r4]
int x[1] | add r1, r1, 4 ldr r2, [r1] | ldr r2, [r1, 4] | mov r4, 4 ldr r2, [r1, r4]
int x[2] | add r1, r1, 8 ldr r2, [r1] | ldr r2, [r1, 8] | mov r4, 8 ldr r2, [r1, r4]
0x41
0x42
0x43
0x44
0x45
0x00
0x00
0x00
0000
0001
0010
0011
0100
0101
0110
0x00
0111
1000
0x00
0x00
0x01
1001
1010
1011
0x00
1100
0x00
0x00
0x01
1101
1110
1111
..0000
r0
..0100
r1
table rows are
independent instructions not a sequence

## Slide 64: ldr/str practice - 2
r1 contains the Address of X (defined as int *X) in memory r1 points at X
r2 contains the Address of Y (defined as int Y) in memory; r2 points at Y
write Y = *X;
ldr r3, [r1] // r3  x (read 1)
ldr r0, [r3] // r0  *x (read 2)
str r0, [r2] // y  *x
x
address of y
0x0100c
r1
r2
X = 0x01010
??
Y contents
??
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
55
0x01010
55
?
r3
0x01010
r0
?
55

## Slide 65: Preview: Return Value and Passing Parameters to Functions (Four parameters or less)
Where r0, r1, r2, r3 are arm registers, the function declaration is (first four arguments):
r0 = function(r0, r1, r2, r3) // 32-bit return
r0, r1 = function(r0, r1, r2, r3) // 64-bit return – long long
Each parameter and return value is limited to data that can fit in 4 bytes or less
You receive up to the first four parameters in these four registers
You copy up to the first four parameters into these four registers before calling a function
For parameter values using more than 4 bytes, a pointer to the parameter is passed (we will cover this later)
You MUST ALWAYS assume that the called function will alter the contents of all four registers: r0-r3
  In terms of C runtime support, these registers contain the copies given to the called function
  C allows the copies to be changed in any way by the called function
Register | Function Call Use
r0 | 1st parameter
r1 | 2nd parameter
r2 | 3rd parameter
r3 | 4th parameter
Register | Function Return Value Use
r0 | 8, 16 or 32-bit result, 32-bit address or least-significant half of a 64-bit result
r1 | most-significant half of a 64-bit result
x

## Slide 66: Using the literal table to fix: Error: invalid constant (3ff) after fixup
In data processing instructions, the field imm8 + rotate 4 bits is too small to store store the immediate value, how do you get larger immediate values into a register?
Answer: use ldr instruction with the constant as an operand: =constant
Assembler creates a literal table entry with the constant
mov r0, 1023
xxx.s:24: Error: invalid constant (3ff) after fixup
ldr r0, =1023
fails
replacement
mov
Rd
rot4
imm8
x
ldr Rd, =constant // =constant
ldr r1, =0x2468abcd // loads the constant 0x246abcd into r1